## Slide 1: Basic production algorithms and its main concepts
Ing.J.Skorkovský,CSc.
and various listed sources
Department of Corporate Economy
Slides 2-18 –basic production theory and 29-48 practical NAV example
Comment : without basic production theory it is useless to model production in ERP

## Slide 2: Main concepts
MRP=Material Requirements Planning (push)
MRP_II=Manufacturing Resource Planning (push)
APS = Advanced Planning and Scheduling
JIT = Just In Time (pull)
TOC (Drum-Buffer-Rope) (push-pull->combined) – was presented in another session of this course
Work Order=Production order in MS Dynamics NAV

## Slide 3: BOM=Bill Of Material (structure of the product)
A
100
300
400
200
B
500
300
600
100
300
400
Component
Product|Semiproduct
0
1
2
3
Independent demand for products and semi-products and dependent for components
Planning backward from production schedule (independent) to dependent- demand components -without statistically calculated Reorder Point (ROP)– see next lesson and next slide as well
IF ROP is not taken into consideration – MRP is PUSH system -> it computes the schedule of what should be started (pushed) into a system, that authorizes production as inventory is consumed (ROP will be explained later in this session- only Czech course BPH-PIS2)
0,1,2,,..Low Level Codes
HOME STUDY

## Slide 4: Push system
Supplier1
Supplier 2
MRP|ERP
Operation 1
Operation 2
Operation 3
Operation 4
Customer 1
Customer 2
FG warehouse
Component
warehouse
Forecast
Purchase orders
ROUTING
(how to do it)
WIP
WIP
Take it !
WIP
Supply
Demand

## Slide 5: Determination of the Reorder Point (ROP)
ROP=expected demand during lead time + safety stock
20
50=ROP
50-20=30
LT =Lead time
Expected demand=30

## Slide 6: Determination of the Reorder Point (ROP) (home study - AOPR-only for avid readers- will be not discussed during exams)
ROP = expected demand during lead time + z* σdLT
where z = number of standard deviations and
σdLT = the standard deviation of lead time demand and z* σdLT =Safety Stock
aan

## Slide 7: Example ( Pareto analysis and ABC model simplified - PWP will be shown later) (home study - AOPR-only for avid readers- will be not discussed during exams)
The manager of a construction supply house determined knows that demand for sand during lead time averages is 50 tons.
The manager knows, that demand during lead time could be described by a normal distribution that has a mean of 50 tons and a Standard Deviation of 5 tons (σdLT )
The manager is willing to accept a stock out the risk of no more than 3 percent

## Slide 8: Example-data (home study - AOPR-only for avid readers- will be not discussed during exams)
Expected lead time averages = 50 tons.
σdLT = 5 tons
Risk = 3 % max
Questions :
  What value of z (number of standard deviations) is appropriate?
  How much safety stock should be held?
  What reorder point should be used?

## Slide 9: Example-solution (home study - AOPR-only for avid readers- will be not discussed during exams)
Service level =1,00-0,03 (risk) =0,97 and from probability tables you will get z= +1,88
See next slide with probability table

## Slide 10: Probability table home study - AOPR-only for avid readers- will be not discussed during exams

## Slide 11: Example-solution (home study - AOPR-only for avid readers- will be not discussed during exams)
Service level =1,00-0,03 =0,97 and from probability tables we have got : z= +1,88
Safety stock = z * σdLT = 1,88 * 5 =9,40 tons
ROP = expected lead time demand + safety stock = 50 + 9.40 = 59.40 tons
For z=1 service level =84,13 %
For z=2 service level= 97,72 %
For z=3 service level = 99,87% (see six sigma)

## Slide 12: MRP_II =MRP + resource capacity planning
Intermediate-range
planning
Short term
control
(Shop floor)
MPS
Demand
management
Rough-cut capacity planning
BOM
MRP
Scheduled
receipts
Job
Pool (planned)
Capacity requirement planning
Job Release
Routings
(operations)
Job
Dispatch

## Slide 13: BOM in MS Dynamics NAV
B OM = Bill of Material
7
6
5
4
3
2
1

## Slide 14: Routings in MS Dynamics NAV

## Slide 15: Capacity of resources in MS Dynamics NAV

## Slide 16: JIT=Just In Time
Toyota Motors and Taiichi Ohno
Production based only on demand
Lower inventory costs
The concept behind it is that a company can save money on parts and components---by not have having to store them--- if they are delivered to the assembly line just in time to be installed on the car as it is being built.

## Slide 17: Kanban principle
Resource :
(home study not fro AOPR-AOMA)

## Slide 18: Orders Tracking
Sales Order
Customer
Purchase Order
Sales Order Line
Demand
Planning production (MRP-II )
Tracking
Production Order
Bill of Material
Routing (OP1-OP4)
Tracking
Requisition Worksheet (MRP)
Tracking
Supply
Supply
Tracking
Stock
Vendor
Tracking

## Slide 19: Product and two components
1150
1151
1155
Bill of material
Product
Components

## Slide 20: Requirement=Demand
Request=Demand (Sales Order) will be for Front Hub 1150 (200), whose BOM consists of two 1151 components (200 in stock) and 1155 (200 in stock).
Preparing data for example: Change both components (1151 and 1155) the following parameters :
Reordering policy: Lot-for-Lot. Furthermore, with the help of an Item Journal, sell 200 pieces of 1150 and its components 1151 and 1155.
Attention: components and product are not stored at any location. Next, change on the Replenishment tab for both components the Vendor number to 10000. The result of the demand (request) will be the production order planning and subsequent consumption registration of components and resources and put-away of the final product
Set Scrap%=0 on all involved items !!!! Lot size parameter on all involved items=0!

## Slide 21: Item (Final) 1150
Set Scrap%->0 !!!

## Slide 22: Partial setup of components (both)
Safety stock value set to 0

## Slide 23: Item (Final) 1150
Safety stock value
set to 0
0

## Slide 24: Items (components) 1151 ( 1155 has the same setup)
Safety stock value set to 0

## Slide 25: Use of Item Journal to „clean“ inventory How to go there ->Warehouse ->Inventory->Tasks->Item Journals
Post it by F9
See related item ledger entries !!!

## Slide 26: Item ledger entries Use Ctrl-F7 and filters

## Slide 27: Working date setup
1.4.2020

## Slide 28: Sales Order for 100 pcs Demand creation- reason for production planning
You might be notified that item 1150 is not in stock !! Our reaction to warning should be YES (if warning message generated)
Next, change the Scheduled Delivery Date in the sales line to 20.4. 2020, well away from the working date (1.4.2020)
Reason: that the scheduling algorithm does not schedule the start of production to date before the working date
Part of the sales line

## Slide 29: Sales Order lines for 100 pcs
Demand
created

## Slide 30: Planning worksheets (MRP)
MRP = Material Requirement Planning

## Slide 31: Planning worksheets
Planning Batch job is running…

## Slide 32: Planning worksheets
Planning worksheet
Production
order
Purchase
order
1151
1155
1150
Creation of Purchase order and
Production order
Diagram of the pocess

## Slide 33: Firm Planned Production Orders

## Slide 34: Firm Planned Production Order
See next slide

## Slide 35: Bill of Material (BOM) & Routing
To go to Routing and Components (BOM) use ikon Line ) see previous slide
To go to Demand use Icon Function and Order Tracking

## Slide 36: Firm Planned Production (animated)
To go to Routing and Components use ikon Line
To go to Demand use Icon Function and Order tracking

## Slide 37: Created Purchase Order lines (Purchasing->Order PROcessing->Purchase Orders)
Post it by F9 and then
see related item ledger entries !!!
Lines of the Purchase order
See next slide

## Slide 38: Item ledger entries (only components)
Used filter to see only entry type=Purchase

## Slide 39: Change the status of Production Order
From status Firm Planned to status Relesed
Before planning we have changed working day to 3.4.2020

## Slide 40: Statistics from Relesed Production Order (F7)
Click and edit->Released Production Order->F7

## Slide 41: Production Journal (from icon Lines)
Data such as Setup times and Run Times was entered manually. We have used exact data from original Routing
Post it by F9 and then
Released
Production Order
We need to register time of manchines
and consumption of components
Manually

## Slide 42: Item entries after registering (F9)

## Slide 43: End of the English section
This is the end Beautiful friend This is the end My only friend, the end…
So why worry now ……

## Slide 44: Czech version of the example Česká verze příkladu na výrobu
Určeno pro kurzy BPH_PIS- BPH_PIS2

## Slide 45: Požadavek
Požadavek (Prodejní objednávka) bude na prodej Předního náboje 1150 (na skladě 200),
jehož kusovník se skládá ze dvou komponent 1151 (200 na skladě)
a 1155 (200 na skladě).
Příprava dat pro příklad : Změňte u obou komponent (1151 a 1155)
Způsob přiobjednání na Dávka-pro- dávku. Dále s pomocí deníku zboží prodejte 200 ks
výrobku 1150 a jeho komponent 1151 a 1155. Pozor: komponenty i výrobek
nejsou uloženy na žádné lokaci. Dále změňte na záložkách Doplnění
u obou komponent dodavatel na 10000. Dále vynulujte pole zmetky a pole
Bezpečnostní zásoba
Výsledkem požadavku bude naplánování Výrobní zakázky a její následné odhlášení
(komponenty do spotřeby a výrobek na sklad)

## Slide 46: Vynulování počtů 1150..1155 na skladě
Deník zboží ->F9

## Slide 47: Prodejní objednávka na 100 ks 1150
Dostaneme upozornění, že podsestava kola 1150 není na skladě !! Reakce->ANO
Dále změňte Plánované datum dodávky na datum 20.4. , tedy dostatečně daleko od pracovního data – Důvod : aby plánovací algoritmus neplánoval počátek výroby na data před pracovním datem.
Prodejní řádek
Další krok procesu plánování
Viz další snímek

## Slide 48: Plánovací sešit
Plánované datum dodávky (viz prodejní řádek)
je pro tuto databázi 4.5.2017. Do Čísla zboží zavedeme ručně Jak číslo výrobku tak i čísla komponent ->1150|1151|1155
Viz další snímek

## Slide 49: Sledování zakázky

## Slide 50: Seši plánování po naplánování
Plánovací sešit
Výrobní
objednávka
Nákupní objednávka
1151
1155
1150

## Slide 51: Řádky nákupní objednávky
Doplňte číslo faktury dodavatele a zaúčtuje F9->podívejte se na položky zboží

## Slide 52: Položky zboží po zaúčtování příjmu komponent

## Slide 53: Výrobní zakázka a změna jejího stavu (Pevně plánovaná VZ ->Vydaná VZ)

## Slide 54: VZ je v dílně

## Slide 55: Vydaná VZ a její komponenty
Viz další snímek

## Slide 56: Kusovník a technologický postup
Řádek VZ->Komponenty
Řádek VZ->TNG postup

## Slide 57: Statistika VZ (s pomocí F7)

## Slide 58: Odhlášení spotřeby a zdrojů
V řádku VZ vydané, kde je ikona Funkce najdete Deník výroby
Zadejte ručně odhadnutou dobu seřízení a zpracování včetně spotřeby materiálu.
Zadané hodnoty by se neměly lišit od TNG postupu uvedeného pře několika snímky.
Na dalším obrázku to zobrazíme ještě jednou pro ulehčení zadávání hodnot do
Výrobního deníku. Zde se často používají dotykové obrazovky a BAR čtečky

## Slide 59: Deník výroby po vyplnění
Záměrně je množné některé časy změnit- reálné časy nemusí přesně odpovídat plánu.

## Slide 60: Statistika VZ po zaúčtování deníku

## Slide 61: Položky VZ po zaúčtování (VZ->Ctrl-F7)

## Slide 62: Dokončená VZ

## Slide 63: VZ- kalkulace

## Slide 64
Konec CZ sekce výroba
Děkuji za pozornost !!