## Slide 1: Chapter 9: Multiarea OSPF
CCNA Routing and Switching
Scaling Networks v6.0
Notes: Cisco Networking Academy Program
Scaling Networks v6.0
Chapter 9: Multiarea OSPF

## Slide 2: Chapter 9 - Sections & Objectives
9.1 Multiarea OSPF Operation
  Explain how multiarea OSPF operates in a small to medium-sized business network.
    Explain why multiarea OSPF is used.
    Explain how multiarea OSPFv2 uses link-state advertisements.
    Explain how multiarea OSPF establishes neighbor adjacencies.
9.2 Implement Multiarea OSPF
  Implement multiarea OSPFv2 and OSPFv3.
    Configure multiarea OSPFv2 and OSPFv3 in a routed network.
    Verify multiarea OSPFv2 and OSPFv3 operation.
Notes: 2
Cisco Networking Academy Program
Scaling Networks v6.0
Chapter 9: Multiarea OSPF

## Slide 3: 9.1 Multiarea OSPF Operation
Notes: 9 – Multiarea OSPF
9.1 – Multiarea OSPF Operation

## Slide 4: Why Multiarea OSPF? Single-Area OSPF
Issues in a large single area OSPF:
  Large routing table
  Large link-state database (LSDB)
  Frequent SPF algorithm calculations
To make OSPF more efficient and scalable, OSPF supports hierarchical routing using areas.
Notes: 9.1 – Multiarea OSPF Operation
9.1.1 – Why Multiarea OSPF?
9.1.1.1 – Single-Area OSPF

## Slide 5: Why Multiarea OSPF? Multiarea OSPF
Multiarea OSPF:
  Large OSPF area is divided into smaller areas.
  Reduces processing and memory overhead.
  Requires a hierarchical network design.
  The main area is the backbone area (area 0) and all other areas connect to it.
Advantages of Multiarea OSPF:
  Smaller routing tables - Fewer routing table entries as network addresses can be summarized between areas.
  Reduced link-state update overhead.
  Reduced frequency of SPF calculations.
Notes: 9.1 – Multiarea OSPF Operation
9.1.1 – Why Multiarea OSPF?
9.1.1.2 – Multiarea OSPF

## Slide 6: Why Multiarea OSPF? Multiarea OSPF – Types of Routers
OSPF Two-Layer Area Hierarchy
  Backbone (Transit) area and Regular (Non-backbone) area(s)
Types (Roles) of OSPF Routers
  Internal router
  Backbone router
  Area Border Router (ABR)
  Autonomous System* Boundary Router (ASBR)
  *) In fact, autonomous system is any non-OSPF network
Internal Router
Internal Routers
Internal Router
All Backbone Routers
ABR and Backbone Router
ABR and Backbone Router
ASBR and Backbone Router
51
Notes: 9.1 – Multiarea OSPF Operation
9.1.1 – Why Multiarea OSPF?

## Slide 7: Multiarea OSPF LSA Operation OSPF LSA Types
Link State Advertisement types
Type 1 - Represents a router
Type 2 - Represents the pseudonode (designated router – DR) for a multiaccess link
Type 3 - A network link summary (internal route)
Type 4 - Represents an ASBR
Type 5 - A route external to the OSPF domain
Type 7 - Used in stub areas in place of a type 5 LSA
LSA types 1 and 2 are found in all areas, and are never flooded outside of an area
LSAs individually act as database records and provide specific OSPF network details.
LSAs in combination describe the entire topology of an OSPF network or area.
Any implementation of multiarea OSPF must support the first five LSAs
Notes: 6.1.2.1 OSPF LSA Types

## Slide 8: Multiarea OSPF LSA Operation OSPF Areas Types
Standard Area
Link State Advertisment types
Type 1 - Represents a router
Type 2 - Represents the pseudonode (designated router – DR)
Type 3 - A network link summary (internal route)
Type 4 - Represents an ASBR
Type 5 - A route external to the OSPF domain
Type 7 - Used in stub areas in place of a type 5 LSA
ASBR
Notes: In the example above, router 2 acts as the area border router (ABR) between a standard area and the backbone. R3 is redistributing routes from an external domain, and is therefore designated as an autonomous system boundary router (ASBR).
As mentioned, type 1 and 2 LSAs are being flooded between routers sharing a common area. This applies to all area types, as these LSAs are used to build an area's shortest-path tree, and consequently only relevant to a single area. Type 3 and 5 LSAs, which describe internal and external IP routes, respectively, are flooded throughout the backbone and all standard areas. External routes are generated by an ASBR, while internal routes can be generated by any OSPF router.
Note the peculiar case of type 4 LSAs. These LSAs are injected into the backbone by the ABR of an area which contains an ASBR. This is to ensure all other routers in the OSPF domain can reach the ASBR.
Standard areas work fine and ensure optimal routing since all routers know about all routes. However, there are often situations when an area has limited access to the rest of the network, and maintaining a full link state database is unnecessary. Additionally, an area may contain low-end routers incapable of maintaining a full database for a large OSPF network. Such areas can be configured to block certain LSA types and become lightweight stub areas.

## Slide 9: Multiarea OSPF LSA Operation OSPF Areas Types
Stub Area
Router(config-router)# area 10 stub
ABR injects type 3 LSA with default route into stub area instead external routes.
Link State Advertisment types
Type 1 - Represents a router
Type 2 - Represents the pseudonode (designated router – DR)
Type 3 - A network link summary (internal route)
Type 4 - Represents an ASBR
Type 5 - A route external to the OSPF domain
Type 7 - Used in stub areas in place of a type 5 LSA
Notes: In this next example, R2 and R3 share a common stub area. Instead of propagating external routes (type 5 LSAs) into the area, the ABR injects a type 3 LSA containing a default route into the stub area. This ensures that routers in the stub area will be able to route traffic to external destinations without having to maintain all of the individual external routes. Because external routes are not received by the stub area, ABRs also do not forward type 4 LSAs from other areas into the stub.
For an area to become a stub, all routers belonging to it must be configured to operate as such. Stub routers and non-stub routers will not form adjacencies.
Configuration command example: Router(config-router)# area 10 stub
This idea of substituting a single default route for many specific routes can be applied to internal routes as well, which is the case of totally stubby areas.

## Slide 10: Multiarea OSPF LSA Operation OSPF Areas Types
Totally Stubby Area
Router(config-router)# area 10 stub no-summary
The default route (in type 3 LSA) substitutes all external and inter-area routes.
Link State Advertisment types
Type 1 - Represents a router
Type 2 - Represents the pseudonode (designated router – DR)
Type 3 - A network link summary (internal route)
Type 4 - Represents an ASBR
Type 5 - A route external to the OSPF domain
Type 7 - Used in stub areas in place of a type 5 LSA
Notes: Like stub areas, totally stubby areas do not receive type 4 or 5 LSAs from their ABRs. However, they also do not receive type 3 LSAs; all routing out of the area relies on the single default route injected by the ABR.
A stub area is extended to a totally stubby area by configuring all of its ABRs with the no-summary parameter:
Configuration command example: Router(config-router)# area 10 stub no-summary
Stub and totally stubby areas can certainly be convenient to reduce the resource utilization of routers in portions of the network not requiring full routing knowledge. However, neither type can contain an ASBR, as type 4 and 5 LSAs are not permitted inside the area. To solve this problem, and in what is arguably the worst naming decision ever made, Cisco introduced the concept of a not-so-stubby area (NSSA).

## Slide 11: Multiarea OSPF LSA Operation OSPF Areas Types
Not So Stubby Area
R3(config-router)# area 10 nssa
R2(config-router)# area 10 nssa default-information-originate
Link State Advertisment types
Type 1 - Represents a router
Type 2 - Represents the pseudonode (designated router – DR)
Type 3 - A network link summary (internal route)
Type 4 - Represents an ASBR
Type 5 - A route external to the OSPF domain
Type 7 - Used in stub areas in place of a type 5 LSA
ASBR
Notes: An NSSA makes use of type 7 LSAs, which are essentially type 5 LSAs in disguise. This allows an ASBR to advertise external links to an ABR, which converts the type 7 LSAs into type 5 before flooding them to the rest of the OSPF domain.
An NSSA can function as either a stub or totally stubby area. To designate a normal (stub) NSSA, all routers in the area must be so configured:
Configuration command example: Router(config-router)# area 10 nssa
Type 3 LSAs will pass into and out of the area. Unlike a normal stub area, the ABR will not inject a default route into an NSSA unless explicitly configured to do so. As traffic cannot be routed to external destinations without a default route, you'll probably want to include one by appending „default-information-originate“.
Configuration command example: Router(config-router)# area 10 nssa default-information-originate
To expand an NSSA to function as a totally stubby area, eliminating type 3 LSAs, all of its ABRs must be configured with the „no-summary“ parameter:
Configuration command example: Router(config-router)# area 10 nssa no-summary
The ABR of a totally stubby NSSA (or not-so-totally-stubby area, if you prefer) injects a default route without any further configuration.

## Slide 12: Multiarea OSPF LSA Operation OSPF Areas Types Summary
Standard areas can contain LSAs of type 1, 2, 3, 4, and 5, and may contain an ASBR. The backbone is considered a standard area.
Stub areas can contain type 1, 2, and 3 LSAs. A default route is substituted for external routes.
Totally stubby areas can only contain type 1 and 2 LSAs, and a single type 3 LSA. The type 3 LSA describes a default route, substituted for all external and inter-area routes.
Not-so-stubby areas implement stub or totally stubby functionality yet contain an ASBR. Type 7 LSAs generated by the ASBR are converted to type 5 by ABRs to be flooded to the rest of the OSPF domain.
Notes: An NSSA makes use of type 7 LSAs, which are essentially type 5 LSAs in disguise. This allows an ASBR to advertise external links to an ABR, which converts the type 7 LSAs into type 5 before flooding them to the rest of the OSPF domain.
An NSSA can function as either a stub or totally stubby area. To designate a normal (stub) NSSA, all routers in the area must be so configured:
Configuration command example: Router(config-router)# area 10 nssa
Type 3 LSAs will pass into and out of the area. Unlike a normal stub area, the ABR will not inject a default route into an NSSA unless explicitly configured to do so. As traffic cannot be routed to external destinations without a default route, you'll probably want to include one by appending „default-information-originate“.
Configuration command example: Router(config-router)# area 10 nssa default-information-originate
To expand an NSSA to function as a totally stubby area, eliminating type 3 LSAs, all of its ABRs must be configured with the „no-summary“ parameter:
Configuration command example: Router(config-router)# area 10 nssa no-summary
The ABR of a totally stubby NSSA (or not-so-totally-stubby area, if you prefer) injects a default route without any further configuration.

## Slide 13: OSPF Routing Tables and Route Types OSPF Routing Table Entries
  O – Router (type 1) and network (type 2) LSAs describe the details within an area (the route is intra-area).
  O IA – Summary LSAs appear in the routing table as IA (interarea routes)
  O E1 or O E2 – External LSAs external type 1 (E1) or external type 2 (E2) routes
    E1 metric=20*+internal cost
    E2 metric=20* [and forward metric]**
    E2 is default
    *) IGP = 20, EGP =1
    **) Forward metric is the path cost from the router to the ASBR. It is not visible by the show ip route command, but you can display it (both values) using show ip route <network>
Notes: 6.1.3.1 OSPF Routing Table Entries

## Slide 14: OSPF Routing Table and Types of Routes OSPF Route Calculation
The order in which the best paths are calculated is as follows:
  All routers calculate the best path or paths to destinations within their area (intra-area). These are the type 1 and type 2 LSAs – O.
  All routers calculate the best path or paths to the other areas within the internetwork. Type 3 LSAs - O IA.
  All routers calculate the best path or paths to the external autonomous system (type 5) destinations - O E1 or an O E2 .
Notes: 9.1 – Multiarea OSPF Operation
9.1.3 –OSPF Routing Table and Types of Routes
9.1.3.2 – OSPF Route Calculation

## Slide 15: 9.2 Configuring Multiarea OSPF
Notes: 9 – Multiarea OSPF
9.2 – Configuring Multiarea OSPF

## Slide 16: Configuring Multiarea OSPF Implementing Multiarea OSPF
There are 4 steps to implementing multiarea OSPF:
  Step 1. Gather the network requirements and parameters
  Step 2. Define the OSPF parameters
    Single area or multiarea OSPF?
    IP addressing plan
    OSPF areas
    Network topology
  Step 3. Configure the multiarea OSPF implementation based on the parameters.
  Step 4. Verify the multiarea OSPF implementation
Notes: 9.2 – Configuring Multiarea OSPF
9.2.1 – Configuring Multiarea OSPF
9.2.1.1 – Implementing Multiarea OSPF

## Slide 17: Configuring Multiarea OSPF Configuring Multiarea OSPFv2
There are no special commands to implement multiarea OSPFv2.
A router becomes an ABR when it has two network statements in different areas.
R1 is an ABR because it has interfaces in area 1 and an interface in area 0.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.1 – Configuring Multiarea OSPF
9.2.1.2 – Configuring Multiarea OSPFv2

## Slide 18: Configuring Multiarea OSPF Configuring Multiarea OSPFv3
There are no special commands required to implement multiarea OSPFv3.
A router becomes an ABR when it has two interfaces in different areas.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.1 – Configuring Multiarea OSPF
9.2.1.3 – Configuring Multiarea OSPFv3

## Slide 19: Verifying Multiarea OSPF Verifying Multiarea OSPFv2
Commands to verify multiarea OSPFv2
  show ip ospf neighbor
  show ip ospf
  show ip ospf interface
  Show ip protocols
  show ip ospf interface brief
  show ip route ospf
  show ip ospf database
Note: For the equivalent OSPFv3 command, simply substitute ipv6 for ip.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.1 – Verifying Multiarea OSPFv2

## Slide 20: Verifying Multiarea OSPF Verify General Multiarea OSPFv2 Settings
Use the show ip protocols command to verify the OSPFv2 status.
  Lists routing protocols configured on router, number of areas, router ID and networks included in routing protocol.
Use the show ip ospf interface brief command to display OSPFv2-related information for OSPFv2-enabled interfaces.
  Lists the OSPFv2 process ID, area that the interfaces are in, and interface cost.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.2 – Verify General Multiarea OSPFv2 Settings

## Slide 21: Verifying Multiarea OSPF Verify the OSPFv2 Routes
Use the show ip route ospf command to verify the muliarea OSPFv2 configuration..
  O represents OSPFv2 routes and IA represents interarea, which means that the route originated from another area.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.3 – Verify the OSPFv2 Routes

## Slide 22: Verifying Multiarea OSPF Verify the Multiarea OSPFv2 LSDB
Use the show ip ospf database command to verify the contents of the OSPFv2 LSDB.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.4 – Verify the Multiarea OSPFv2 LSDB

## Slide 23: Verifying Multiarea OSPF Verify Multiarea OSPFv3
Use the show ipv6 protocols command to verifyOSPFv3.
Use the show ipv6 interface brief to verify the OSPFv3-enabled interfaces and the area to which they belong.
Use show ipv6 route ospf to display the routing table.
Use show ipv6 ospf database to display the contents of the LSDB.
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.5 – Verify Multiarea OSPFv3

## Slide 24: Verifying Multiarea OSPF Packet Tracer - Configuring Multiarea OSPFv2
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.6 – Packet Tracer - Configuring Multiarea OSPFv2

## Slide 25: Verifying Multiarea OSPF Packet Tracer - Configuring Multiarea OSPFv3
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.7 – Packet Tracer - Configuring Multiarea OSPFv3

## Slide 26: Verifying Multiarea OSPF Lab - Configuring Multiarea OSPFv2
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.8 – Lab - Configuring Multi-area OSPFv2

## Slide 27: Verifying Multiarea OSPF Lab - Configuring Multiarea OSPFv3
Notes: 9.2 – Configuring Multiarea OSPF
9.2.2 – Verifying Multiarea OSPF
9.2.2.9 – Lab - Configuring Multi-area OSPFv3

## Slide 28: 9.3 Chapter Summary
Notes: 9 – Multiarea OSPF
9.3 – Summary

## Slide 29: Conclusion Chapter 9: Multiarea OSPF
Explain how multiarea OSPF operates in a small to medium-sized business network.
Implement multiarea OSPFv2 and OSPFv3.
Notes: 9.3 – Summary
9.3.1 – Conclusion
9.3.1.2 – Chapter 9: Multiarea OSPF

## Slide 30: Chapter 5: Dynamic Routing New Terms and Commands
Internal router Backbone router Autonomous System Boundary Router (ASBR) route redistribution LSA Type 1 LSA Type 2 LSA Type 3 LSA Type 4 LSA Type 5 | 
Notes: New Terms and Commands