## Slide 1
Implementing EtherChannel in a Switched Network

## Slide 2: Implementing EtherChannel in a Switched Network
The need for EtherChannel technology
Port aggregation negotiation protocols
Configuration steps for bundling interfaces into a Layer 2 EtherChannel
Configuring EtherChannel
Changing EtherChannel load-balancing behavior
How EtherChannel load-balancing works
The role of EtherChannel Guard

## Slide 3: The Need for EtherChannel

## Slide 4: EtherChannel Overview
EtherChannel is a technology that was originally developed by Cisco as a LAN switchto- switch technique of grouping several Fast or Gigabit Ethernet ports into one logical channel.
This technology has many benefits:
  It relies on the existing switch ports. There is no need to upgrade the switch-to-switch link to a faster and more expensive connection.
  Most of the configuration tasks can be done on the EtherChannel interface instead of on each individual port, thus ensuring configuration consistency throughout the switch-to-switch links.
  Load balancing is possible between the links that are part of the same EtherChannel. Depending on the hardware platform, you can implement one or several methods, such as source-MAC to destination-MAC or source-IP to destination-IP load balancing across the physical links.
Notes: Note Using new technologies like VSS (Virtual Switching System) and vPC (Virtual Port Channel), a port channel can be created across two aggregation switches from the same access layer to provide better redundancy.

## Slide 5: EtherChannel Mode Interactions
EtherChannel can be established using one of the following three mechanisms:
  LACP: IEEE’s negotiation protocol
  PAgP: Cisco’s negotiation protocol
  Static persistence: No negotiation protocol

## Slide 6: LACP
Link Aggregation Control Protocol (LACP) is part of an IEEE specification (802.3ad) that allows several physical ports to be bundled together to form a single logical channel. LACP allows a switch to negotiate an automatic bundle by sending LACP packets to the peer.
It ensures that when EtherChannel is created, all ports have the same type of configuration speed, duplex setting, and VLAN information. Any port modification after the creation of the channel will also change all the other channel ports.
The switch with the lowest system priority is allowed to make decisions about what ports actively participate in EtherChannel.

## Slide 7: LACP
Ports become active according to their port priority.
A lower number means higher priority.
Commonly up to 16 links can be assigned to an EtherChannel, but only 8 can be active at a time.
Nonactive links are placed into a standby state and are enabled if one of the active links goes down.
The maximum number of active links in an EtherChannel varies between switches.

## Slide 8: LACP Modes of Operation
These are the LACP modes of operation:
Active: Enable LACP
Passive: Enable LACP only if an LACP device is detected
The following are some additional parameters that you can use when configuring LACP:
System priority
  Each switch running LACP must have a system priority. The system priority can be specified automatically or through the CLI. The switch uses the MAC address and the system priority to form the system ID.
Port priority
  Each port in the switch must have a port priority. The port priority can be specified automatically or through the CLI.
Administrative key
  Each port in the switch must have an administrative key value, which can be specified automatically or through the CLI. The administrative key defines the capability of a port to aggregate with other ports, determined by these factors: the port’s physical characteristics, such as data rate, duplex capability, and point-to-point or shared medium.
Notes:   The port priority and the port number form the port identifier. The switch uses the port priority to decide which ports to put in standby mode when a hardware limitation prevents all compatible ports from aggregating.

## Slide 9: PAgP
Port Aggregation Protocol (PAgP) provides the same negotiation benefits as LACP.
PAgP is a Cisco proprietary protocol, and it will work only on Cisco devices.
PAgP packets are exchanged between switches over EtherChannel-capable ports.
Neighbors are identified and capabilities are learned and compared with local switch capabilities.
Ports that have the same capabilities are bundled together into an EtherChannel.
PAgP forms an EtherChannel only on ports that are configured for identical VLANs or trunking.
PAgP will automatically modify parameters of the EtherChannel if one of the ports in the bundle is modified.
PAgP and LACP are not compatible.
Notes: For example, if configured speed, duplex, or VLAN of a port in a bundle is changed, PAgP reconfigures that parameter for all ports in the bundle.

## Slide 10: PAgP Modes of Operation
These are the following two PAgP modes of operation:
■ Desirable: Enable PAgP
■ Auto: Enable PAgP only if a PAgP device is detecte

## Slide 11: Statically Bundle Links
Negotiation with either LACP or PAgP introduces overhead and delay in initialization.
As an alternative, you can statically bundle links into an EtherChannel.
This method introduces no delays but can cause problems if not properly configured on both ends.

## Slide 12: Layer 2 EtherChannel Configuration Guidelines
Before implementing EtherChannel in a network, plan the following steps necessary to make it successful:
The first step is to identify the ports that you will use for the EtherChannel on both switches.
Each interface should have the appropriate protocol identified (PAgP or LACP), have a channel group number to associate all the given interfaces with a port group, and be configured whether negotiation should occur.
After the connections are established, make sure that both sides of the EtherChannel have formed and are providing aggregated bandwidth.

## Slide 13: Layer 2 EtherChannel Configuration Guidelines
Follow these guidelines and restrictions when configuring EtherChannel interfaces:
EtherChannel support
  All Ethernet interfaces on all modules support EtherChannel, with no requirement that interfaces be physically contiguous or on the same module.
Speed and duplex
  Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode.
VLAN match
  All interfaces in the EtherChannel bundle must be assigned to the same VLAN or be configured as a trunk.
Range of VLANs
  An EtherChannel supports the same allowed range of VLANs on all the interfaces in a trunking Layer 2 EtherChannel.

## Slide 14: Layer 2 EtherChannel Configuration Guidelines
STP path cost
  Interfaces with different STP port path costs can form an EtherChannel as long as they are compatibly configured.
  Setting different STP port path costs does not, by itself, make interfaces incompatible for the formation of an EtherChannel.
Port channel versus interface configuration
  After you configure an EtherChannel, any configuration that you apply to the port channel interface affects the EtherChannel.
  Any configuration that you apply to the physical interfaces affects only the specific interface that you configured.

## Slide 15: EtherChannel Load-Balancing Options
Notes: To verify load-balancing options available on the device, use the port-channel loadbalance ? global configuration command.
Note Default configuration can differ from switch to switch, but commonly the default option is src-dst-ip. It is not possible to have different load-balancing methods for different EtherChannels on one switch. If the load-balancing method is changed, it is applicable for all EtherChannels.

## Slide 16: Configuring EtherChannel in a Switched Network

## Slide 17: Configuring EtherChannel in a Switched Network
Step 1.
Configure the two ports that connect each switch to use channel group 1 and LACP active mode:
Switch1# configure terminal
Switch1(config)# interface range Ethernet 1/1-2
Switch1(config-if-range)# channel-group 1 mode active
Creating a port-channel interface Port-channel 1
Step 2.
Enter interface configuration mode for the newly created port channel interface and configure it for trunk mode using dot1Q:
Switch1(config)# interface port-channel 1
Switch1(config-if)# switchport trunk encapsulation dot1q
Switch1(config-if)# switchport mode trunk

## Slide 18: Configuring EtherChannel in a Switched Network
Step 3.
On Switch 1, enter the show etherchannel summary command:

## Slide 19: Configuring EtherChannel in a Switched Network
Step 4.
Enter the show etherchannel load-balance command to verify which information EtherChannel uses to load balance traffic: