## Slide 1: Instructor Materials Chapter 5: Ethernet
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 2: Instructor Materials – Chapter 5 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3
Introduction to Network 6.0 Planning Guide
Chapter 5: Ethernet
Notes: Introduction to Network Planning Guide
Chapter 5: Configure a Network Operating System

## Slide 4: Chapter 5: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
5.0.1.2 | Class Activity | Join My Social Circle | Optional
5.1.1.5 | Interactive Activity | MAC and LLC Sublayers | Recommended
5.1.1.6 | Interactive Activity | Ethernet Frame Fields | Recommended
5.1.1.7 | Lab | Use Wireshark to Examine Ethernet Frames | Optional
5.1.2.8 | Lab | Viewing Network Device MAC Address | Optional
5.2.1.4 | Video Demonstration | MAC Address Tables on Connected Switches | -
5.2.1.5 | Video Demonstration | Sending a Frame to the Default Gateway | -
5.2.1.6 | Interactive Activity | Switch It! | Recommended
5.2.1.7 | Lab | Viewing the Switch MAC Address Table | Recommended
5.2.2.4 | Interactive Activity | Frame Forwarding Methods | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 5: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
5.3.1.3 | Packet Tracer | Identify MAC and IP Addresses | Optional
5.3.2.3 | Video Demonstration | ARP Request | -
5.3.2.4 | Video Demonstration | ARP Reply | -
5.3.2.5 | Video Demonstration | ARP Role in Remote Communication | -
5.3.2.8 | Packet Tracer | Examine the ARP Table | Recommended
5.4.1.1 | Class Activity | MAC and Choose… | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 5: Assessment
Students should complete Chapter 5, “Assessment” after completing Chapter 5.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7
Prior to teaching Chapter 5, the instructor should:
Complete Chapter 5, “Assessment.”
The objectives of this chapter are:
  Explain how the Ethernet sublayers are related to the frame fields.
  Describe the Ethernet MAC address.
  Explain how a switch builds its MAC address table and forwards frames.
  Describe switch forwarding methods.
  Describe the types of port settings available for Layer 2 switches.
  Compare the roles of the MAC address and the IP address.
  Describe the purpose of ARP.
  Explain how ARP requests impact network and host performance.
Chapter 5: Best Practices
Notes: 7

## Slide 8
Chapter 5: Best Practices (Cont.)
Explain that this chapter focuses on the Ethernet protocol, the most commonly used LAN technology in the world. Ethernet is a combination of Data Link layer software and Physical layer hardware, because the Physical and Data Link layers are tightly coupled.
Section 5.1
Remind students that Ethernet is a standardized protocol, therefore, it has well-defined rules for how it operates and for the structure of the Data Link layer frames and Physical layer signals it uses.
Explain that the Ethernet Data Link layer today has two main parts. The LLC sublayer links Ethernet to the upper layers, while the MAC sublayer controls the hardware. Ethernet can be used with a wide variety of physical media.
Notes: 8

## Slide 9
Chapter 5: Best Practices (Cont.)
Use the following web site to explaine IEEE shorthand identifiers, such as 10BaseT, and 100BaseT: http://computernetworkingnotes.com/network-technologies/10base-ethernet.html
Explain the chart on 5.1.2.1 and how it can be used to quickly translate hexadecimal to binary and decimal.
Describe the OUI and vendor assigned components of a MAC address.
Note: MAC addresses are unique to Ethernet networks (serial interfaces have no MAC address).
MAC Address vendor lookup - www.macvendorlookup.com
Perform a Wireshark demonstration (perhaps demo lab 5.1.1.7). Use Wireshark to capture several packets. Point out the different fields in the Layer 2 PDU.
Notes: 9

## Slide 10
Chapter 5: Best Practices (Cont.)
Section 5.2
Encourage students to view the video demonstrations on switch Mac address tables (5.2.1.4 and 5.2.1.5).
Use the good interactive activity on page 5.2.1.6.
Section 5.3
It is important that students understand the ARP process. Recommend that students watch the videos in 5.3.2 on ARP.
Use Packet Tracer to demonstrate the ARP process in a local network and in a remote network (see lab 5.3.2.8).
Describe how ARP entries age out of the ARP table.
View an overview of ARP at this web site: https://www.youtube.com/watch?v=hx9ZZivtzEE
Notes: 10

## Slide 11: Chapter 5: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna-blog
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Packet Tracer Know How 1: Packet Tracer 101 (self-enroll)
Notes: 11

## Slide 13: Chapter 5: Ethernet
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 14: Chapter 5 - Sections & Objectives
5.1 Ethernet Protocol
  Explain how the Ethernet sublayers are related to the frame fields.
  Describe the Ethernet MAC address.
5.2 LAN Switches
  Explain how a switch operates.
  Explain how a switch builds its MAC address table and forwards frames.
  Describe switch forwarding methods.
  Describe the types of port settings available for Layer 2 switches.
5.3 Address Resolution Protocol
  Compare the roles of the MAC address and the IP address.
  Describe the purpose of ARP.
  Explain how ARP requests impact network and host performance.
Notes: 14

## Slide 15: 5.1 Ethernet Protocol
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 16: Ethernet Protocol Ethernet Frame
Ethernet Encapsulation
  Ethernet operates in the data link layer and the physical layer.
  Ethernet supports data bandwidths from 10Mbps through 100Gbps.
  Ethernet standards define both the Layer 2 protocols and the Layer 1 technologies.
MAC Sublayer
  MAC constitutes the lower sublayer of the data link layer.
  Responsible for Data encapsulation and Media access control.
Ethernet Evolution
  Ethernet has been evolving since its creation in 1973.
  The Ethernet frame structure adds headers and trailers around the Layer 3 PDU to encapsulate the message being sent.
Ethernet Frame Fields
  The minimum Ethernet frame size is 64 bytes and the maximum is 1518 bytes.
  Frame smaller than the minimum or greater than the maximum are dropped.
  Dropped frames are likely to be the result of collisions or other unwanted signals and are therefore considered invalid.
Notes: 5.1 – Ethernet Protocol
5.1.1 – Ethernet Frame

## Slide 17: Ethernet Protocol Ethernet Frame (Cont.)
Notes: 5.1 – Ethernet Protocol
5.1.1 – Ethernet Frame

## Slide 18: Ethernet Protocol Ethernet MAC Addresses
MAC Addresses and Hexadecimal
  MAC address is 48-bit long and expressed as 12 hexadecimal digits.
MAC Addresses: Ethernet Identity
  IEEE requires a vendor to follow two simple rules:
  Must use that vendor's assigned OUI as the first three bytes.
  All MAC addresses with the same OUI must be assigned a unique value in the last three bytes.
Frame Processing
  The NIC compares the destination MAC address in the frame with the device’s physical MAC address stored in RAM.
  If there is a match, the framed is passed up the OSI layers.
  If there is no match, the device discards the frame.
MAC Address Representations
  MAC addresses can be represented with colons, dashes or dots and are case-insensitive.
  00-60-2F-3A-07-BC, 00:60:2F:3A:07:BC, 0060.2F3A.07BC and 00-60-2f-3a-07-bc are all valid representations of the same MAC address.
Notes: 5.1 – Ethernet Protocol
5.1.2 – Ethernet MAC Addresses

## Slide 19: Ethernet Protocol Ethernet MAC Addresses (Cont.)
Unicast MAC Address
  Unique address used when a frame is sent from a single transmitting device to a single destination device.
  The source MAC address must always be a unicast.
Broadcast MAC Address
  Used to address all nodes in the segment.
  The destination MAC address is the address of FF-FF-FF-FF-FF-FF in hexadecimal (48 ones in binary).
Multicast MAC Address
  Used to address a group of nodes in the segment.
  The multicast MAC address is a special value that begins with 01-00-5E in hexadecimal.
  The remaining portion of the multicast MAC address is created by converting the lower 23 bits of the IP multicast group address into 6 hexadecimal characters.
Notes: 5.1 – Ethernet Protocol
5.1.2 – Ethernet MAC Addresses

## Slide 20: 5.2 LAN Switches
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 21: LAN Switches The MAC Address Table
Switch Fundamentals
  An Ethernet Switch is a Layer 2 device.
  It uses MAC addresses to make forwarding decisions.
  The MAC address table is sometimes referred to as a content addressable memory (CAM) table.
Learning MAC Addresses
  Switches dynamically build the CAM by monitoring source MACs.
  Every frame that enters a switch is checked for new addresses.
  The frame is forwarded based on the CAM.
Filtering Frames
  Since the switch knows where to find a specific MAC address, it can filter the frames to that port only.
  Filtering is not done is the destination MAC is not present in the CAM.
Notes: 5.2 – LAN Switches
5.2.1 – The MAC Address Table

## Slide 22: LAN Switches Switch Forwarding Methods
Frame Forwarding Methods on Cisco Switches
  Store-And-Forward
  Cut-Through
Cut-Through Switching
  Fast-forward switching
    Lowest level of latency immediately forwards a packet after reading the destination address.
    Typical cut-through method of switching.
  Fragment-free switching
    Switch stores the first 64 bytes of the frame before forwarding.
    Most network errors and collisions occur during the first 64 bytes.
Memory Buffering on Switches
  Port-based memory
  Share memory
Notes: 5.2 – LAN Switches
5.2.2 – Switch Forwarding Methods

## Slide 23: LAN Switches Switch Port Settings
Duplex and Speed Settings
  Full-duplex – Both ends of the connection can send and receive simultaneously.
  Half-duplex – Only one end of the connection can send at a time.
  A common cause of performance issues on Ethernet links is when one port on the link operates at half-duplex and the other on full-duplex.
Auto-MDX
  Detects the type of connection required and configures the interface accordingly.
  Helps reducing configuration errors.
Notes: 5.2 – LAN Switches
5.2.3 – Switch Port Settings

## Slide 24: 5.3 Address Resolution Protocol
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 25: Address Resolution Protocol MAC and IP
The combination of MAC and IP facilitate the End-to-End communication.
Layer 2 addresses are used to move the frame within the local network
Layer 3 addresses are used to move the packets through remote networks.
Destination on Same Network
  Physical address (MAC address) is used for Ethernet NIC to Ethernet NIC communications on the same network.
Destination on Remote Network
  Logical address (IP address) is used to send the packet from the original source to the final destination.
Notes: 5.3 – Address Resolution Protocol
5.3.1 – MAC and IP

## Slide 26: Address Resolution Protocol ARP
Introduction to ARP
  ARP allows the source to request the MAC address of the destination.
  The request is based upon the layer 3 address of the destination (known by the source).
ARP Functions
  Resolving IPv4 addresses to MAC addresses
  Maintaining a table of mappings
  ARP uses ARP Request and ARP Reply to perform its functions.
Removing Entries from an ARP Table
  Entries are removed from the device’s ARP table when its cache timer expires.
  Cache timers are OS dependent.
  ARP entries can be manually removed via commands.
ARP Tables
  On IOS: show ip arp
  On Windows PCs: arp -a
Notes: 5.3 – Address Resolution Protocol
5.3.2 – ARP

## Slide 27: Address Resolution Protocol ARP Issues
ARP Broadcasts
  ARP requests can flood the local segment.
ARP Spoofing
  Attackers can respond to requests and pretend to be providers of services. Example: default gateway
Notes: 5.3 – Address Resolution Protocol
5.3.2 – ARP Issues

## Slide 28: 5.4 Chapter Summary
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 29: Chapter Summary Summary
Explain the operation of Ethernet.
Explain how a switch operates.
Explain how the address resolution protocol enables communication on a network.
Notes: 5.4.1 - Summary

## Slide 30: Section 5.1 New Terms and Commands
IEEE 802.2
IEEE 802.3
LLC Sublayer
MAC Sublayer
Data Encapsulation
Frame Delimiting
Cyclic Redundancy Check
Carrier Sense Multiple Access (CSMA)
Ethernet II
Frame Check Sequence (FCS)
Preamble
EtherType
Runt
Collision Fragment
Jumbo
Baby Giant Frame
Hexadecimal
Organizationally Unique Identifier (OUI)
Notes: New Terms and Commands

## Slide 31: Section 5.2 New Terms and Commands
burned-in address (BIA)
ipconfig /all command
ifconfig command
Unicast MAC Address
Broadcast MAC Address
Multicast MAC Address
Content Addressable Memory (CAM)
Store-and-forward
Cut-through
Fast-forward switching
Fragment-free switching
Port-based Memory Buffering
Shared Memory Buffering
Half-duplex
Full-duplex
Auto-MDIX
Address Resolution Protocol (ARP)
Notes: New Terms and Commands

## Slide 32: Section 5.3 New Terms and Commands
ARP Table
ARP Cache
ARP Request
ARP Reply
show ip arp, arp –a
ARP spoofing
Notes: New Terms and Commands