## Slide 1: PV198 – One-chip Controllers Ethernet

## Slide 2: Content
What is Ethernet used for
Overview
  ISO/OSI Model
  Headers
FRDM-K66F Ethernet
lwIP
Application

## Slide 3: What is Ethernet used for
Connecting embedded devices to a network

## Slide 4: Overview – ISO/OSI Model
Application
Physical structure
Physical
Network
HTTP, SMTP, DNS
IP, ICMP
Data
Transport
TCP, UDP
MAC
Session
Presentation
FTP, SSH

## Slide 5: Overview
By David Mudrák (mudrdmz) - Vlastní produkt, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=5181616

## Slide 6: Overview – IPv4 header
K66 Sub-Family Reference Manual, Figure 50-6.

## Slide 7: Overview – UDP header
K66 Sub-Family Reference Manual, Figure 50-11.

## Slide 8: FRDM-K66F Ethernet
10/100-Mbps Ethernet MAC (ENET)
Compliant with the IEEE802.3-2002 standard
Hardware acceleration block to optimize the performance of network controllers providing TCP/IP, UDP, and ICMP protocol services
CRC-32 checking / CRC-32 generation
Programmable MAC address

## Slide 9: FRDM-K66F Ethernet
Application
Micrel 32-pin Ethernet PHY
Physical
Network
Data
Transport
Session
Presentation
10/100-Mbps Ethernet MAC, ENET driver
Lightweight IP stack

## Slide 10: lwIP
Lightweight IP stack – link
Small independent implementation of the TCP/IP protocol suite – used in embedded
Features: IP, ICMP, UDP, TCP, DNS, DHCP, and more

## Slide 11: Application – Overview
The application sends a message to a Database
Uses UDP packets, InfluxDB and data are shown with Grafana
When you successfully send a message, it will be visible on a dashboard

## Slide 12: Application – Template
Contains initialization of pins, clocks, peripherals and lwIP
Works as UDP echo – when the board receives an UDP packet, it sends the packet back to the sender
Uses predefined static IP address

## Slide 13: Application – Source Code
Main:
  Configure (pins, clocks, peripherals, lwIP)
  Send udp packet – your task to implement
  Loop:
    Receive packets
UDP Callback:
  handle received packet – send the packet back to the sender

## Slide 14: Application – Task
Define your unique IP address (192.168.0.x)
Implement method in udpecho_raw.c:
  void udp_send_data(const ip4_addr_t dst_addr, uint16_t dst_port, char *msg);

## Slide 15: Homework
Send meaningful data to the database.
E.g.:
  Data from sensor (temperature, pressure, accelerometer, … )
  Logging information (button pressed, …)