## Slide 1: PV198 – One-chip Controllers I2C

## Slide 2: Content
What is I2C
What is it used for
How does it work
FRDM-K66F I2C
Accelerometer & Magnetometer
Application

## Slide 3: What is I2C
I2C – Inter-Integrated Circuit
Invented in 1982 by Philips Semiconductor (now NXP Semiconductors)

## Slide 4: What is it used for
Intra-board communication
Peripherals
Sensors

## Slide 5: How does it work
2 wires (Clock – SCL, Data – SDA) – pulled high
Multi-master & multi-slave
100 kbit/s – 5 Mbit/s
7-bit addressing / 10-bit addressing
Synchronous
Half-duplex

## Slide 6: How does it work – Scheme
https://learn.sparkfun.com/tutorials/i2c/all

## Slide 7: How does it work – Message
K66 Sub-Family Reference Manual, Figure 58-2.

## Slide 8: FRDM-K66F I2C
4 I2C modules
Address match wakeup in low power modes
SMBus support
DMA support
Methods to use:
  BOARD_I2C_Receive
  BOARD_I2C_Send

## Slide 9: Accelerometer & Magnetometer
FXOS8700CQ – link
3-axis, linear accelerometer + 3-axis, magnetometer combined into a single package

## Slide 10: Accelerometer & Magnetometer
Connected to I2C bus and 2 GPIO signals
Freedom FRDM-K66F Development Platform User’s Guide, Table 6.

## Slide 11: Application – Template
startInitialization (check sensor ID, wake-up)
setupOrientationDetection (enable detection, interrupts, etc.) – Homework
finishInitialization (setup frequency, activate sensor)

## Slide 12: Application
Create an application that reads accelerometer output data registers
Print register values into console
Bonus:
Calculate tilt angle from received values

## Slide 13: Homework
Create an application that detects orientation of the board (the same way as mobile phones do)
Use the feature of the sensor – do not calculate it in the MCU from XYZ register values
Use interrupt from sensor
Print current orientation into console when orientation of the board changes

## Slide 14: Homework
Write your code into method setupOrientationDetection()
Link to Application note: AN4068