## Slide 1: PV198 – One-chip Controllers SPI

## Slide 2: Content
What is SPI
What is it used for
How does it work
FRDM-K66F SPI
Sensor – BMP 280
Application

## Slide 3: What is SPI
SPI – Serial Peripheral Interface
Serial interface bus

## Slide 4: What is it used for
Intra-board communication
External peripherals
Sensors

## Slide 5: How does it work – Scheme
Figure 1. SPI configuration with master and a slave
https://www.analog.com/en/analog-dialogue/articles/introduction-to-spi-interface.html

## Slide 6: How does it work
4 wires (Clock, Chip Select, Master In Slave Out, Master Out Slave In)
Single-master & multi-slave
Chip Select selects slave for communication
Synchronous
Full-duplex
Possibility to use only 3 wires (only 1 data wire)

## Slide 7: How does it work – Message
By SPI_timing_diagram.svg: en:User:Cburnettderivative work: Jordsan (talk) - SPI_timing_diagram.svg, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=11405368

## Slide 8: FRDM-K66F SPI
3 SPI modules
Master & Slave support
Interrupts
Programmable frame size (4 to 16 bits)
6 peripheral Chip Selects

## Slide 9: Temperature & Pressure sensor
Bosch BMP280 Digital Pressure Sensor – link
Digital interfaces I²C (up to 3.4 MHz) SPI (3 and 4 wire, up to 10 MHz)
Pressure resolution 0.16 Pa
Temperature resolution 0.01°C

## Slide 10: BMP 280

## Slide 11: BMP 280 SPI
BST-BMP280-DS001-11

## Slide 12
BMP 280 SPI – Write
PV198 – One-chip Controllers, SPI / Dávid Danaj
<number>

## Slide 13
BMP 280 SPI – Read
PV198 – One-chip Controllers, SPI / Dávid Danaj
<number>

## Slide 14: Application
Create an application that reads temperature from BMP280 sensor
Print temperature into console

## Slide 15: Accelerometer & Magnetometer
GND
VCC
SCL
SDA
CSB
Temp &
Pressure
Sensor
BMP 280
SDO

## Slide 16: Application – Step-by-step guide
Study BMP280 Datasheet
Study Serial Peripheral Interface (SPI) chapter in MCU Reference manual
Setup pin routing
Setup DSPI peripheral driver (speed, timing, etc.)
Download BMP280_driver and temperature example
Import driver to the project, use example code
Implement HW specific functions – your main task
Repeat steps 1-7 if necessary

## Slide 17: Application – Template
Study BMP280 Datasheet
Study Serial Peripheral Interface (SPI) chapter in MCU Reference manual
Setup pin routing
Setup DSPI peripheral driver (speed, timing, etc.)
Download BMP280_driver and temperature example
Import driver to the project, use example code
Implement HW specific functions – your main task
Repeat steps 1, 2 and 7 if necessary

## Slide 18: Application – Template
Check pin routing
Check DSPI configuration
  Check timing
Check sensor.c/.h files

## Slide 19: Application – Traps
There are multiple traps in the template, here are hints:
  Make sure you do proper error checking for input data (And check that it works)
  You have to enable continuous chip select for the Transfer call

## Slide 20: Homework
Update the application to print pressure as well as temperature
Make sure to print the uncompressed pressure (don’t change it)