## Slide 1
NiTi ?

## Slide 2
Biological Objectives
Of the Root Canal Treatment
Eliminate pulp and debris
Eliminate bacteria and endotoxins
From the root canal system

## Slide 3
The Keys to Success
IRRIGATION
Shaping (apical taper or enlargement)
3D OBTURATION (Lateral and apical seal)

## Slide 4
IRRIGATION Protocole
- SODIUM HYPOCHLORITE (0,5% to 5.25%)
with
- LUBRICATING / CHELATING GEL (Glyde™)
And
- LIQUID EDTA (to eliminate smear layer)
Other solutions and irrigation devices are advocated to allow better desinfecting efficiency:
(Chlorhexidine, heat, ultrasonics, sonics…..)

## Slide 5
Evaluation of Glyde File Prep in Combination with Sodium Hypochlorite as a Root Canal Irrigant
Grandini S. et al. J Endodon 2002 ; 28 : 300-303
« Combined use of 2.5% Sodium Hypochlorite and Glyde File Prep allowed to obtain cleaner canal walls (less debris, less smear layer and a greater number of open dentinal tubules) than irrigation with saline or hypochlorite alone»
_______________________________________________________

## Slide 6
GLYDE File Prep™
Available in single dose compules
(avoids cross contamination)
EDTA
CARBAMIDE
PEROXIDE
HYDROSOLUBLE
GEL (GLYDE)

## Slide 7
Drawbacks of Conventional Hand Stainless Steel Preparation Techniques
TIME CONSUMING
LESS PREDICTABLE SHAPES IN CURVED
CANALS
DEBRIS EXTRUSION WITH FILING MOTION
MISHAPS (ledges, canal blockade, zipping of foramen)

## Slide 8
Advantages of
Rotary NiTi Techniques
FASTER THAN HAND PREPARATION
LESS CANAL TRANSPORTATION
MORE PREDICTABLE RESULTS
LESS DEBRIS EXTRUSION (LESS Post Op PAIN)

## Slide 9
Constant Taper (All instruments)
Variable Taper (ProTaper)
Characteristics of Rotary Nickel Titanium Instruments
Cutting blades
Or
Non cutting blades
(Radial Land)
Cutting blades

## Slide 10
NON CUTTING BLADE
(with Radial Land)
ProFile, GT System, K3
CUTTING ACTIVE
BLADE
(Hero 642, HeroShaper,
Mtwo, Alpha File, RaCe)

## Slide 11
Rotary Instrument with
a Constant taper
and Cutting Blades
have a tendency to screw-in

## Slide 12
Requires more pressure to cut and are subjected to more stress
(surface contact is
increased)
Berutti et al.J Endodon
2003;29:15-19
Rotary Instruments with a Constant taper and a Radial Land

## Slide 13
Rotary Instrument with a large cross-section
(central mass)
and a constant taper
are too stiff in taper higher than 4% to shape curvatures without risks of mishaps