## Slide 1: (VIII.) blood pressure in man (IX.) Non-invasive methods of blood pressure measurement
Physiology - practicals

## Slide 2
Arterial blood pressure curve
SBP
Systolic blood pressure
area above MAP
area under MAP
DBP
Diastolic blood pressure
MAP
Mean arterial pressure
inter-beat interval
Mean arterial pressure (MAP) : mean value of blood pressure in the inter-beat interval (IBI)
  area under MAP = area above MAP
  aproximation: MAP DBP + 1/3 PP (PP = SBP – DBP)
PP
pulse pressure
Blood pressure (BP): pressure on vascular vall (continual variable)
Definition:
SBP - maximum of BP in the inter-beat interval
DBP – minimum of BP in the inter-beat interval
Attention: Values of SBP and DBP varies in different parts of cardiovascular system

## Slide 3: MAP is a function of cardiac output and total peripheral resistance
SBP is given mainly by CO
DBP is given mainly by TPR
Mean arterial pressure (MAP)
Total peripheral resistance (TPR)
Heart rate
(HR)
Stroke volume
(SV)
=
*
*
Cardiac output
(CO)

## Slide 4: Blood pressure regulation
Short-term – neural control, mainly baroreflex
Medium-term – hormonal regulation, renin-angiotensin-aldosteron system (RAAS)
Long-term – hormonal regulation of blood volume

## Slide 5
Short-term BP control: Baroreflex
Autonomic nervou system: sympathetic nerves ( BP, HR, SV a TPR) X parasympathetic nerves (BP, HR, SV a TPR)
Baroreflex: regulation of BP via changes of HR and TPR
baroreceptors – sinus caroticus + aorticus afferentation: n. vagus, n. glosopharingeus
Cardiac branch of baroreflex:
efferentation: n. vagus - SA node
sympathetic efferentation: change of HR and cardiac contractility
↑BP →↓HR and vice versa
Peripheral branch of baroreflex:
efferentation: sympathetic vascular innervation ↑BP →↓TPR and vice versa (vasoconstriction, venoconstriction)

## Slide 6
Short-term influences
blood volume - influence to SV (bleeding, dehydration)
external pressure to the vessels - intrathoracal a intraabdominal pressure (cough, defecation, childbirth, artificial ventilation)
position – orthostasis: higher DBP (TPR) a lower STK (venous return heart filling  Starling principle cardiac contraction  SV)
CNS – emotions, mental stress,…
physical load – BP changes depend on intensity, duration and type of exercise
heat ( TPR), cold ( TPR)
alcohol, medicaments,…
Long-term influences
age (the fastest changes during childhood and adolescence)
sex (men: higher BP)
Blood pressure changes

## Slide 7
Methods of the arterial blood pressure measurement
24-hour blood pressure monitoring
Photoplethysmografic (volume-clamp method, Peňáz)
Palpatory
(sphygmomanometer)
Auscultatory
(sphygmomanometer,
stethoscope)
Oscillometric
In practicals:
Another approaches:

## Slide 8
Laminar / turbulent flow, Korotkoff sounds
Reynolds number Re: predicts the transition from laminar to turbulent of flo v: velocity of blood flow
S: area of vascular lumen (.r2)
: density of blod
: viskosit of blood
(higher in anemy)
S1 < S2 a v1≈ v2 → Re1 < Re2 → turbulent flow
laminar flow Re < 2000
turbulent flow Re > 3000
r1
r2
cuff
a. brachialis
laminar flow
turbulent flow
Re1
Re2
v1
v2
closely behind narrowing of the artery:

## Slide 9
Korotkoff sound
(auscultatory method)
Continually measured BP
Pressure in the cuff
Pressure oscillations in the cuff
(Oscillometric method)
SBP
DBP
SBP
MAP
DBP
Blood flow in the artery
Principles of blood pressure measurement

## Slide 10
24-hour blood pressure monitoring
BP decrease during night: 10 - 15%
8
9
11
10
12
13
14
16
15
17
18
19
21
20
22
23
24
2
1
3
4
5
7
6
100
120
140
100
80
120
80
60
60
[bpm]
[mmHg]
SBP
DBP
Heart rate
waking
sleeping
Blood pressure
Heart rate
hours

## Slide 11
Patient is sitting for a few minutes before the measurement.
Only validated apparatus must be used.
Perform at least two measurements in the course of 1–2 minutes.
Use cuff of standard size (12–13 cm width and 35 cm length); however smaller and bigger cuffs must be available for patients with smaller or bigger size of arm, respectively.
Cuff must be always at the level of heart of examined person.
Pressure in the cuff must be decreased slowly: 2mmHg/s.
During BP measurement following rules must be observed

## Slide 12
methods | advantages | disadvantages | measured value
auscultatory | exact estimation of SBP/DBP easy, it doesnt require electricity | subjective, experience is necesary SBP/DBP from differen IBI | STK a DTK
oscillometric | exact estimation of MAP automatic, fast BP can be measured by layman, cheap (home measurement) | DBP/SBP is calculated (dependence on model, influence on shape of puls wave) SBP/DBP from different IBI false values during arrhytmia | MAP, sometimes SBP (it depends on device)
24 – hour BP monitoring | BP record from whole day diagnosis of white-coat hypertension | disruptive influence of measuring (during sleeping) SBP/DBP from different IBI | BP is mesured each 15 – 60 min
photople-thysmographic (Peňáz) | continual BP record possibility of beat-to beat SBP/DBP calculation (BP variability analysis) | measuring on the finger, brachial BP recalculating expensive device | continual BP record

## Slide 13
Diagnosis of hypertension
 | blood pressure | SBP [mmHg] | DBP [mmHg] | posible complications
normal | optimal | <120 | <80 | 
 | normal | 120 – 129 | 80 – 84 | 
 | high normal | 130 – 139 | 85 – 90 | 
hyper-tension | stage | 140 – 159 | 90 – 99 | without organ changes
 | 2. stage | 160 – 179 | 100 – 109 | hypertrophy of L ventricle, proteinuria, angiopathy, ...
 | 3. stage | > 180 | > 110 | morphological and functional changes of some organs, retinopathy, heart and renal insufficiency, ischemia of CNS, bleeding in CNS
isolated systolic hypertension: SBP> 140 and DBP <90
high normal BP – annual monitoring recomended
home measurement to exclude white coat hypertension
hypertension is diagnosed when:
average BP from 4 – 5 examinations is > 140/90
BP during a home measurement repeatedly > 135/80
mean BP from 24-hour monitoring is > 130/80

## Slide 14
Changes of blood pressure during exercise
increase of BP depends on the type, intensity and duration of the load
sympathetic activation: changes in the cardiovascular system serve to satisfy metabolic needs of working muscle
impact of exercise on blood pressure
  increased cardiac output  ↑STK
  Redistribution of blood in the body - metabolic vasodilation in muscle (muscle increases blood flow), vasoconstriction in the GIT, skin and kidneys  maintaining or slight change in DBP (depending on the extent of the TPR decrease)
vasoconstriction in the skin is temporary, since thermoregulatory mechanisms dominate
DBP increases during isometric muscle work (eg. weightlifting)
after exercise: decrease of BP on the initial or a slightly lower value, the blood flow in the muscle remains elevated until recovery
Recovery interval is determined by the parasympathetic tone (can be increased training)