## Slide 1
Water and health
RNDr. Danuše Lefnerová, Ph.D.
Doc.Ing. Martin Krsek, CSc.

## Slide 2
Water and health
Act No. 258/2000 Coll.
on public health protection:
„Drinking water is all water in its original state or after treatment intended for drinking, cooking, preparation of food and drinks, water used in the food industry, water intended for body care, cleaning of objects , which by their intended purpose come into contact with food or human body and for other purposes of human consumption, irrespective of its origin, state and mode of delivery. „

## Slide 3
Function of water in body:
- transport (transmission of nutrients, waste products, heat,
electrolytes, hormones)
- assistance in thermoregulation
- acts as a solvent and a suitable environment for chemical reactions taking place
in the body
- protects the surroundings of joints, spinal cord and brain
- surrounds the fetus like amniotic fluid
- involved in maintaining homeostasis, ensuring a physically and chemically
stable internal environment of the body
Water and health

## Slide 4
Water requirement:
Very individual, can not be standardized.
It depends on many factors - age, sex, weight, ambient temperature and air humidity,
health, diet, physical activity
After birth, water is 75% of body weight, in adults 60% and in old age 50% of body weight
The need for water is partly covered by its natural content in foods ranging from 20-30%
(very fatty products) and very often between 80-90% (fruits, vegetables, soups, sauces).
Water and health

## Slide 5
By the oxidative metabolism of organic macronutrients, 300 ml of water per day is
produced in the human body.
Necessary water intake is average 2.5 l per day for an average adult (1.5 liters in the form
of beverages and 1 l from regular food).
Literature - 22 ml - 50 ml per kg of body weight, regardless of climatic conditions
Children are dehydrated faster, so they should drink more - schoolchildren by half more
than adult of the same weight.
Water output and intake should always be in equilibrium
Water and health

## Slide 6
Lack of water in the body (dehydration) - headaches, fatigue, malaise, decrease
in physical and mental performance, including decreased concentration
- children - decreased ability to concentrate
Long-term fluid deficiency - renal impairment, kidney and urinary stones,
risk of urinary tract infection,…
Water and health

## Slide 7
Biological (biogenic) value of drinking water
Drinking water must be health-conscious with a satisfactory biological value.
Mineral substances contained in drinking water are usually in ion form, perfectly dissolved, and are therefore easily resorbable and more usable for the organism.
Water is an important source of all required minerals
(fluorine in the form of fluoride anions, iodine, sodium,
potassium, the calcium / magnesium ratio, selenium,
zinc and other macro and micro elements).

## Slide 8
Drinking water sources - their protection
Czech Republic - surface sources: underground source = 1: 1 2016 - 2.305 water treatment plants - 600 million m3 (Prague 100 million) Brno dam - 7.6 - 10.8 million m3
When determining the range of hygiene protection, account shall be taken of:
- geological composition of soil, its permeability (sand x clay) - slope of the land around the source - yield of water source - industrial activity - agricultural activity - transportation around the source

## Slide 9
Drinking water sources - a multi-barrier approach to their protection
To ensure that water is microbiologically safe, it is necessary to apply: 1. barrier - consistent protection of water source (functional protection zone) 2. barrier - the use of such water treatment technology, which corresponds to
the quality of raw water 3. barrier - water protection against secondary contamination during
distribution/transport to the consumer 4. barrier - internal water supply (domestic water supply) - design of hygienically
safe materials

## Slide 10
Drinking water sources - water treatment
Category according to Decree of the Ministry of Health No. 428/2001 Coll., As amended by Decree No. 146/2004 Coll. Sources % Sources % surface underground A 1 - Simple physical treatment and disinfection, for example fast filtration and disinfection, or simple sand filtration, chemical deacidification or mechanical deacidification or removal gaseous components by aeration. 7.1 76.5 A 2 - common physical treatment, chemical treatment and disinfection, coagulation filtration, infiltration, slow biological filtration, flocculation, sedimentation, filtration, disinfection (final behavior), single- or two-stage jamming and demagnetization. 54 9 A 3 - intensive physical and chemical treatment, extended treatment and disinfection, for example chlorination to break point, coagulation, flocculation, sedimentation, filtration, adsorption (activated carbon), disinfection (ozone, final chlorination). Combination physically chemical and microbiological and biological treatment 38,9 14,5

## Slide 11
Drinking water sources and their protection
Suspicion or finding that the water in the source is contaminated:
The source of the pollution is removed, building modifications are carried out, the hygienic protection zone is restored
Wells - the inner walls of the well are mechanically cleaned, the water is drained, the bottom is cleaned from sludge
One-off disinfection is carried out

## Slide 12
Disinfection of drinking water
Chloramine - 2-3 g / m3 of water, Savo, Chlorine, Sagen (AgCl – oligodynamic effects of Ag), Ozone, UV, filtration
Boiling : bubbles on the whole surface of water (100 ° C), leave for 10 minutes stand and naturally cool down - do not put ice in it. Water is not sterile !!! (sterility only ensures sterilization in the autoclave).

## Slide 13
Non-potable/running water
It is hygienically safe water, which is not used as drinking water and for cooking but only for washing, bathing and for production purposes.
Domestic hot water is produced from drinking water under the Public Health Act but is not considered drinking water (for ex. Legionella pneumophila).
Industrial water
Technological water
Water for irrigation

## Slide 14
Microbes transmitted by water
Condition: excretion of agent by excrement (humans and animals) and possibility of new food infections
Viruses:
Rotaviruses - diarrhoeal diseases Polioviruses - agents of poliomyelitis RNA viruses – hepatitis A, E, (F)

## Slide 15
Viruses – cont.:
Norovirus - originally called the Norwalk virus
(1972 Norwalk USA)
- RNA virus - it causes an epidemic acute gastroenteritis - diseases from water (Prague-Dejvice 2015), food, but also through direct contact
- symptoms of the disease - nausea, vomiting, diarrhea and abdominal cramps, mild fever, fever, pain of muscles and headache, fatigue - it is also transmitted via a faecal oral route
Microbes transmitted by water

## Slide 16
Gram negative facultative anaerobic rods:
Escherichia coli, Klebsiella spp., Citrobacter spp., Salmonella typhi, Salmonella paratyphi - frequent water transfer
Shigella sonei, Shigella flexneri - bacillary dysentery
Yersinia entrocolitica - diarrheal diseases in children Serratia marcescens - infection of the urogenital and respiratory tract Proteus mirabilis, Proteus vulgaris – urogenital tract, gastroenteritis in infants
Microbes transmitted by water

## Slide 17
Gram negative aerobic rods and cocci:
Klebsiella pneumoniae, Pseudomonas aeruginosa
via aerosols
inflammation of the upper respiratory tract, lung,
urogenital tract
Neisseria gonorhoea, Treponema pallidum
- they do not survive in the waters, transmission is unlikely
Campylobacter spp. - diarrheal diseases
Microbes transmitted by water
Notes: Klebsiella pneumoniae se často vyskytuje jakou součást fyziologické střevní flóry, a proto ji běžně nacházíme ve stolici.
Tato bakterie patří mezi tzv. podmíněně patogenní kmeny. To znamená, že člověku způsobuje potíže pouze, pokud se dostane mimo své přirozené prostředí, tedy mimo střevo. Nejčastěji tedy způsobuje infekce močových cest.
P. Aer - kolonizuje hlavně sliznice dýchacího a močového ústrojí.

## Slide 18
Legionella pneumophila (Legionella) – G- aerobic rod
Occurrence:
hot and cold water, surface water, water courses as part of biofilms, filters, refrigeration circuits of air conditioners.
Survives in humid environments It lives and multiplies at 25-50 oC. Spread with air - inhalation of aerosol contaminated water
Respiratory tract infections, pneumonia (Legionnaires' disease)
Microbes transmitted by water
1976 Philadelphia
(182 – 29)

## Slide 19
Leptospirosis – G- spirochete
Febrile bacterial disease, a zoonotic disease caused by genera Leptospira
The way of infecting people is contacting damaged skin, eyes or mucous membranes with water contaminated by the urine of the infected animal
This is an antropozoonosis – transfer from animal (rats, mice, cattle) to humans
Symptoms - high fever, chills, tremor, severe headache
and muscle aches, abdominal pain, nausea, vomiting
Microbes transmitted by water

## Slide 20
Microbes transmitted by water
Fungi and yeasts – water mains, air washers, air conditioning

## Slide 21
Cryprosporidium - protozoa - occurrence in surface waters. - it can also penetrate into drinking water - chemical disinfection
against oocysts is ineffective.
causes diarrheal disease - cryptosporidiosis.
1993 Milwaukee Cryptosporidiosis outbreak - 400,000 patients
104 death Giardia intestinalis - human lamblia - it causes diarrheal disease – giardiasis
Protozoa
Infective germ can enter the body
and cause the disease not only
by the digestive tract, but also
by the airways, skin abrasions
and injuries.
Notes: Cryptosporidium oocysts that passed through the filtration system of one of the city's water-treatment plants, arising from a sewage treatment plant's outlet 2 miles upstream in Lake Michigan.
This abnormal condition at the water purification plant lasted from March 23 through April 8, after which, the plant was shut down. Over the span of approximately two weeks, 403,000[3] of an estimated 1.61 million residents in the Milwaukee area (of which 880,000 were served by the malfunctioning treatment plant) became ill with the stomach cramps, fever, diarrhea and dehydration caused by the pathogen.[3] Deaths have been attributed to this outbreak, mostly among the elderly and immunocompromised people, such as people with AIDS.

## Slide 22
Health aspect
The route of inhalation and dermal - may be more risky than the oral route
substances after entry into the body can affect the target organs before liver
biotransformation.
- doses received by inhalation and dermal route are, in their sum, at least equal
to the dose obtained by ingestion of 2 liters of water.
Extra-intestinal and intestinal disease - extra-intestinal and intestinal infections

## Slide 23
Water hardness and cardiovascular diseases
Water hardness - mainly composed of calcium and magnesium carbonate
History: The 50s of the last century - Japanese chemist Kobayashi pointed out that mortality on the cerebral vascular disease of the population is higher in the vicinity of the Japanese rivers, where the water is more acidic (softer) than the rivers with water harder (more basic) - from where the water was used for drinking purposes.
The relationship between drinking water hardness and mortality in cardiovascular disease - demonstrated
in many further studies.

## Slide 24
Water hardness and cardiovascular disease
Calcium: necessary for the proper functioning of the heart's transfer system, for blood clotting and neuromuscular irritation
Magnesium: an important role as a cofactor and activator of over 300 enzymatic reactions including glycolysis, ATP metabolism, transport of elements such as Na, K, Ca through membranes.
It is also important for protein and nucleic acid synthesis.
Magnesium deficiency increases the risk of vascular spasms and promotes cardiac arrhythmias.
Protective effect of calcium and magnesium against the development of tooth decay

## Slide 25
Water hardness and cardiovascular disease
Calcium and magnesium - beneficial antitoxic function
Ca and Mg also prevent the absorption of some toxic metals such as lead and cadmium.
Utilization of magnesium from the water is also higher than that from food.
Cooking in soft water causes considerable loss of elements from food, while cooking in hard water minimizes losses.

## Slide 26
Drinking water and cancer
Water disinfection with chlorination – chlorine can react with higher level of organic substances in water – production of low-molecular substances (chloroform, chlorobenzene, heptachlor and other chlorinated compounds) - genotoxic activity.
Studies show a connection between drinking chlorinated drinking water and the occurrence of bladder, rectum, kidney tumors. Negative effects on reproduction have also been demonstrated.
Arsenic in drinking water - exposure is associated with the occurrence of various skin lesions (pigmentation, keratoses, skin tumors and malignant tumors).
Arsenites show high embryotoxicity.
Notes: Přidá-li se do vody chlor, reaguje s ní za vzniku rovnovážné směsi chloru, kyseliny chlorné a kyseliny chlorovodíkové (poměr závisí na pH):[1]
Cl2 + H2O → HClO + HCl
Kyselina chlorná je považována za silnější oxidant než chlor.
Kyselina chlorná reaguje s širokou škálou biomolekul, včetně DNA, RNA[6][7][8][9], mastnými kyselinami, cholesterolem[10][11][12][13][14][15][16][17] a bílkovinami
2 HClO → 2 HCl + O2

## Slide 27
Drinking water and cancer
Nitrates - no clear epidemiological evidence that people who consume drinking water with increased nitrate content are at increased risk of cancer (reaction with amino acids to produce nitrosamines).
Only one of three UK studies has revealed a relationship between stomach cancer mortality and nitrate content in water. So far, the results are inconsistent.
Methemoglobinemia may be more significant – especially in infants
Radionuclides – mainly natural radionuclides are important for drinking water.
It is generally assumed that the ingestion of radon in drinking water is not associated with any significant risk of cancer.
Notes: Methemoglobin is a form of hemoglobin that contains the ferric [Fe3+] form of iron (oxydized form of hemoglobin). The affinity for oxygen of ferric iron is impaired. The binding of oxygen to methemoglobin results in an increased affinity for oxygen in the remaining heme sites that are in ferrous state within the same tetrameric hemoglobin unit.[1] This leads to an overall reduced ability of the red blood cell to release oxygen to tissues,
Normální hladina methemoglobinu je pod 1 %, měřeno ko-oximetrickým testem;[zdroj?] u zdravých dětí je tato hladina až 3,61—6.44 % (měřeno spektrofotometricky), protože mají méně aktivní enzym methemoglobinreduktázu

## Slide 28
Drinking water and cancer
Fluorides - fluorization of drinking water to prevent tooth decay has been reversed in the Czech Republic.
Environmental studies have not confirmed the effect of fluorides on cancer.
Industrially produced organic substances (chlorophenols, trichlorethylene, volatile organic compounds) - besides impairment of the immune system, there was an increased incidence of bladder cancer.

## Slide 29
Drinking water and cancer
Cyanobacterial toxins (cyanotoxins)
Cyanobacteria - in warmer waters with higher nutrient
content (especially phosphorus - agriculture,
detergents)
They can cause digestive tract disorders, allergic reactions, liver disease, immune system weakness, respiratory and contact dermatitis…
They have embryotoxic and genotoxic effects

## Slide 30
Drinking water and cancer
Drinking water can theoretically contribute to the annual increase in the probability of developing cancers in the Czech Republic by only 1-2 cases to the total number of over 60,000 new cases of newly reported cancer.

## Slide 31
Bottled water
Natural mineral water Spring water Infant water Drinking water Natural mineral water: extracted from an underground source that must be approved and regularly inspected by the Ministry of Health
Mattoni, Magnesia, Podebrady

## Slide 32
Spring water (table): from a protected underground source that does not need to be approved by the Department of Health.
It must not be modified in any way that would alter the characteristic composition
Toma natura, Bonaqua
Infant water: from a protected underground source, and more stringent requirements apply to it Mountain spring (Horský pramen)
Drinking water: It does not have to come from an underground source, it can be tapped from the public water supply, the quality is comparable to drinking water quality from the water supply
Bottled water

## Slide 33
Parametr (mg/l) Infant water drinking water
Nitrates 10 50
Nitrites 0,02 0,5
Na 20 200
Fluorides 0,7 1,5
Chlorides 100 100
Antimon (Sb) 0,003 0,005
Cyanides 0,005 0,05
Arsenic 0,005 0,01
Chrome 0,025 0,05
Cadmium 0,002 0,005
Copper 0,2 1
Lead 0,005 0,01
Mercury 0,0005 0,001
Infant water x normal drinking water

## Slide 34
Mineral bottled water
If you would drink only mineral water, you would get too much salt into your body, especially sodium.
The mineral waters - benefit mainly in heat, during heavy work and intense sports
Pregnant and lactating women should choose those with higher potassium and calcium levels
The sodium content should be mainly watched by the cardiac
Dyspnoeic people, people who suffer from swelling, who tend to develop kidney stones – no mineral water at all
Artificially supplied carbon dioxide does not bring anything to the body to benefit. It contributes to bloating and burying. Carbon dioxide is the waste product that our body must actually constantly get rid of.

## Slide 35
Health risks - demineralized water
Demineralized water - it does not have the character of drinking water and its regular consumption or one-off consumption in large quantities must be considered as a health risk
Devices based on distillation or deionization must be rejected as the final stage of drinking water treatment:
- virtually zero intake of calcium and magnesium with water
- reduced intake of some essential elements and microelements
- high losses of calcium, magnesium and other essential elements from foods cooked
in demineralized water

## Slide 37
Water enriched with oxygen
Water artificially enriched with pure oxygen - a food supplement
Manufacturers claim: increased oxygen concentration in blood, increased vitality and performance, blood pressure regulation, improved metabolism, increased immunity, increased resistance to stress, improved concentration and memory
Our body needs oxygen in blood and tissues but definitely not in digestive system, which is supposed to be anaerobic.
A safe concentration of oxygen in drinking water can be considered to be up to 25 mg per liter.
Increased oxygen saturation - the risk of oxidative stress and its cytotoxic effects
An increase in chromosome aberrations was observed in rats

## Slide 38
Water enriched with oxygen
Oxygen-enriched water manufacturers have not yet submitted any scientific study that would confirm the safety of higher oxygen values in water (when consumed)
Further work is needed to confirm or eliminate the potential physiological and toxic effect of oxygen enriched water
No international recommendations (WHO, FAO, etc.) on the safe maximum concentration of oxygen in drinking water
Natural pure water has a maximum of about 10 mg of oxygen per liter

## Slide 39
DECREE No. 83 of 30 April 2014 amending Decree No. 252/2004 Coll., laying down
the sanitary requirements for drinking and warm water and the frequency and scope
of drinking water control, as amended
Limit value (MH): Exceeding does not usually present an acute health risk.
Unless otherwise indicated, this is the upper limit of the allowable range.
Highest limit value (NMH): The value of a health-related indicator of the quality
of drinking water as a result of which the use of water as a drinking water is excluded,
unless the public health authority decides otherwise under the law.
Water and health - Microbiological analysis of water

## Slide 40
Microbiological analysis of water
Indicator (groups of) bacteria
Psychrophilic bacteria (22oC) - indicators of general contamination (200)
Mesophilic bacteria (36oC) - indicators of general contamination (40)
Faecal contamination
Coliform bacteria - indicators of faecal contamination
(Escherichia spp., Salmonella spp., Shigella spp., Yersinia spp.) Enterococci - indicators of faecal contamination
Clostridium perfringens
Escherichia coli

## Slide 41
Sampling procedure for microbiological analysis
If the well has not been used for a long period of time (eg in the winter season), it is necessary to drain the well prior to sampling (at least rinse well pipes from the well to the sampling point). If the well is drained, the water is allowed to rise and then sample of water is taken. • A sample of water is taken from the point where water is normally used (from the distribution line, from the tap, from the pump, etc.). The sample can not be taken over the hoses used for watering and sprinkling. • Prior to sampling, the water is drained for 1 to 5 minutes evenly (according to the length of the pipeline) and then sampling bottle is filled with the sample as described below. The sample bottle is held in such a way that any impurity from the hands does not get into the sampler. • Samples should be stored in a refrigerator and taken to the laboratory within 48 hours after sampling, sample for bacteriological analysis within 24 hours! Sampling for chemical analysis:  The sample is taken up in polyethylene sample bottles (bottles). When sampling, the sample bottle, including the closure, is rinsed three times with tap water.  The sample bottle is filled to the edge. Sample collection for bacteriological analysis:  The sample is to be taken only into glass bottles with aluminum foil.  The sample bottle is opened just before sampling. The sample bottle is not flushed and it is filled so that between the surface and the plug there is about 2 cm of air.  After closure of the bottle, the socket plug is again covered with aluminum foil.

## Slide 42
Microbiological analysis of water Determination of indicators of general contamination
1 ml of water plus 15 ml of TYEA agar
Cultivation
at 22oC – psychrophilic bacteria at 36oC – mesophilic bacteria
Drinking water surface water
1 ml
1 ml
1 ml
Water
sample
Phosphate
buffer

## Slide 43
Microbiological analysis of water Determination of indicators of faecal contamination
Cultivation medium
Endo 37oC
coliform bacteria
mFC 44oC
termotolerant coliform bacteria
SB 37oC
enterococci

## Slide 44
Coliform bacteria

## Slide 45
Escherichia coli

## Slide 46
HiCrome Chromogenic Coliform Agar (CCA)
HiChromogenic Coliform Agar is a selective medium recommended for the simultaneous detection of Escherichia coli and total coliforms in water samples (1).
The medium contains three chromogenic substrates.
The enzyme ß-D-galactosidase produced by coliforms cleaves 6-chloro-3-indoxyl-β-D-galactopyranoside to form pink to red coloured colonies (3).
The enzyme ß-D-glucuronidase produced by E.coli, cleaves 5-bromo-4chloro-3-indoxyl-β-D-glucuronic acid (2).
Colonies of E.coli give dark blue to violet coloured colonies due to cleavage of both the chromogens.
The presence of the third chromogen IPTG enhances the colour reaction. Addition of L-Tryptophan improves the indole reaction thereby increasing the detection reliability.

## Slide 47
Termotolerant coliform bacteria

## Slide 48
Slanetz & Bartley Medium
Originally intended as a medium for the enumeration of enterococci in water using
Membrane Filtration, this medium has become more popular in many other areas such
as food bacteriology.
The medium contains Tetrazolium Chloride, which is reduced by enterococci
to the insoluble red dye Formazan resulting in dark red colonies of enterococci on the agar.
It should be noted that this reaction is not exclusive to enterococci and colonies should
be confirmed by additional testing e.g. aesculin hydrolysis.
Enterococci

## Slide 49
Physico-chemical properties
pH Alkalite Total hardness Nitrates
Nitrites Chlorides Sulfates Phosphates
Oxidability Ammonia Calcium Magnesium Iron Cadmium Trihalomethanes PAH - polyaromatic hydrocarbons
Organoleptic evaluation - temperature, color, turbidity, taste, smell

## Slide 50
Accredited water analysis in Brno Water management services of the Czech Republic
Basic analysis of water with mikrobiology - 1290, - CZK pH overall hardness COD-Mn (Chemical Oxygen Demand) nitrates nitrites iron manganese sulphates chlorides ammonium ions coliform bacteria - cfu Escherichia coli - cfu

## Slide 51
Unit (cfu/ml) limit
Intestinal enterococci
Coliform bacteria
Abioseston – org.+anorg.
particles
Number of organisms
Number of live organisms
Number of bacterial colonies (cfu)
at 22 o C
Number of bacterial colonies (cfu)
at 36oC
Vyhláška č. 83/2014 Sb.
Decree amending Decree No. 252/2004 Coll. Laying down hygiene requirements for drinking
and hot water and frequency and scope of drinking water control, as amended

## Slide 53
Example of a real protocol of water analysis

## Slide 55
Waste water
• Ancient Greece, Rome - the first sewer system, sewage drawn into rivers, or soak up.
• The Middle Ages - a great decline. • 18th century - construction of sewerage systems (drainage of army objects, later church and public buildings). • The end of the 19th century - sewer systems in most European cities. • 1865 - England - The creation of the "Royal Commission on River Pollution". • 1860 - First sewage WWTP - sewage farms. • 1880 - First sedimentary treatment plant. • 1900 - First intermittent biofilters. • 1910 - USA - experimental aeration of sewage • 1912 - England - Invention of the activation system

## Slide 56
• The protection of watercourses is primarily aimed at ensuring the required quality of effluent on runoff from WWTP. • Typical symptoms of waste water content in streams (odor, sludge, oxygen deficiency) caused by organic substances - in European proportions are virtually eliminated. • New cleaning issues: nitrogen, phosphorus, microfibers, pharmaceuticals. • Act No. 254/2001 Coll. on water - defines the concept of wastewater. • Act No. 274/2001 Coll. about public water supply systems and sewers as amended by
Act No. 76/2006 Coll. • Government Decree No. 61/2003 Coll. in the act 229/2007 Coll. A 23/2011 Coll. about
indicators and values of permissible surface water pollution, discharging requirements of sewage into surface water and sewage waters and about sensitive areas. • Act No. 185/2001 Coll. on waste - determines the treatment of waste from WWTPs
(sludge, shrubs, sand, soil from root fields, etc.)
Waste water

## Slide 57
Basic methods of wastewater treatment
• Mechanical • Physical-chemical • Biological • In practice, combination of the three procedures are used Sewage sorting
• Wastewater sewage • Waste water industrial • Wastewater rainfall (rainfall)
Waste water

## Slide 58
Waste water – WWTP scheme
Inflow
Ramp Sand trap
Settling tank Activation tank Secondary settling tank
Primary sludge Activated sludge
Outflow

## Slide 59
The waste water first goes to the gravel trap. The next level is ramp - removal of rough floating dirt (protection of other parts of the
treatment plant) - landfill, composting, combustion. A sand trap is next The last device for mechanical cleaning - the settling tank is a gravitational separation of suspended substances Primary sludge is formed - processed in the sludge management.
Waste water – WWTP

## Slide 60
BIOLOGICAL CLEANING (SECONDARY)
- activation line - secondary settling tank Activation tank - microorganisms in aerobic conditions decompose organics
biological oxidation of organic substrate, ammoniacal nitrogen, nitrification,
denitrification, biological decomposition of phosphorus, or its chemical precipitation. Secondary settling tank separation of activated sludge from purified water
Waste water – WWTP

## Slide 61
Sludge processing technology 1. Concentration 2. Stabilization 3. Drainage 4. Hygiene
• Stabilization of sludge - reduction of degradable organic matter (microbes in aerobic
or anaerobic conditions) and the destruction of pathogenic microorganisms
• Total decomposition and other sludge stabilization methods: - drying at low temperatures, - drying at high temperatures (105 ° C), - total decomposition with oxygen at 160 ° C, - combustion of sludge with other fuels in power stations or cement plants
Waste water – WWTP

## Slide 62
Sludge hygiene
- heat treatment of sludge at high temperatures - pasteurization of sludge - chemical treatment of sludge - liming - anaerobic thermophilic processing methods - composting - special methods: ionizing radiation, ozone, decomposition
Waste water – WWTP

## Slide 63
Category I - sludges can generally be applied to land used in agriculture Category II - sludge can be applied to agricultural land intended for the cultivation of technical crops, and land that will not grow for at least 3 years after the use of sewage sludge field vegetables and intensely fruit-bearing fruit planting
Waste water – WWTP
Sludge category Acceptible microbial count per gram of dry matter of sludge

## Slide 64
Limit values of concentrations of selected hazardous substances and elements in slurries for their use on agricultural land
Waste water – WWTP
In dry matter

## Slide 65
Waste and health
Waste is every movable thing the person discards, or has the intention or duty to discard it, and it belongs into one of the categories of waste listed in the catalog waste
(Act No. 185/2001 Coll.) Types by production: Communal-mixed - occurring in the activity of natural persons, dangerous drugs, cans from paints and thinners, etc. - it is the largest amount of all wastes Agricultural - wastes from plant and livestock production (urine, manure), agrochemicals (fertilizers) Industrial - from industrial activities

## Slide 66
According to the composition:
Inert - not subject to biodegradation - does not decompose/rot Construction waste, glass, has no dangerous properties Biological - is capable of aerobic and anaerobic digestion. Food, paper, green mater Toxic, radioactive - nuclear waste, old batteries, drugs, oils Hospital - parts of human bodies, infectious waste, needles, plasma, cytostatics
Waste and health

## Slide 67
Waste and health
Categories of waste from medical facilities Specific waste Sharp objects Pathological and biologically contaminated waste Discarded chemicals, drugs Non-specific waste Other wastes not requiring protection against the spread of infections

## Slide 68
Exposure:
Dust Contact Mediated (contamination of water, soil, food chains, insects, rodents
Waste and health

## Slide 69
Effects: Irritation, toxic smoke
Parasitic infections - helminthoses, amoebae, cercariae (maggot stage, the evolutionary stage of the motolic, leaving the guts and looking for the host - the human)
Zoonoses
Hepatitis, AIDS
Poisoning
Waste and health

## Slide 70
Action:
Minimizing quantity (recycling, use of one – off packaging)
Selection of suitable sites and landfill security
Separation of toxic, infectious, radioactive waste
Education of the population
Waste and health

## Slide 71
Waste disposal:
Landfills Composting Combustion Chemical destruction Storage Feeding to animals Recycling of sorted waste (glass, paper, plastics, metals)
Waste and health

## Slide 72
Preparation of landfills – must be waterproof

## Slide 73
But also drained – any water from waste and rainfall – otherwise there
would be a lake soon

## Slide 74
When the landfills is full

## Slide 75
Once the landfills is covered we must remove gases – methane etc – burn it