## Slide 1: Total hip replacement
MUDr. Jan Emmer, I. Ortopedická klinika FNUSA v BRně

## Slide 2: History
1891 Profesor Themistocles Glück (Germany)
  Femoral head replacement made of ivory (post TBC)
Further attempts with interposition arthroplasy (fascia lata, xenogenic tissues)
1925 Marius Smith-Petersen – glass, stainless steel
1953 George McKee
  Co-Cr acetabular component + cemented Thompson´s stem (stainless steel)

## Slide 3: History
1960´ Sir John Charnley – Low friction artroplasty
  Bone (dental) cement, polyethylen, alloy
  1. st modern functional THR

## Slide 4: History
  1964-1965 1966
  Setzholzprothese Banana – shaped
  1977 Geradeschaft

## Slide 5: History
Prof. MUDR. Oldřich Čech, DrSc. (1928-2020)
Stems Poldi – Čech 1969 – present days

## Slide 6: Anatomy
Enarthrosis – simple joint
Ball – socket, limited ROM
Acetabulum - hemisphere
Femoral head
  2/3 surface of ball
  Diameter aprox 2,5 cm

## Slide 7: Anatomy
Ligaments:
  Lig iliofemorale
  Lig pubofemorale
  Lig. ischiofemorale
  Zona orbicularis
  Lig. Capitis femoris
  Joint capsule

## Slide 8: Anatomy
Muscles of hip joint – flexors
  M. iliopsoas (flexon + aditional hip adduction; n. femoralis, plexus lumbalis)
Muscles of hip joint – extenzors, abductors
  M. gluteus maximus (extension + ER + abduction; n. gluteus inferior)
  M. gluteus medius (abduction, IR; n. gluteus superior)
  M. gluteus minimus (IR; n. gluteus superior)
  M. tensor fasciae latae (aditional flexor, abductor, IR; knee extension at standing position; n. gluteus superior)

## Slide 9: Anatomy
Muscles of hip joint - pelvitrochanteric muscles
  M. piriformis (abduction in flexion, ER ; plexus sacralis)
  M. gemellus superior (ER, plexus sacralis)
  M. gemellus inferior (ER, plexus sacralis)
  M. obturatorius internus (ER, plexus sacralis)
  M. quadratus femoris (ER, plexus sacralis)

## Slide 10: THR indications
Painfull hip joint condition
Poor effect of conservative therapy
Life comfort deteriorated
No salvage surgeries indicated

## Slide 11: THR indications
OA primary
OA secundary
Psoriatic arthropathy
Aseptic femoral head necrosis
Rheumatoid arthropathy
Tumors
Intracapsular femoral neck fracture, no indication for OS or conservative therapy (vital indication!)

## Slide 12: THR contraindications
Poor general condition, poor physical status (ASA IV)
Persistent infection
Severe comorbidity with poor prognosis
Extreme obesity
Strong malcompliance

## Slide 13: THR fixation options
Cemented
  Both components fixed with bony cement
  Older patients > 70 y.o.
  Poor bone quality - osteoporosis
  Inferior implant survival
  The cheepest option

## Slide 14: THR fixation options
Hybrid
  One component fixed with bone cement (femoral)
  65-70 y.o.
  Compromise bone quality
  Better implant survival
  Price?

## Slide 15: THR fixation options
Cementless
  Both components fixed with no bone cement
  <65 y.o.
  Good bone quality
  Contraindication for bone cement (alergy, right ventricle function)
  Best implant survival
  The most exepensive

## Slide 16: Hip replacement range
Cervicocapital replacement
  Not frequently nowdays, fracture if patient polymorbid
  Acetabular abrasion
  Inferior results
Total
Methafyseal conservative stems - why?

## Slide 17: materials
Polyethylen
  Longest used material for cup
  Viscoelastic
  Plastic deformation (cold flow)
  Higer wear rate
  Oxidative degradation

## Slide 18: Materials
Polyethylen
  UHLMWH - Ultra high molecular weight polyethylen
  HXLPE – cross - linked
  Tocoperol doped PE (vit E)
  Aim:
    Wear reduction
    Oxidative degradation reduction
    Keeping elasticity modulus

## Slide 19: Materials
Femoral component - requirements
  Biocompatibility
  Mechanical strenght
  Osteointegration (cementless implants)
  Antialergic implants (if metal allergy presented)
  Future? Biofilm resistance

## Slide 20: Materials
Cementless implants requirements – bone adjacent surface
  Trabecular titan
  Trabecular tantal
  Hydroxyapatite surface

## Slide 21: Materials – bone cement
Poly methyl methacrylate (metylesther metacrylic acid)
Powder polymer, liquid monomer
Exotermic response
Stabilisation of the implant in 10 minutes
Cytotoxic effect
Protein coagulation (termical + chemical)
Microembolisation

## Slide 22: Materials – ceramic
Pure aluminium oxide - AL2O3 - corundum
ZrO2 – zirkonium oxide
Extremely smooth surface, minimal friction ratio
An order of magnitude smaller wear rate comapare to metal
Fragile
Expensive

## Slide 23: Materials – ceramic
Biolox forte
  Pure AL2O3 (yellow)
Biolox delta
  Stronger
  Lower grain size – even more smooth
  More homogenic
  Pink
  AL2O3
  ZrO2
  Zirconium oxides stabilized by Ytrium

## Slide 24: Materials – Oxinium
Zirconium oxides
Combines properties of alloy and ceramic
2x harder than ceramic
Abrasion and scratch resistant
Fracture resistance
Trace amount of Ni only (hypoallergenic)
20% lighter than CoCr

## Slide 25: Acetabular comoponent cemented
Cement + PE, monobloc
RTG marker (metal wire around)
Structured surface for cement retention

## Slide 26: Acetabular comoponent cementless
Metalback + inlay (ev. monobloc)
Material of inlay variable
Offset optional
Double cup – lower displacemet risk
Osteoinductive surface

## Slide 27: Acetabular comoponent cementless
Press fit Threaded Expansion

## Slide 28: Acetabular comoponent cementless
Press fit Threaded Expansion

## Slide 29: Acetabular comoponent cementless
Press fit
  Golden standard, most cases
Theraded
  Best primary fixation
  Postdisplastic arthritis, shellow acetabulum, low / defect ac. wall support
  Partial acetabular defects
Expasion
  Obsolent, worse results
  PE/bone contact
  Failure – leafs breaking off

## Slide 30: Femoral component
Smooth polished surface
  cement
Porous osteoinductive surface
  Non cement
Different designs
  Straight
  Anatomic
  Banana - shaped
  Metaphyseal conservative
Revision, Tumorous, total femur…

## Slide 31: femoral comoponent
Colodiafyzar angle (CCD)
  Pysiolgical 126°
  Always respect anatomy!
  115-140° range
  High offset option

## Slide 32: femoral comoponent
Cone:
  12/14mm
  Always use compatible head/stem, never mix producers!
  Structured surface for head retention
  If ceramic head replaced, always use revision!

## Slide 33: femoral comoponent cemented
Highly polished surface
Dirct x anatomical shape
Equally cemet layer around the stem!
Never direct contact stem x bone
Centraliser
Obturator

## Slide 34: femoral comoponent cementless
Osteoinductive surface
Metafyzar x diafyzar anchoring

## Slide 35: Head
Alloy x ceramic x oxinium
28, 32, 36 mm
„head lenght“ – depth of bore for cone
Bigger head diameter incerases ROM and stability

## Slide 36: Articulation surfaces matching
PE/alloy head
PE/ceramic head
Ceramic inlay/ceramic head
Alloy/alloy head
Oxinium

## Slide 37: Surgical techniques
Standardized, routine
Standardized approaches
  Anterolateral (Watson Jones)
  Dorzal (Moore, Langenback)
  Anterior (Smith – Petersen)
  Lateral (Harding)
MIS

## Slide 38: Surgical techniques
Operation field overview
Gentle soft tissue treatment
Lavage – PAO development prevention
Standardized approaches – minimal nerve and vessels leasions risk
Correct compoent alignment – impotrant for ROM and stability
Reliable suture!

## Slide 39: Preoperative examination
ASA risk ratio
Infection focus exclusion (neg FW, CRP), stomatological examination incl. OPG
CAVE!
  Warfarin
  NOAK
  NSAID
  PAD

## Slide 40: periprosthetic joint infection (PJI) prevention
Preop. Examination!
ATB perioperatively – Cefazolin i.v. 1 dose before + 3 doses post op.
Drainage EX in 24h
If urinary catheter present - ATB
Strict régime at op. theater
Wound care till healing
Lege artis diagnostic and therapy protocol of eventual PJI

## Slide 41: Post op. management
ICU (post op ward) one day if no complication
Hospitalization at orthopedic ward for 5 days
Verticalization fhe first post op. day
Complex rehabilitation protocol, rehabitalitation nurse obligatory
6. day – transfer to rehabilitation ward
Spa – in CZ covered by public health insurance in 3 post op. months
DVT prevention – 6 weeks
Displacment prevention – no adduction, no deep flection, no axial extremity traction!
Trends: Shortening inpation period (risc of nosocomial infection, economic aspects)
Fast track physiotherapy
Outpatient surgery?

## Slide 42: Follow up
Standardized
First check up by orthopedical surgeon in 6 weeks (X ray included)
Second in 3 months, then 6 month
Further each 2 years (X ray included) if no problem present
EDUCATION, EDUCATION, EDUCATION!
  Activity, limitation and régime with TKR
  PJI prevention
  Urgent check – up if suspected PJI

## Slide 43: Complications
Peri and early pos op. morbidity and mortality
  Nervous and vascular injury
  Blood loss
  Perioperative fracture
  Hip displacement (luxation)
  Pulmonary embolism
  IM
  General decompensation
  Development of delirium

## Slide 44: Complications
THR luxation (displacement)
  Shortening and (extra)rotation of extremity, pain, no active hip flexion
  No active walking and no weight - bearing
  Downfall
  Risky movement (adduction in hip, deep felxion)
  Wrong mainpulation with pac. (Axial leg traction)
  Primary instable prosthesis (incorrect implantation)
  Therapy:
    Close hip redduction attempt. Hip orthosis with reduced ROM obligatory
    If close reduction impossible, revision, identification of cause, solution
    Different („longer“) head, stabilisation elements
    If malposition of components present, replantation

## Slide 45: Complications
Peri and early pos op. morbidity and mortality
  Nervous and vascular injury
  Blood loss
  Perioperative fracture
  Hip displacement (luxation)
  Pulmonary embolism
  IM
  General decompensation
  Development of delirium

## Slide 46: Complications
THR luxation (displacement)
  Shortening and (extra)rotation of extremity, pain, no active hip flexion
  No active walking and no weight - bearing
  Downfall
  Risky movement (adduction in hip, deep felxion)
  Wrong mainpulation with pac. (Axial leg traction)
  Primary instable prosthesis (incorrect implantation)
  Therapy:
    Close hip redduction attempt. Hip orthosis with reduced ROM obligatory
    If close reduction impossible, revision, identification of cause, solution
    Different („longer“) head, stabilisation elements
    If malposition of components present, replantation

## Slide 47: Complications
Peri and early pos op. morbidity and mortality
  Nervous and vascular injury
  Blood loss
  Perioperative fracture
  Hip displacement (luxation)
  Pulmonary embolism
  IM
  General decompensation
  Development of delirium

## Slide 48: Complications
THR luxation (displacement)
  Shortening and (extra)rotation of extremity, pain, no active hip flexion
  No active walking and no weight - bearing
  Downfall
  Risky movement (adduction in hip, deep felxion)
  Wrong mainpulation with pac. (Axial leg traction)
  Primary instable prosthesis (incorrect implantation)
  Therapy:
    Close hip redduction attempt. Hip orthosis with reduced ROM obligatory
    If close reduction impossible, revision, identification of cause, solution
    Different („longer“) head, stabilisation elements
    If malposition of components present, replantation

## Slide 49: Complications
Periprosthetic infeciton (PJI) – 1-2% primo, 5-10% revision
  Early – up to 2 weeks after surgery
  Late hematogenic
  Diagnostic
    General symptomas of infection
    Local condition, persistant pain
    Punction + aspiration, cultivation + PCR
    Synovasure (α defensine) test perioperatively
    Implant sonication + cultivation
    Fistula with purulent secretion
    Radiolucent periprosthehic lines around implant on X ray (chronic PJI)

## Slide 50: complications - Periprosthetic infection (PJI)
Therapy
  Up to 2 weeks from manifestation - DIAR (debridement, ATB, implant retention)
  Uprard of 2 weeks – revision, debridement, replantation
    One stage – dubious outcome
    Two stage – cemented ATB spacer, after healing ínfection revision and new implant possible
    ATB supression of chronic infection optional (old patients with no perspective to surgery)
ATB therapy
  Cultivation (punciton + aspiration, perioperativly samples, sonication of implant)
  ATB i.v. 2 weeks minimum
  6 weeks p.o.

## Slide 51: complications - Periprosthetic infection (PJI)
ATB spacers
  Custom – made
  Ready - made

## Slide 52: complications - Periprosthetic infection (PJI)
Ultimum refugium – sec. Girdlestone

## Slide 53: aSeptic loosening
Most frequent THR revision reason
Macrophage-induced inflammatory response resulting in bone loss and implant loosening
PE particle inducted granuloma

## Slide 54: aSeptic loosening - therapy

## Slide 55: aSeptic loosening - therapy
Revision, replantation
Revision systems, augments, spongioplasty (alografts)…
Double ATB combination – higer infection risk
Higer complication rate
Inferior outcome
Lower ROM
Longer no full weight bearing period (3M)
Higer mortality
Higer displacement risk ratio

## Slide 56: aSeptic loosening - therapy

## Slide 57: aSeptic loosening - therapy
Revision, replantation
Revision systems, augments, spongioplasty (alografts)…
Double ATB combination – higer infection risk
Higer complication rate
Inferior outcome
Lower ROM
Longer no full weight bearing period (3M)
Higer mortality
Higer displacement risk ratio

## Slide 58: aSeptic loosening - therapy
Revision stems:
Modular x monobloc
Wide range of option
Cemented x cement less

## Slide 59: aSeptic loosening - therapy
Revision acetabular component systems
Spongioplasty x augments
Trabecular metal, titan tantal
Cemented x cement less
Pelvis discontinuity often

## Slide 60: Acetabular defects
Classification - Paprosky

## Slide 61: Acetabular defects
Solution - mechanic
  Bone cement

## Slide 62: Acetabular defects
Solution - mechanic
  Augmentation

## Slide 63: Acetabular defects
Solution - biologic
  Impact grafting

## Slide 64: Acetabular defects
Solution - biologic
  Solid allograft

## Slide 65: Acetabular defects
Ring and cage reconstruction

## Slide 66: Acetabular defects
Ring and cage reconstruction

## Slide 67: Periprosthetic fracture
Relatively frequent complication
Femur in the most cases, acetabulum rarely
Starší pacienti, v horším klinickém stavu
Older patients, worse general condition
Osteoporosis, poor implant retention
High mortality and morbidity rate
High compliction rate
Demanding surgeries (experienced surgeon)

## Slide 68: Periprosthetic femoral fracture - classification
Vancouver
  Frequently used
  Guide to therapy

## Slide 69: Periprosthetic femoral fracture - therapy
Conservative
  No/minimal displacecement
  Implant retention
  Poor patient genetal condition
Surgiclal
  Revision stem + cerclage (cables, wires)
  Ostheosynthesis (LCP x cables/wires)

## Slide 70: Periprosthetic femoral fracture - therapy
OS (LCP, control cable )

## Slide 71
Thank you for yor attention