## Slide 1: (VII.) Electrocardiography
Physiology

## Slide 2: Electrocardiography
Definition: the process of recording the electrical activity of the heart
Keywords
Specialized excitatory and conductive system of the heart
equipment for ECG recording
limb and chest leads
unipolar and bipolar leads
heart vector, electrical axis of the heart

## Slide 3: Specialized excitatory and conductive system of the heart
Purkyne fibers
Sinoatrial node (SA)
internodal pathways
Atrioventricular node (AV)
Bundle of His
Bundle branch
SA node
atrial myocard
AV node
bundle of His
bundle branch
Purkyne fibers
ventricular myocard

## Slide 4: Electric dipole
Electrode: records electrical potential (Φ)
Elektric lead: connection of two electrodes
Recordes voltage between electrodes
Voltage: difference between el. potentials (V= Φ1- Φ2)
electrode
lead
Φ1
Φ2

## Slide 5: Einthoven´s triangle (standard, limb, bipolar leads)
I
II
III
R
L
F
Bipolar leads: both electrodes are active (variable potential en electrodes)

## Slide 6: Augmented leads (Goldberger´s, limb, unipolar leads)
aVF
aVL
avR
R
L
F
Unipolar leads:
one electrode is active (variable el. potential) and the second one is indifferent (constant el. potential)
Active electrode is always positive

## Slide 7: Chest leads
1
2
3
4
5
6
Wilson´s cental teminal
R
R
R
Chest electrode: connection of chest electrode and Wilson´s central terminal
Unipolar leads: chest electrodes are active (positive) and Wilson´s central terminal is indifferent (el. potential 0 mV, electrically centre of the heart)
chest electrode

## Slide 8: Leads acording to Cabrera
I
aVF
II
III
aVR
aVL
–
+
–
+
+
+
+
+
–
–
–
–
120°
90°
60°
30°
0°
-30°
+
-
+
R
L
F
aVR
-
+
-
+
aVL
aVF
–
–
+
+
–
I
III
II

## Slide 9: ECG description
Bazett´s formula:
QT depends onRR interval – correction of QT on RR
name | Norm
P wave | 80 ms
Interval PQ (PR) | 120-200 ms
Segment PQ (PR) | 50-120 ms
Q | -
QRS | 80-100ms
R | -
S | -
segment ST | 80-120 ms
Interval QT | >= 420ms
wave T | 160 ms
P
R
T
Q
S
P wave
PQ interval
PQ segment
QRS complex
ST segment
T wave
QT interval

## Slide 10: Electrical axis of heart
1. ORS of I,II and III lead
2. Sumation of QRS complex
I | II | III
Q = -1 | Q = - 1 | Q = 0
R = 5 | R = 6 | R = 4
S = -1 | S = 0 | S = 0
3 | 5 | 4
+
R
L
F
–
–
+
+
–
I
III
II
3
5
3. Drawing in triangle
Physiological interval: -30° - 110°
Average deviation of QRS complex in each lead

## Slide 11: Diagnostic use of ECG
Arrhytmia: irregular heartbeat
Atrial fibrillation
(absence of P, „jagged“ isolinia, irregular RR, HR 80 – 180 bpm)
Ventricular fibrillation
(heart cannot pump, brain damage after 3 – 5 min)
https://upload.wikimedia.org/wikipedia/commons/thumb/6/64/Afib_ecg.jpg/400px-Afib_ecg.jpg http://www.qureshiuniversity.com/Ventricular%20Fibrillation.gif
https://ekg.academy/ekgtracings/313.gif
Fibrillation: is the rapid, irregular, and unsynchronized activity of cardiac muscle fibers
fibrillation
normal
AV block I. degree
Atrioventricular block: conduction between the atria and ventricles of the heart is impaired
AV block II. degree
AV block III. degree
P
P
P
P
P
P

## Slide 12: Diagnostic use of ECG
Myocardial ischemia, heart-attack
A
B (ST elevation)
hyperkalaemia

## Slide 13
24-hour monitoring of ECG (Holter)
Diagnostic use of ECG