## Slide 1: XVII. Pneumography XX. Pneumotachography
Physiology I – practice
Autumn, weeks 10-12

## Slide 2: Pneumography
= a method for registration of respiratory movements
Respiratory muscles
  Main inspiratory muscles: diaphragm and external intercostal muscles
  Accessory inspiratory muscles: sternocleidomastoid musculus and a group of scalene muscles
  Expiratory muscles: internal intercostal muscles and anterior abdominal wall muscles
Inspiration – active process (contraction of respiratory muscles)
Expiration – a passive process at rest (elasticity of the lungs pulls the chest wall back to the expiratory position), and forced exhalation is an active process (use of expiratory muscles)

## Slide 3: Pneumography
inspiration
expiration

## Slide 4: Chemical regulation of ventilation
Ventilation = tidal volume * respiratory rate
  The volume of air ventilated over time (l/min)
  Respiratory rate in pneumography – determined by the duration of the whole respiratory cycle (breathing interval, BI), duration of inspiration (Ti) and expiration (Te)
  Depth of breathing in pneumography – amplitude of breathing movements (Amp)
Chemical control of ventilation leads to a change in depth and frequency of breathing based on chemoreceptor information
Chemoreceptors
  Central – cells in the medulla oblongata near the respiratory centre
  Peripheral – carotid and aortic
Amp
Ti
Te
BI

## Slide 5: Central chemoreceptors
Located near the respiratory centre in the medulla oblongata
CO2 passes the blood-brain barrier into the cerebrospinal and intercellular fluids of the brain
CO2 + H2O → CHO3- + H+
Increased concentration of H+ in cerebrospinal fluid stimulates chemoreceptors → increased ventilation

## Slide 6: Peripheral chemoreceptors
They contain two types of cells
  Type I: located beside nerve fibres
  Type II: glia (each one surrounds 4-6 type I cells)
Registration of pO2 levels dissolved in the blood plasma over time
  Stimulation by a decrease in pO2 or by a decrease in blood flow
Peripheral receptors also register pCO2 and pH
Type II cell
Type I cell (glomus)
Afferent fibres of n. IX

## Slide 7: Dead space
Air volume in the conductive airway area where no gas exchange with blood occurs
  Anatomical DS: volume of the respiratory system outside the alveoli (150-200 mL)
  Functional (physiological) DS: the volume of air that does not participate in gas exchange with the blood – includes non-perfused alveoli
In healthy individuals, both dead spaces are the same

## Slide 8: Partial pressures of gases (mmHg)
in different parts of the respiratory and circulatory systems

## Slide 9: Pressures in lungs
nádech výdech
Visceral pleura
Parietal pleura
Pleural cavity – between parietal and visceral pleura
Pleural
fluid
Intraalveolar (pulmonary) pressure
Atmospheric pressure
(now 0)
Intrapleural pressure (always negative)
The volume of inhaled air
http://worldartsme.com/images/happy-lungs-clipart-1.jpg

## Slide 10: Lung compliance C
  the slope of the curve on the graph
The value of C is the highest at rest
The value of C depends on
  Own tissue elasticity (ensured by elastin and collagen fibres)
  Surface tension forces (surface tension forces in the alveoli: liquid-air interface, surfactant)
3
2
1
0
-1
80 120 160
Forced inspiration curve
Relaxation pressure curve
Forced expiration curve
Position at rest
(relaxation volume)
Vital capacity
-80 -40 0 40
Pulmonary pressure (mmHg)
(0 = atmospheric pressure)
Volume change from relaxation volume (L)

## Slide 11: Statistical evaluation – in general
Mann-Whitney test
  Nonparametric sequential test, it compares samples A and B
Null hypothesis H0: sample A do not differ from sample B
Alternative hypothesis HA: sample A is bigger or smaller than sample B
Statistical significance of α (usually α = 0.05 or 0.01)
  The probability of error, in other words, that we reject H0 based on the selection, but in reality H0 is true
Test results:
  The test is not significant = confirmation of H0: we did not confirm the difference between A and B
  The test is significant with significance α = rejection of H0: we confirmed that there is a difference between A and B
 |  | Reality | 
 |  | H0 | HA
Results | H0 | OK | β
 | HA | α | OK

## Slide 12: Statistical evaluation – an example
Sample A: Amp at rest, sample B: Amp after exercise
Null hypothesis H0: Amp at rest will be the same as Amp after the exercise
Alternative hypothesis HA: Amp at rest is bigger or lower than Amp after exercise
We compare T1 ́-T1 with the table values for α while the number of elements n = 6. Possible results:
  T1 ́-T1 < 13 → we do not reject H0 at the significance level of α = 0.01, i.e. we have not shown that Amp at rest differed from Amp after exercise
  T1 ́-T1 > 13 → we reject H0 at the significance level of α = 0.05, i.e. we have shown that Amp at rest differs from Amp after exercise (logically it should be higher after exercise)
  T1 ́-T1 > 16 → we reject H0 at the significance level of α = 0.01, i.e. we have shown that Amp at rest differs from Amp after exercise (logically it should be higher after exercise)
Amp
Ti
Te
BI

## Slide 13: Pneumotachography

## Slide 14: Pneumotachography
Pneumotachography is a method enabling the estimation of airway resistance. It measures the pressure difference between two ends of a tube through which the examined person breathes.
An increased value of airway resistance indicates obstruction of the airways.

## Slide 15: Poiseuille-Hagen law
Volume flow () in rigid tube equals directly to the pressure gradient between the beginning and end of the tube () and to the fourth power of its radius (), and indirectly to its length () and viscosity of the fluid ()
is tube resistance against gas flow
  The pressure required to pass a given volume of liquid/gas through the tube
  Valid only in laminar flow

## Slide 16: Airway resistance
Airway resistence (Rd) results from inner friction between flowing gas and the airway wall.
A small change in the radius of the airways (rd) causes a substantially bigger change in the airway resistance to airflow (Rd).
  Narrowing (obstruction) of the airways occurs when the chest is compressed, the mucous membrane is swollen, vocal cords are swollen, smooth muscles of the airways are constricted when a foreign body is inhaled, asthma attack or other allergic reaction
  Bronchioles are the main contributors to resistance: a large proportion of smooth muscle and no cartilaginous reinforcement, they contain receptors for various agents (histamine – bronchioloconstriction, adrenaline – bronchiolodilatation)

## Slide 17: Principle of pneumotachography
The airflow in the pneumotachograph is the same as the airflow in the airways:
Substitution:
Pneumotachograph resistence:
and are measured
(Note: The values are in mV, not kPa, which does not matter because they are in ratio. Do not write minus for expiratory values.)
pneumotachograph tube
valve
lung
trachea

## Slide 18
Calculation of
  During inspiration with a normal mouthpiece
  During expiration with the normal mouthpiece
  During inspiration with a narrowed mouthpiece
  During expiration with the narrowed mouthpiece
  Physiological values:
  A narrowed mouthpiece increases several times
0
U [V]
Pp
Palv
t [s]
U [V]
Pneumotachographic curve
Pneumographic curve
M
marker
inspirium
expirium
Valve closing at the start of inspirium/expirium
Pp
Palv