## Slide 1
Petr Beňovský
SOLVENT SELECTION

## Slide 2
IMPORTANCE OF SOLVENTS
Reaction medium (transport, combine, separate)
Dissolution
(In)solubility
Kinetics
Health
Safety
Environmental aspects
Course of the reaction
Cost (purchase, recycle, dispose)

## Slide 3
PERSPECTIVE ON SOLVENT SELECTION
ASPECT | COMMENT
Safety | Avoid solvents that are toxic or highly flammable
Promote high-yielding reactions | Compatible with desired chemistry; Can isolate product in good yield?
Convenient (minimize processing operations) | Isolate product from reaction solvent? Operate at high concentrations?
Water miscibility | Azeotroping ability Control amount of water
Cost of bulk and recoverability | More important at end of development cycle
Environmental | Ethics, and cost of recovery and non-compliance
Long-term availability | 
Acceptability for human use | 
Water as solvent | But, recovery of product from aqueous layer can be costly, plus cost of disposal
Neat reactions | 
Ionic liquids | 

## Slide 4
SOLVENT SELECTION GUIDES
Almost every company created specific solvent guide
SmithKline Beecham – Curzons, A.D. et al Clean Products and Processes 1, 82 (1999)

## Slide 5
SOLVENT SELECTION GUIDES
Sanofi – Prat D. et al Org.Process Res. Dev. 17, 1517 (2013)

## Slide 6
SOLVENT SELECTION GUIDES
GlaxoSmithKline – Henderson, R.K. et al Green Chemistry 13, 854 (2011)

## Slide 7
SOLVENT CONSIDERATIONS
Watch out hydrocarbon solvents with even number of carbons (toxicity, electrostatic buildup);
Classification of solvents – ICH Harmonised Guideline Q3C – Impurities: Guideline for Residual Solvents
Class 1 – solvents to be avoided (known human carcinogens, strongly suspected human carcinogens, and/or environmental hazards, e.g. carbon tetrachloride (concentration limit 4 ppm), 1,2-dichloroethane (5 ppm), 1,1,1-trichloroethane (1500 ppm), benzene (2 ppm))
Class 2 – solvents to be limited (non-genotoxic animal carcinogens, agents of irreversible toxicity, e.g. acetonitrile (410 ppm), chlorobenzene (360 ppm), chloroform (60 ppm), N,N-dimethylformamide (880 ppm), hexane (290 ppm), methanol (3000 ppm), N-methylpyrrolidone (530 ppm), toluene (890 ppm))
Class 3 – solvents with low toxic potential (permissible daily exposure 50 mg or more per day, e.g. acetic acid, acetone, ethyl acetate, heptane, 2-propanol, triethylamine)
Solvents for which no adequate toxicological data was found – a manufacturer is asked to supply justification for residual levels of these solvents (e.g. diisopropyl ether, petroleum ether, trifluoroacetic acid)

## Slide 8
SOLVENT CONSIDERATIONS
The best reaction solvent is the one that crystallizes the product directly from the reaction
Novartis – the Dimroth rearrangement – temperature and solubility turned out to be the most important – the product simply precipitated from the reaction mixture
Fischer, R.W. Org.Process Res. Dev.5, 581 (2001)

## Slide 9
SOLVENT CONSIDERATIONS
Homogeneous vs. Heterogeneous
Reactions using gases
Insolubility is sometimes advantageous (the Schotten-Baumann reaction, the Finkelstein reaction)
Menshutkin (1890)
The reaction rate of the reaction rate of triethylamine with alkyl halides providing quaternary ammonium salts strongly depends on a solvent (hexane 1, acetone 338, benzyl alcohol 739)
Solvents commonly used in academia are not often welcomed for industrial applications
Safety first !

## Slide 10
SOLVENT CONSIDERATIONS
Solvent | TWA (ppm)
Acetone | 500
EtOAc | 400
MeOH | 200
t-BuOH | 100
MTBE | 50
MeCN | 20
DMF | 10
Pyridine | 1
2-Methoxyethanol | 0.1
TWA = Time-Weighted Average shift for five days for nearly for safe exposure over an 8 h shift for five days for nearly all workers

## Slide 11
SOLVENT CONSIDERATIONS
Also, always consider physical-chemical properties like
Flash point
Flammability
Boiling point
Melting point
Electrostatic charge accumulation
Recycling potential
Cost of solvent
Environmental aspects
Cost of disposal
Polarity

## Slide 12
SOLVENT CONSIDERATIONS
Solvents rarely used in the pharmaceutical industry
Solvent | Disadvantage | Alternative replacement
Diethylether | Flammable | MTBE
Diisopropylether | Peroxide formation | MTBE
Hexane | Electrostatic charge Neurological toxicity | Heptanes, i-octane
Chloroform | Mutagenicity, environmental aspects, toxicity | Dichloromethane, 2-MeTHF, toluene
Benzene | Toxicity | Toluene
Ethylene glycol | Toxicity | 1,2-Propandiol
Acetonitrile | Animal teratogen, potential acetamide generation (genotoxic) | 2-propanol, acetone - water

## Slide 13
SOLVENT CONSIDERATIONS
Solvents preferred for process development (Pfizer)
Preferred | Usable | Undesirable
Water | Cyclohexane | Pentane
Acetone | Heptane | Hexanes
Ethanol | Toluene | Diisopropyl ether
2-Propanol | Methyl cyclohexane | Diethyl ether
Ethyl acetate | MTBE | Dichloroethane
i-Propyl acetate | i-Octane | Dichloromethane
Methanol | 2-MeTHF | Chloroform
Methyl ethyl ketone | DMSO | DMF
n-Butanol | AcOH | NMP
t-Butanol | Ethylene glycol | 1,4-Dioxane
 |  | Benzene
 |  | Carbon tetrachloride

## Slide 14
SOLVENT CONSIDERATIONS
Polarity of solvents
Reichardt, C. Pure Appl.Chem 76, 1903 (2004)
Reichardt, C. Solvents and Solvent Effects in Organic Chemistry,
3 rd Ed., Wiley-VCH, 2003
Hughes-Ingold rules ((de)stabilization of transition state)

## Slide 15
SOLVENT CONSIDERATIONS
Polarity of solvents
ETN parameter – the negative solvatochromism of the p  p* shifts of solutions of the betaine dye – more polar solvents stabilize the ground energy of the polar dye, producing thus greater shift in the position of p  p* absorption relative to that found for solutions of the dye in tetramethylsilane.
Colors of this dye in a solvent are indikative of the polarities of the solvent and solvent combination used to dissolve it.

## Slide 16
SOLVENT CONSIDERATIONS
Polarity of solvent
Solvent | Polarity ETN | Solubility in water (wt%) | Bp of water-solvent azeotrope | wt% of water removed by azeotrope | ICH solvent class
Water | 1.000 | - | None | None | 
EtOH | 0.654 |  | 78 C | 4.0 | 3
AcOH | 0.648 |  | 77 C | 97 | 3
DMF | 0.404 |  | None | None | 2
Acetone | 0.355 |  | None | None | 3
CH2Cl2 | 0.309 | 1.3 | 38 C | 1.5 | 2
Toluene | 0.099 | 0.06 | 84 C | 13.5 | 2
Et3N | 0.043 | 5.5 | 75 C | 10 | 3
Heptane(s) | 0.012 | 0.0004 | 79 C | 12.9 | 3
Cyclohexane | 0.006 | 0.006 | 69 C | 9 | 2

## Slide 17
SOLVENT CONSIDERATIONS
Polarity of solvent mixtures
Solvent | Polarity ETN | Solvent mixture | Calculated ETN
MeOH | 0.762 | EtOH:H2O = 6.9:3.1 | 0.762
EtOH | 0.654 | Acetone:H2O = 4.6:5.4 | 0.654
H2O:CH2Cl2 = 0.2:99.8 | 0.310 | H2O:MIBK = 1.9:98.1 | 0.283
H2O:CH2Cl2 = 0.2:99.8 | 0.310 | H2O:EtOAc = 3.3:96.7 | 0.253
H2O:CH2Cl2 = 0.2:99.8 | 0.310 | H2O:2-MeTHF = 5.3:94.7 | 0.223
i-PrOAc | 0.210 | Heptanes:EtOAc = 0.8:9.2 | 0.210
MeOH:H2O = 7:1 | 0.792 | EtOH:H2O = 5:3 | 0.783

## Slide 18
SOLVENT CONSIDERATIONS
Tendency of solvents to form azeotropes with water is considered advantageous (it is not practical and economical to dry solvents using drying agents on large scale);
Be careful – dependence on pressure (breaking the azeotrope)
Pressure (mm) | Bp (C) | Water in azeotrope (wt%)
760 | 70.4 | 8.5
250 | 42.6 | 6.3
25 | 1.9 | 3.6
Effect of reducing distillation pressure on EtOAc – water:

## Slide 19
IMPURITIES IN SOLVENTS
Absolute solvents are rather expensive, common solvents contains some amount of water, for certain operations they should be dried (azeotropic distillation, molecular sieves, use of an excess of cheap reagent);
Denatured solvents (ethanol)
Stabilizers (e.g. BHT in THF)
Tendency to form (hydrogen)peroxides (diisopropyl ether, butadiene, acetaldehyde, 1,4-dioxane, styrene, acrylonitrile, 2-butanol, benzyl alcohol, THF, MIBK, 2-propyl alcohol)

## Slide 20
IMPURITIES IN SOLVENTS
Degradation of solvents (ethyl acetate, DMF)
Side reactions (reesterifications, reaction with dichloromethane)
Avoid unwanted formation of esters of sulfonic acids (potentially mutagenic)

## Slide 21
SACRIFICIAL SOLVENTS
Harrington, P.J. et al Org. Process Res. Dev. 10, 1157 (2006)
About 50 eq. of 98% H2SO4 at 50 oC for 3 h followed by an aqueous quench provided ring sulfonation in the product;
5-6 eq. of 98% H2SO4 in toluene at 70 oC for 2 h – sulfonation of the product was significantly diminished.

## Slide 22
IONIC LIQUIDS
Ionic liquids are ionic compounds (salts) which are liquid below 100 oC. More commonly, ionic liquids have melting points below room temperature.

## Slide 23
SUPERCRITICAL CARBON DIOXIDE
Peach, J.; Eastoe, J. Beilstein J.Org.Chem. 10, 1878 (2014)
Beckman, E.J. J.Supercritical Fluids 28, 121 (2004)