## Slide 1
Sparky
NMR Assignment and Integration Software

## Slide 2
NMR software
Paid
  TopSpin
    Developed and mainly used for Bruker spectrometers controlling
    Many functions for processing, view and analysis of one- and multi-dimensional spectra
    Basically impossible analysis of multi-dimensional
  Mnova
    Processing, analysis and visualization of 1D and 2D spectra
    Support of different formats of spectra (Bruker, Jeol, Agilent...)
    Free trial version
  ACD/NMR processor
    see Mnova
    Free version for academic purposes with noncomplete functionalities

## Slide 3
NMR software
Freeware
  NMRPipe
    Multiplatform
    Processing and analysis of any spectra
    Based on UNIX systems → knowledge of UNIX environment is advantage
  SpinWorks
    For the Windows systems (emulator of Windows are needed for UNIX a Mac)
    Processing and analysis of 1D and 2D spectra
    User very unfriendly
  Sparky

## Slide 4
Sparky NMR Assignment and Integration Software
Originally developed on University of California, San Francisco, currently upgraded on University of Wisconsin–Madison (as NMRFAM-Sparky)
Multiplatform (Windows and Linux OS)
Free for download:
https://nmrfam.wisc.edu/nmrfam-sparky-distribution/
Written in Python language, open source, it is not developed anymore (last version is from the 2008)
Fast and undemanding for hardware
It can handle only multi-dimensional spectra (2D, 3D)

## Slide 5
Sparky - spectra
It can work with different formats of spectra, but to work with them is hard and slow (computationaly)
  Conversion of spectra into *.ucsf format
    Unix: bruk2ucsf 2rr name_of_the_spectrum.ucsf
    Windows: on the command line bruk2ucsf.exe 2rr name_of_the_spectrum.ucsf
  Spectrum does not contain any information about acquisition, temperature and so on → it is necessary to give the *.uscf file proper name (colchicine_noesy_800_D2O_25C.ucsf)
It has its own structure of folders
  Lists, Projects, Save
Sparky start
  Windows: /sparky/bin/sparky.bat
Notes: Prikaz konverzie: bruk2ucsf -> nazov programu, 2rr -> subor s 2D spektrom (obe dimenzie su realne)
5

## Slide 6
Sparky - start
Windows: batch file – sparky.bat

## Slide 7
main window
changing the mode of the left mouse button
by using F1-F12 keys
File open/save spectrum or project

## Slide 8
main window
changing the mode of the left mouse button
by using F1-F12 keys

## Slide 9
Sparky - control
Control by using
  Two letter shortcuts (case-sensitive)
  Menu in the main window
*.ucsf file - spectral data from a NMR exp
*.save file – Sparky format (plain text) contains all settings, assignment
*.proj file – Sparky project file contains link to multiple *save files
Open spectrum/project: fo/jo
Save spectrum/project as: fa/ja
Save spectrum/project: fs/js
Backup files*.bak are created automatically during the saving of the spectrum

## Slide 10
Notes: Takto to vyzera, ked sa otvori nove spektrum, neulozene
10

## Slide 11
zf – full view
Notes: zf – odzoomovanie na full view
11

## Slide 12
vC – contour scale
ct – contour levels
Notes: Uprava kontur vC alebo ct
12

## Slide 13
adjustment of the contours:
manually overwrite the values
change by dragging the left mouse button
Notes: 13

## Slide 14
Lowest positive
Levels = 1
Lowest positive
Levels = 3
Lowest positive
Levels = 2
adjustment of the contours:
1D
2D

## Slide 15
zooming the spectrum:
keyboard shortcut: zi (zoom in)
preset zoom in
alternatively use of middle mouse bottom
pointer mode– zoom: key F11
selected region is zoomed
by clicking and dragging of the mouse
Notes: 15

## Slide 16
PEAK PICKING:
pointer mode – find/add peak: key F8
one peak is added by one left click,
peaks in every local maximum/minimum are added by selecting the rectangle region
Notes: 16

## Slide 17
peak picking:
changing the size of ornaments (peaks, labels...): ot → sizes → change the size
as desirable (proper value 0.05) → apply
Notes: 17

## Slide 18
PEAK SELECTION
selection: pointer mode – select: key F1
one object is selected by clicking on it,
more object are selected by dragging the mouse (or Shift+click)
Notes: 18

## Slide 19
peak picking:
adding of central peak from the selected group of peaks – pg
(useful for multiplets in COSY spectra)
Notes: Pooznačovať všetky relevantné píky (krospíky len na jednej polovici a diagonálne píky dokopy 16ks)
19

## Slide 20
peak picking:
list of the peaks – lt
Notes: Pooznačovať všetky relevantné píky (krospíky len na jednej polovici a diagonálne píky dokopy 16ks)
20

## Slide 21
identification of the spin systems:
add vertical and horizontal line: key F3
add horizontal line: key F4
add vertical line: key F5
add a vector: key F7
F3
F5
F7
F4
Notes: 21

## Slide 22
identification of the spin systems:
changing the color of ornaments (lines, labels...): ot → color → select object/s→ choose the color → apply
Notes: 22

## Slide 23
identification of the spin systems:
COSY – correlation through bonds, isolated spin systems
expected number of signals:
Gly – 2: Hα, NH
Cys – 4: Hα, NH, Hβ‘, Hβ‘‘
Glu – 3: Hα, Hβ, Hγ
Notes: Priradiť nájdené spinové systémy k reziduám podľa odhadu počtu signálov
23

## Slide 24
Signal assignment:
select the peak: pointer mode – select: key F1 → shortcut at – assignment → fill in the name of the group (e.g. abbreviation of residuum/molecule) and the name of the atom (eg. NH) according to the resonance in w1 and w2 axis → type apply
Notes: 24

## Slide 25
Signal assignment:
the assignment with the closest resonance to the current selected resonance is highlighted when clicking on the name of the axis. (not necessarily correct one!!), double click on the highlighted line adds the name of the group and atom label to currently selected peak. Use unique naming, otherwise resonances will be averaged. Display position of resonance by vR command (view Resonances).
Notes: Dopriradzovať samostatne!!!
25

## Slide 26
signal assignment:
shortcut tb – assignment table
residues vs. atoms, statistical data can be shown as well
shortcut lt – list of the peaks already with assignments, or with other information
both can be exported as a plain text file
(→ Save)
Notes: 26

## Slide 27
working with more spectra:
view assigned (averaged) resonances on the edge of the spectra - vR
Notes: 27

## Slide 28
working with more spectra:
assign ROESY spectrum by using at:
Notes: Opíkovat ROESY a popriradzovať (ideálne pomocou at)
28

## Slide 29
working with more spectra:
synchronize views of spectra: shortcut yt – it allows simultaniously move synchronized axes of spectra when moving one of them,
click on the axes in spectra we want synchronize → Synchronize
Notes: 29