## Slide 1: What NMR can tell about proteins
This project received funding by the European Commission under the GA n° 2019-1-IT02-KA203-063391
innocore-project@unitn.it
www.innocore-project.eu
Core Technologies for Education and Innovation in Life Sciences
For Application to Protein Characterization
by
Radovan Fiala, Karel Kubicek, and Pavel Kaderavek
CEITEC, Masaryk University

## Slide 2
A] Scientific question / I’d like to obtain:
  Structure
  Relaxation properties
  Interaction at atomic level resolution
  Analysis (NMR is also analytical method)
  Image (MRI)
B] What do I need to provide / prepare?
C] How much would it cost?
D] How long would it take?
E] Can I do it on my own (or a sudent/colleague of mine)
How to prepare and what to expect from NMR spectroscopy

## Slide 3
NMR
sample
spectrum
Structure
Relaxation properties
Interaction at atomic level resolution
Analysis
Image
200-500 ml of
100-1000 mM compound
Method of choice
Data to be analyzed
Results

## Slide 4
Exp. Method | Proteins | NA | Protein/NA Complex | Other | Total
X-Ray | 133461 | 2098 | 7091 | 8082 | 150732
NMR | 11493 | 1309 | 267 | 92 | 13161
EM | 4181 | 47 | 1478 | 501 | 6207
Other | 32 | 1 | 0 | 4 | 37
Multi Method | 162 | 6 | 3 | 6 | 177
PDB Data Distribution by Experimental Method and Molecular Type
Source: http://www.rcsb.org as of 03Nov2020

## Slide 8
NMR
Safety First

## Slide 10
For most of modern NMR applications,
13C, 15N, and often 2H needed
Isotope | Ground state spin | Natural abundance [%] |  | Rel. Sensitivity
1H | ½ | ~100__ |  | 1.00x10+0
13C | ½ | 1.10 |  | 1.59x10-2
15N | ½ | 0.37 |  | 1.04x10-3
19F | ½ | 100__ |  | 8.30x10-1
31P | ½ | ~100__ |  | 6.63x10-2
12C | 0 | 98.90 |  | -
16O | 0 | ~100__ |  | -

## Slide 11
Samples:
  Small organic molecules - synthesis
  Peptides (10-40 aa) - synthesis
  Proteins (40-200 aa) - 13C/15N enriched media
  Large proteins > 200 aa - 2H/13C/15N enriched media
If high concentrations (>1 mM) multidimensional spectra in natural abundance can be performed

## Slide 12
NMR as a tool for structure determination of proteins and biological complexes:
From single proteins to large systems

## Slide 13
Conventional scheme for structure determination by NMR
Sample preparation / protein expression
NMR data acquisition and processing
Backbone chemical shifts assignment
Assignment of side-chain chemical shifts
Peak-picking of NOESY spectra
Structure calculation
(iterative improvement of 5 and 6)

## Slide 14
Before we start with assignment of backbone chemical shifts we need to know:
1) Protein primary sequence
MQQDDDFQNF VATLESFKDL KSGISGSRIK KLTTYALDHI DIESKIISLI IDYSRLCPDS HKLGSLYIID SIGRAYLDET RSNSNSSSNK PGTCAHAINT LGEVIQELLS DAIAKSNQDH KEKIRMLLDI WDRSGLFQKS YLNAIRSKCF AMDLEHHHHHH
2) Standard chemical shifts of Ca and Cb (vide infra)
3) Secondary structure prediction (values of 2) will be affected accordingly)
4) Precise peak-picking (manually or semi-automatically)
5) 13C/15N uniformly labeled protein (6-30kDa)

## Slide 15
N- C-terminus
Hydrogen bond
Protein backbone and secondary structure
b-strand a-helix
parallel antiparallel

## Slide 16
a-helix
b-strand
Cavanagh et al. Protein NMR Spectroscopy 2nd ed.
13C chem. shift in proteins

## Slide 17
13Cg
13Cb
13Ca
13C’
Ha
Hb
Hb
15N
HN
13Cb
13Ca
13C’
Ha
35Hz
130Hz
140Hz
35Hz
55Hz
35Hz
55Hz
-15Hz
-11Hz
7Hz
-92Hz
< 1Hz
In a 13C/15N uniformly labeled protein, correlation spectra can be measured through single- and double-bond couplings
Sattler et al. Prog. NMR Spectrosc. (1999) 34, 93-158

## Slide 18
1H 1D, Cavanagh et al., 2007
water

## Slide 19
1H 1D, Cavanagh et al., 2007
water
1H-15N HSQC, cca 155 aa, well folded, 600MHz, 293K

## Slide 20
15N-1H HSQC – Heteronuclear SingleQuantum Correlation
1 peak ≅ 1 amino acid
Excellent info about the protein fold
No info about primary sequence

## Slide 21
1H
13C
15N
Traditional triple resonance NMR spectra for protein backbone assignment
HNCO – chem. shifts of C=O
HNCA – chem. shifts of Ca,i, Ca,i-1
HNCOCA – chem. shifts of Ca,i-1
HNCACB – chem. shifts of Ca,i, Ca,i-1, Cb,i, Cb,i-1
HNCOCACB – chem. shifts of Ca,i-1, Cb,i-1
Two of the above spectra needed
15N-1H HSQC rovina

## Slide 22
i-1 i i+1
Alanine Glycine Serine
13C 10 20 30 40 50 60 ppm
Cbi-1, Cai-1
Cbi, i-1
Cai, i-1
1Hi/ 15Ni
1Hi/ 15Ni
1Hi/ 15Ni

## Slide 23
Backbone chemical shifts assignment example:
- fragment S65-S71 (50-66ppm v 13C)

## Slide 24
Automatic chemical shifts assignment
With a known 3D protein structure (e.g. X-ray, Modeller)
Without prior knowledge of a structure
e.g. Automated Projection SpectroscopY APSY (S. Hiller, F. Fiorito, K. Wüthrich & G. Wider, PNAS (2005) 102, 10876-81)
Advantages
Time
Disadavantages
1) With increasing size of the protein (increasing spectral overlap) the reliability is decreasing

## Slide 25
A] Scientific question / I’d like to obtain:
  Structure
  Relaxation properties
  Interaction at atomic level resolution
  Analysis (NMR is also analytical method)
  Image (MRI)
B] What do I need to provide / prepare?
C] How much would it cost?
D] How long would it take?
E] Can I do it on my own (or a sudent/colleague of mine)
How to prepare and what to expect from NMR spectroscopy

## Slide 26: Thank you for your attention
This project received funding by the European Commission under the GA n° 2019-1-IT02-KA203-063391
innocore-project@unitn.it
www.innocore-project.eu
Core Technologies for Education and Innovation in Life Sciences
For Application to Protein Characterization
by
Radovan Fiala, Karel Kubicek, and Pavel Kaderavek
CEITEC, Masaryk University