## Slide 1: Ecotoxicology Part 2 - HAZARDS & RISKS
Ludek Blaha + ecotox colleagues

## Slide 2
Ecotoxicology
Science of doses / concentrations
HAZARDS vs RISKS

## Slide 3
Assessment of chemical hazards
…to…
Humans Other organisms
(TOXICOLOGY) (ECOtoxicology)

## Slide 4: ASSESSMENT and MANAGEMENT of RISKS
Risk ASSESSMENT 
MANAGEMENT 

## Slide 5: WHAT IS HAZARD ? RISK?
HAZARDS
(Inherited properties of stressors … including chemicals)
RISKS
(Probability of the actual occurrence of hazard under specific situation)

## Slide 6: Cause – effect  Risk assessment
Atmospheric
Deposition
Erosion
& Runoff
Untreated discharges
Predicted Environmental
Concentration (PEC)
Laboratory (and field) studies
Ecotoxicity tests
WWTP
Predicted No Effect Concentrations
(PNEC)
Exposure
(resulting from load)
Effects
(what exposures cause effects ?)

## Slide 7: Regulatory approach: risk assessment and management
Hazard
Exposure assessment Dose (or PEC)
Effect assessment
TDI (or PNEC)
Risk characterisation
RQ = Dose / TDI (or PEC / PNEC)
RQ < 1
RQ > 1
Risk management

## Slide 8: Regulatory approach: risk assessment and management
Hazard
Exposure assessment Dose (or PEC)
Effect assessment
TDI (or PNEC)
Risk characterisation
RQ = Dose / TDI (or PEC / PNEC)
§ EU Directive 98/83/EC
(in addition to others) pesticide in drinking water
DW in city of Bruno … atrazine 0.15 mg/L
No pesticide in DW >0.1 mg/L
RQ < 1
RQ > 1
Risk management
RQ = 0.15/0.1 = 1.5
DWTP company $$ for penalty
$$ for DWTP improvement $$ lobbying to affect legislation

## Slide 9: „magnitude“ or „impact“ of actual risk
Vs.
Example - „P“ (probability) is the same for both events
- impact is very different
In ecotoxicology – e.g. fish species:
10% risks of malformations … is compensated by large numbers of eggs 10% risks of feminization  much large impact on population

## Slide 10: (Eco)Toxicology – science of „doses“
‘What is there which is not a poison?
„Cause-effect paradigm“
All things are poison and nothing without poison.
Solely the dose determines that a thing is not a poison.
Paracelsus (1493 - 1541)

## Slide 11: Toxicology – ultimate goal ?
To identify (or predict)
safe vs hazardous levels

## Slide 12: Ecotoxicology: what approaches are available?
RETROSPECTIVE
PROSPECTIVE
Bioassessment
Field assessment
Monitoring
Bioassessment
Field assessment
Monitoring
Lab studies
BIOASSAYS
Simulated small
ecosystems
DISASTERS
PREDICTIONS for future
Time: NOW !
Most common in practice
Lab studies
BIOASSAYS

## Slide 13: Hazard assessment
Organism
Chemical
Adverse Effects
Death
Altered Reproduction
Inhibition of Growth
Tumorigenicity
Skin irritation
…
+
Traditionally – Evaluation of adverse effects using the whole organism models
REGULATORY FOCUS (APICAL ENDPOINTS)

## Slide 14: (Eco)Toxicology methods 1 - standardized assays
Exposure to toxicant (for defined time)
Effective doses Effective concentrations

## Slide 15: Ecotoxicology in current practice
Most legislations on chemicals) (e.g. REACH, Pharmaceuticals, Pesticides)
  have very simple (basic) requirements
    EC50 from acute toxicity
    Of 3 basic assays
      Algae
      Daphnia
      Fish
  Ecotox database:
  www.epa.gov/ecotox

## Slide 16: Laboratory data and results
50
100
LD50 LC50
[concentration] in mg/L or % effluent
Threshold:
TOXICOLOGY No Obervable Adverse Effect Level (NOAEL)
ECOTOXICOLOGY No Observed Effect Concentration (NOEC)
How are LC50 from ecotox assays used ?

## Slide 17: Ecotoxicology in current practice
How to extrapolate 3 (or few more) EC50 values to get legally binding safe concentration, which is protecting virtually all organisms?
PNEC
(Predicted No Effect Concentration)
“value recommended by scientists”
EQS
(Environmental Quality Standard)
“value that occurs in legislation”
?
?

## Slide 18: Extrapolation for Risk Assessment
Data
Assessment factor
L(E)C50 short-term toxicity tests
NOEC for 1 long-term toxicity test
NOEC for additional long-term
toxicity tests of 2 trophic levels
NOEC for additional long-term
toxicity tests of 3 species of 3
trophic levels
1000
100
50
10
Protection level: 95%
(Eco)Toxicological data
Species sensitivity distribution (SSD)
HC5 = 95% protection level
[C]
Assessment / Extrapolation factors
PNEC

## Slide 19
MIXTURES!
Industrial chemicals
Cosmetics
PPP (pesticides)
Biocides
Human pharmaceuticals
Veterinary pharmaceuticals
Chemical laws („bulk“)
nano nano nano nano
REACH (ECHA)
PPP (EFSA)
MPs
(EMA)
§§
§§
WFD – surface w.
GWD – ground w.
Air quality
Food and feed
Soil & Sediments
Wastes
SOIL
AIR
WATER
Two §§ approaches:
Prospective (chemicals…)
Retrospective (mixtures …)

## Slide 20: Notes on practical testing
Testing chemicals
  Traditional / bioassays developed to assess individual chemicals
  Advantages: Standardized approaches
  Disadvantage: Limited ecological relevance
    often acute tests only
    „too standardized…“ (? Less representative ?)
    does not assess/consider bioavailability
    no consideration of mixture effects
    no consideration of specific modes of action
    no consideration of ecological situation
Example: Acute (96h) fish toxicity assay with ethanol
  No deaths (but fish are passive – slow swimming)  OK ?
  Real life: easy prey  population decline

## Slide 21: Notes on practical testing
Testing toxicity of natural contaminated matrices
  Rather new in ecotoxicology – many open challenges
    Whole effluent toxicity testing (WET)
    Contact soil toxicity assays
  More complex and more complicated
    „cause-effects“ often not clear
      Natural variability in matrices
      Algal tests - nutrients (Nitrogen, Phosporus) >> Toxic compounds

## Slide 22
Results of ecotoxicology
WHAT IS IT GOOD FOR ?
SOLVING PRACTICAL PROBLEMS

## Slide 23
Example 1
Application of ecotoxicity results (ECx  EQs)
in regulatory context
European Water FrameworkDIRECTIVE

## Slide 24: EQS in reality – example EU Water Framework Directive

## Slide 25: List of priority compounds EU WFD (selection/examples)
  Most recent (2015) 44 priority compounds (table here) + additional “watch list”  see further
PRACTICE:
Chemical measurements vs limits (EQs)

## Slide 26
http://eur-lex.europa.eu/legal-content/EN/TXT/PDF/?uri=uriserv:OJ.L_.2015.078.01.0040.01.ENG

## Slide 27
Another example where ecotoxicology results are used
European strategy
how to deal with chemicals
REACH

## Slide 28
REACH Registration, Evaluation and Authorisation
of Chemicals
  27-2-2001: White Paper on the Strategy for Future Chemicals Policy
  23-10-2003: Commission’s proposal REACH
  December 2008: Pre-registration mandatory (all chemicals in EU must be registered at ECHA
  European Chemicals Agency (http://echa.europa.eu)

## Slide 29: Existing substances and REACH
  > 95,000,000 known chemicals (…and counting http://www.cas.org/)
  100,000 substances in EINECS (i.e. commercial use)
  30,000 relevant for REACH
  cc 3000 HPVCs (High Production Volume Chemicals)

## Slide 30: REACH legislation in EU
Registration, Evaluation and Authorisation and Restriction of Chemicals

## Slide 31: REACH: what data type must be registered?
Physico-chemical properties, e.g.:
  Vapour pressure, boiling point, Kow,…
Human toxicology, e.g.:
  Acute and chronic toxicity, skin irritation, carcinogenity,…
Environment/ Ecotoxicological information, e.g.:
  Acute and/or chronic toxicity for aquatic organisms, biodegradation, …

## Slide 32: REACH: testing
Total costs: 2,8 to 5,6 billion € (industry pays)
Testing costs (50-60% of total): 86% for Human, 14% Ecotox

## Slide 33: What assays and how exactly?
Depends on legislation (… of course !)
… but current EU legislations tend to be harmonized (use similar approaches)
 example of REACH
Assays must be STANDARDIZED for REACH should follow OECD Guidelines
Other standardization agencies (also include toxicity tests) e.g. ISO, ASTM

## Slide 34: OECD guidelines for testing of chemicals
5 main sections
  Section 1: Physical Chemical Properties
  Section 2: Effects on Biotic Systems (i.e. Ecotoxicity)
  Section 3: Degradation and Accumulation
  Section 4: Health Effects (i.e. Toxicity)
  Section 5: Other Test Guidelines
Organization for Economic Cooperation Development

## Slide 35: OECD guidelines (examples – selection)
Test No. 201: Alga, Growth Inhibition Test | 11 July 2006
Test No. 221: Lemna sp. Growth Inhabition Test | 11 July 2006
Test No. 202: Daphnia sp. Acute Immobilisation Test | 23 Nov 2004
Test No. 211: Daphnia magna Reproduction Test | 16 Oct 2008
Test No. 203: Fish, Acute Toxicity Test | 17 July 1992
Test No. 204: Fish, Prolonged Toxicity Test: 14-Day Study | 04 Apr 1984
Test No. 210: Fish, Early-Life Stage Toxicity Test | 17 July 1992
Test No. 212: Fish, Short-term Toxicity Test on Embryo and Sac-Fry Stages | 21 Sep 1998
Test No. 215: Fish, Juvenile Growth Test | 21 Jan 2000
Test No. 229: Fish Short Term Reproduction Assay | 08 Sep 2009
Test No. 230: 21-day Fish Assay | 08 Sep 2009
Test No. 231: Amphibian Metamorphosis Assay | 08 Sep 2009
SECTION 2 - Aquatic organisms

## Slide 36: OECD guidelines (examples – selection)
Test No. 401: Acute Oral Toxicity
Test No. 402: Acute Dermal Toxicity
Test No. 403: Acute Inhalation Toxicity
Test No. 404: Acute Dermal Irritation/Corrosion
Test No. 405: Acute Eye Irritation/Corrosion
Test No. 406: Skin Sensitisation
Test No. 407: Repeated Dose 28-day Oral Toxicity Study in Rodents
Test No. 408: Repeated Dose 90-Day Oral Toxicity Study in Rodents
Test No. 409: Repeated Dose 90-Day Oral Toxicity Study in Non-Rodents
Test No. 410: Repeated Dose Dermal Toxicity: 21/28-day Study
Test No. 411: Subchronic Dermal Toxicity: 90-day Study
Test No. 412: Subacute Inhalation Toxicity: 28-Day Study
SECTION 4 – Human health effects

## Slide 37
Try it! … download and study your guideline for free!

## Slide 38: Risks of chemicals: a balancing act …. between perception, uncertainties, science and pragmatism?
Final considerations

## Slide 39: SOCIETY – RISKS vs BENEFITS (!)
Local
Global
Value
Time to benifit
Technology
Science
Practice
Other Technologies
Other Laws and Regulations
Other Social Needs
Other Sciences

## Slide 40: Society is a balancing act …
Scientists
Scientists should contribute (provide valid data) for decision making

## Slide 41: WRAP UP and take home message – part 2
What are hazards vs risks?
  Risk assessment and management?
  IMPACTS of risks? Risks vs benefits?
How are the risks calculated
  By comparing EXPOSURES (PEC) with HAZARDS (PNEC)
How are hazards assessed?
  By toxicity assays
    there are 3 most widely used!
    They must be done by standardized approaches (OECD guidelines)
  What are results of toxicity assays (ICx, NOEC, LOEC)?
  How are the results used?
    Predictions of PNEC (by application of AFs)
    Regulatory acceptance  EQS
Know examples of ecotox applications
  PNEC (EQs) in Water framework directive
  Predictive risk assessment in REACH regulation