## Slide 1
Radiomedicinské methody
SPECT – single photon emission computer tomography
PET – positron emission tomography
Radiotherapy

## Slide 2
Radiodiagnostické metody
Jednofotonová emisní tomografie (SPECT)
-emitující radioisotopy
rozlišení ~1 cm3

## Slide 3: SPECT

## Slide 4
Izotopy pro SPECT
Izotop | Přeměna | Poločas | Zdroj
99mTc |  | 6 h | generátor, 99Mo(–)99mTc, 66 h
111In |  | 68 h | cyklotron, 111Cd(p,n)111In
131I | , b– | 8 d | reaktor
153Sm | , b– | 46 h | reaktor
166Ho | , b– | 26 h | reaktor
177Lu | , b– | 6.7 d | reaktor

## Slide 5
PET

## Slide 6: PET
radioisotopes emitting positrons (b+-particles)
annihilation with electrons
two co-linear photons with an energy of 511 keV
detection of both photons at the same time
resolution about 1 mm3
low energy  better resolution

## Slide 7
Izotopy pro PET
Izotop | Přeměna | Poločas | Zdroj
19F | + | 110 min | cyklotron, 18O(p,n)18F
11C | + | 20 min | cyklotron, 14N(p,a)11C
61Cu | + | 3.3 h | cyklotron, 61Ni(p,n)61Cu
64Cu | + | 13 h | cyklotron, 64Ni(p,n)64Cu
66Ga | + | 9.5 h | cyklotron, 63Cu(,n)66Ga
68Ga | + | 68 min | generátor, 68Ge(–)68Ga, 288 d
86Y | + | 15 h | cyklotron, 86Sr(p,n)86Y
110In | + | 69 min | generátor, 110Sn(–)110In, 4.11 d

## Slide 8
Každá minuta se počítá
Příprava izotopu
Izolace izotopu
Příprava radiofarmaka
Separace radiofarmaka
Analýza radiofarmaka
Doprava k pacientovi
Aplikace pacientovi
Dosažení žádané biodistribuce
Snímkování

## Slide 9: PET vs. SPECT
[18F]-FDG-PET
99mTc-MDP-SPECT

## Slide 10: Fused images
localization in tissues – combined techniques with CT or MRI
fused images – PET/CT, PET/MRI, SPECT/CT, SPECT/MRI
multimodal contrast agents

## Slide 11: Radiotherapy
Leksell gamma knife
  focuses the radiation from external sources into tumour
internal sources of radiation
  short and defined radius of particles in tissue
  -emitters
  -emitters
  -emitters with low energy
  emission of Auger electrons (EC isotopes)
  selective deposition in tumors – half-lives in hours

## Slide 12: Radiotherapy
Isotope | Decay | Half-life | Source | Mean range in tissue
64Cu | – | 12.8 h | cyclotron, 64Ni(p,n)64Cu | 0.2 mm
67Cu | – | 62 h | cyclotron, 67Zn(n,p)67Cu | 
67Ga | Auger | 3.26 d | cyclotron | 
89Sr | – | 50.5 d | reactor | 
90Y | – | 64 h | generator, 90Sr(–)90Y | 3.9 mm
111Ag | – | 179 h | cyclotron | 1.1 mm
149Pm | – | 2.2 d | reactor | 
153Sm | – | 1.9 d | reactor | 
161Tb | – | 166 h | reactor | 0.3 mm
166Ho | – | 1.1 d | reactor | 
177Lu | – | 6.7 d | reactor | 
186Re | – | 90 h | reactor | 1.1 mm
188Re | – | 17 h | generator, 188W(–)188Re | 3.3 mm
212Pb | –/ | 10.6 h/1.01h | reactor | 0.1 mm

## Slide 13: Radiotherapy

## Slide 14
Common criteria for radiopharmaceuticals
Selected molecule must be amenable to radiolabelling. Reaction must provide sufficient radiochemical yield, specific activity and must proceed in appropriate time, that means maximally 4, ideally less than 3 half-lives of radioisotope – also depends on half-life itself. Reaction must proceed under reasonable conditions because of automation of procedure in the case of clinical production. Procedure including yield must be reliable and reproducible.
Biodistribution of a radiopharmaceutical must be related to the physiological response to enable measuring functionality of biochemical process under investigation.
High affinity to the target leading to high contrast of a PET image. Interaction between radiopharmaceutical and biomolecules in target tissue must be the major mechanism. Also high specificity for target molecule is essential because interaction with similar targets leads to interference with desired radioactive signal detected by a PET camera.
The lipophilicity (defined as usual partition coefficient between n-octanol and water – log P) that determines ability to cross cell membranes.
Optimal passage of lipid bilayers requires log P ~ 1.5 – 2. Higher log P values result in nonspecific binding caused by hydrophobic interactions with lipids and proteins.
Certain properties as passage across the cell membrane or other barriers like blood brain barrier (BBB). Besides mentioned lipophilicity, also active transport of compounds must be taken in account, e.g. dopamine, serotonin and amino acids.

## Slide 15
Common criteria for radiopharmaceuticals
In general, a low affinity to P-glycoprotein (P-gp) is a desirable property for most radiopharmaceuticals. P-gp is an ATP-dependent efflux pump naturally expressed in BBB. It can be over-expressed in tumours. P-gp transports compounds that have high affinity for the pump out of the cell and then radiotracers that have high affinity for P-gp show little accumulation in tissues like brain and tumour.
Metabolism of a radiopharmaceutical is a very important point. Rapid metabolism is generally undesirable. Metabolites can then bind to other molecules or take part in other metabolic processes and result in non-specific accumulation of radioactivity. It is preferable to have the radioisotope in the part of molecule which reaches the target at first and after that is further metabolised. In some cases, metabolism of radiotracer is the mechanism underlying the accumulation of radioactivity in tissue.
Clearance of non-specifically bound radioactivity by the time of measurement PET must be discriminated. This is relevant mainly for labelled macromolecules that slowly diffuse into cells and only small portion is bound to the target of interest. The unbound radiolabelled molecules must leave the cells again and be cleared from the circulation.
Mutagenicity and toxicity, despite the radiophramaceutical is prepared under non-carrier added (NCA) conditions and small mass is administrated to the patient, must be tested. This differs in different countries according to the law. Usually toxicity tests on rodent species and Ames test for mutagenicity are performed at dosages much higher than those applied in PET studies.

## Slide 16: Preparation and administration
RCY – RadioChemical Yield
CA – Carrier Added
NCA – Non-Carrier Added

## Slide 17: Targeting
vector – selectivity for imaged tissue: peptide, oligosacharide, etc.
chemically sensitive – labelling at mild conditions

## Slide 18
include a biologically active molecule covalently linked to the complex
e.g.
Progesterone receptor analogues
(prostate cancer)
Cocaine analogues
(CNS diseases)
Targeting
Notes: 18

## Slide 19
Octreoscan – 111In –DTPA-Octreotide
Targeting
Octreoscan imaging for neuroendocrine tumors.
a) Coronal octreoscan image demonstrating radiotracer uptake in multiple liver metastases and a large pancreatic primary neuroendocrine carcinoma.
(b) Coronal octreoscan fusion images with single photon emission tomography (SPECT) providing increased anatomic detail.
(c) Axial octreoscan fusion images with SPECT.

## Slide 21
Technetium 99mTc
predicted by Mendeleev
first isolated 1938
20 isotopes (7 relatively stable)
used extensively (>90% of all diagnostic nuclear medicine)
t1/2 = 6 h
-ray emission energy of 141 keV
versatile coordination chemistry
multiple oxidation states
easily generated from 99Mo (t1/2 = 66 h)
Rhenium
186Re, t1/2 = 90 h, available from reactor
188Re, t1/2 = 17 h, available from 188W(–)188Re generator
chemical properties similar to Terchnetium: diagnostic/therapeutic isotop-pair
Notes: 21

## Slide 22
Technetium 99mTc
99Mo/99mTc Generator
patented in 1958
fission-produced 99Mo is processed and purified to anionic molybdate
loading on the positively charged alumina (Al2O3) column

## Slide 23
Technetium 99mTc
Radionuklidový generátor

## Slide 24
Technetium 99mTc
Počty elucí z generátoru 99mTc

## Slide 25
Chemistry
TcO4– most stable oxidation state, produced in generator, can not be complexed
insoluble TcO2
reduction with ascorbic acid, FeCl2, NaBH4, Na2S2O4, SnCl2
– oxidation states IV, V – oxocation technecyl
(disproportionation V  IV + VII)
– oxidation states I, II, III (oxidation  IV)
stabilization of oxidation states with ligands
Technetium kit
reducing agent
coordinating ligand
antioxidants
buffers
lyophilized and sealed under inert atmosphere
Technetium 99mTc
Notes: 25

## Slide 26
Pharmacology
bio-distribution and targeting depends much on size and charge:
  neutral – brain
  cationic – hart
  anionic – bones and kidney
so called technetium essential or first generation agent
targeting of other organs requires designer ligands:
  must traverse the blood brain barrier
  moderately lipophilic
  neutral charge
Technetium 99mTc
Notes: 26

## Slide 27: Neutral complexes – brain imaging – oxidation states IV, V
Technetium 99mTc

## Slide 28
Cationic complexes
hart imaging
uptake via Na-K ATPase pump as K+ mimics
Technetium 99mTc
Cardiolite
Notes: 28

## Slide 29
Cardiolite
Each 5 mL vial contains a sterile, non-pyrogenic, lyophilized mixture of:
Tetrakis (2-methoxy isobutyl isonitrile) Copper (I) tetrafluoroborate – 1.0 mg
Sodium Citrate Dihydrate – 2.6 mg
L-Cysteine Hydrochloride Monohydrate – 1.0 mg
Mannitol – 20 mg
Stannous Chloride, Dihydrate, minimum (SnCl2•2H2O) – 0.025 mg
Prior to lyophilization the pH is 5.3 to 5.9. The contents of the vial are lyophilized and stored under nitrogen.
This drug is administered by intravenous injection for diagnostic use after reconstitution with sterile, non-pyrogenic, oxidant-free Sodium Pertechnetate 99mTc Injection. The pH of the reconstituted product is 5.5 (5.0 - 6.0). No bacteriostatic preservative is present.
The precise structure of the technetium complex is 99mTc[MIBI]6+ where MIBI is 2-methoxy isobutyl isonitrile.
Over 40 million people have received cardiac scans using Cardiolite.
Technetium 99mTc
Notes: Cardiolite has now been commercialized and is used to determine heart function and myocardial perfusion
201Tl is also used for heart imaging, but cardiolite is preferred
29

## Slide 30
Imaging agents in action
Myoview = tetrofosmin
Technetium 99mTc
Notes: 30

## Slide 31
Bone imaging
hydroxyapatite principal mineral component of bones Ca10(PO4)6(OH)2
phosphate (PO43-) and pyrophosphate (P2O72-) bone seeking anions
diphosphonates give improved performance
absorption via calcium coordination to phosphonate
stressed bone has higher calcium concentration
main use to detect cancer metastasis into bone
arthritic right ankle
Technetium 99mTc
Notes: 31

## Slide 32: Carbon 11C
half-life 20.40 min
decay mode: 99.8 % b+, 0.2 % EC
max b+ energy: 0.96 MeV
range in tissue: 0.96 mm
decay product: 11B
Production
cyclotron-generated: mainly produced by the proton bombardment of 14N
14N(p,a)11C nuclear reaction
target gas:
2% O2 in N2  11CO2
5% H2 in N2  11CH4

## Slide 33
Carbon 11C

## Slide 34: Carbon 11C
Palladium mediated reactions

## Slide 35: Carbon 11C
11CH3I
methylation of N –, O –, S – compounds

## Slide 36: Carbon 11C

## Slide 37: Carbon 11C

## Slide 38: Carbon 11C

## Slide 39: Carbon 11C

## Slide 40: Fluorine 18 F
half-life 109.7 min
decay mode: 96.9 % b+, 3.1 % EC
max b+ energy: 0.63 MeV
range in tissue: 0.54 mm
decay product: 18O

## Slide 41: Fluorine 18 F
Production

## Slide 42: Fluorine 18 F
Electrophilic 18F-Fluorination
reaction of highly polarized fluorine with an electron rich reactant, e.g., an aromatic system, an alkene, or a carbanion
starting with [18F]F2 – 50% RCY (molecule compsition 18F–19F)
other fluorination agents [18F]XeF2, [18F]AcOF

## Slide 43: Fluorine 18 F
Nucleophilic 18F-Fluorination
[18F]fluoride
protonation at low pH
formation of ion pairs with cations – decrease of reactivity
phase transfer catalysis or use of crownethers and cryptands
Nucleophilic Aliphatic Fluorination
R–X + F– R–F + X–
Nucleophilic Aromatic Fluorination

## Slide 44: Fluorine 18 F
Prosthetic groups (PG)
labelled compound containing reactive moiety
fluoromethylation with [18F]FCH2I or [18F]FCH2Br
fluoroethylation with [18F]FCH2CH2X
other precursors

## Slide 45: Fluorine 18 F
Prosthetic groups for biomolecules
enable labelling of peptides and proteins
Amine reactive PGs
Carboxylic acid reactive PGs
Thiol reactive PGs

## Slide 46: Fluorine 18 F
Prosthetic groups (PG)

## Slide 47: Fluorine 18 F
18F-FDG: [18F]fluoro-2-deoxy-D-glucose – vyrábí se cyklotronicky v MOÚ
1968, J. Pacák and M. Černý, Department of Organic Chemistry, UK
the most common PET tracer
distribution similar to glucose
can not be metabolized
accumulation in metabolically-active tissues
Whole-body PET scan using 18F-FDG to show liver metastases of a colorectal tumor

## Slide 48: Fluorine 18 F

## Slide 49: Iodine isotopes

## Slide 50: Metalic nuclides (non-Tc, non-Re)

## Slide 51: Complex stability
Thermodynamic stability
proton vs. metal competition
ligand basicity
stability constants

## Slide 52: Complex kinetics
Formation kinetic
chemistry – high concentrations; NMR, UV-VIS
radiochemistry – low concentrations
Kinetic inertness
in vitro experiments
  transmetallation (Zn(II))
  decomplexation in acidic solutions
  incubation in plood plasma

## Slide 53: Open-chain ligands
high thermodynamic stability
kinetically labile
fast complexation
applied in large excess

## Slide 54: Macrocyclic ligands
high thermodynamic stability
kinetically inert
slow complexation
variation of pendant arms
– carboxylates, alcohol, amine, phosphorus derivatives
– changes in stability, inertness, complexation rate, charge, lipophylicity

## Slide 55: Bifunctional chelators
Thiourea bond

## Slide 56: Gallium 68Ga
half-life 67.6 min
decay mode: 89 % b+, 11 % EC
max b+ energy: 1.90 MeV
range in tissue: 2.12 mm
decay product: 68Zn
Generator produced
source 68Ge (T1/2 = 271 d)
adsorbed on TiO2 or SnO2
elution with HCl or citric acid
Chemistry
trivalent
hexacoordination
hard metal ion
precipitation of hydroxide at wide pH range
formation of tetrahydroxido complex at high pH

## Slide 57: Ligands for 68Ga complexation Aminocarboxylates Hydroxybenzyl and hydroxypyridyl derivatives Thiol and amino-thiol chelates
R =
Gallium 68Ga

## Slide 58: Copper isotopes
Isotope | Decay | Half-life | Source
60Cu | + | 24 min | cyclotron, 60Ni(p,n)60Cu
61Cu | + | 3.3 h | cyclotron, 61Ni(p,n)61Cu
62Cu | + | 9.74 min | generator, 62Zn(–)62Cu, 9.3 h
64Cu | + (61%), – (39%) | 12.8 h | cyclotron, 64Ni(p,n)64Cu
67Cu | – | 62 h | cyclotron, 67Zn(n,p)67Cu
isotopes 60, 61, 62 and 64 – PET
isotopes 64 and 67 – SPECT and therapy
difficult production and isolation
Chemistry
divalent
hexacoordination
Jahn-Teller effect

## Slide 59: Ligands for copper complexation Open-chain ligands
Copper isotopes

## Slide 60: Ligands for copper complexation Macrocyclic ligands
Copper isotopes

## Slide 61: Sc, Y, In and Lanthanoides
 | Decay | Half-life | Source
Diagnotic isotopes |  |  | 
44Sc | + | 3.93 h | generator, 44Ti(EC)44Sc, 59 y or cyclotron, 44Ca(p,n)44Sc
86Y | + | 14.7 h | cyclotron, 86Sr(p,n)86Y
110In | + | 69.0 min | generator, 110Sn(–)110In, 4.11 d
111In |  | 68 h | cyclotron, 111Cd(p,n)64In
134La | + | 6.70 min | generator, 134Ce(–)134La, 3.0 d
140Pr | + | 3.39 min | generator, 140Nd(–)140Pr, 3.3 d
Therapeutic isotopes |  |  | 
90Y | – | 64 h | generator, 90Sr(–)90Y, 28.8 y
149Pm | – | 2.2 d | reactor
153Sm | – | 1.9 d | reactor
161Tb | – | 166 h | reactor
166Ho | – | 1.1 d | reactor
177Lu | – | 6.7 d | reactor

## Slide 62: Sc, Y, In and Lanthanoides
Chemistry
octa- or nona-coordination
octadentate ligands
hard metal ions

## Slide 63
Radiochemical research
Bisphosphonate-containing dota-amides
ligand synthesis and characterization
chemical complexation study
labelling (complexation of radionuclide)
– pH, temperature, ligand concentration
affinity and stability study
Chart: t [min]
| 0 | 1 | 3 | 5 | 10
40°C | 0 | 2.1333 | 2.6 | 3 | 4.1333
60°C | 0 | 5.7667 | 10.5 | 14.1667 | 21.1333
95°C | 0 | 7.9333 | 32.3333 | 60.5333 | 85.3
Chart: t [min]
| 0 | 2 | 5 | 10
40°C | 0 | 12 | 13 | 15
60°C | 0 | 31 | 77 | 93
95°C | 0 | 84 | 92 | 98
Labeling
Affinity

## Slide 64
Radiochemical research
Biodistribution of 177Lu-complexes in Lewis rat 24 h after injection

## Slide 65
Radiochemical research
In vivo SPECT/CT visualization of 177Lu-complex
1 h p.i.
24 h p.i.

## Slide 66
64Cu complex
Radiochemical research

## Slide 67
PET/CT imaging of bone metastases with 68Ga-complex
(a) = coronal PET, (b) = sagittal PET/CT. For comparison (c) shows 18F-fluoride PET.
University of Mainz, Zentral Klinik Bad Berka
Radiochemical research

## Slide 68
Radiochemical research
68Ga-complex

## Slide 69
Děkuji za pozornost!