## Slide 1
Protein characterization by mass spectrometry
C7250
Part IV
Zbyněk Zdráhal
RG Proteomics, CEITEC-MU
Proteomics CF, CEITEC-MU
NCBR FS MU
zdrahal@sci.muni.cz
Functional Genomics and Proteomics
National Centre for Biomolecular Research
Faculty of Science Masaryk University

## Slide 2
GIGO
Appropriate sample preparation – key stone of success
conservation of original protein status conservation of modification status (e.g. phosphatase inhibitors)
removal of contaminants interferring MS analysis
...
C7250

## Slide 3
Demandingness of proteome analysis
protein number exceeds substantially number of genes
human genome contains ~21 000 genů, but human proteome might contain
~ 1 000 000 proteins and their forms
(isoforms, PTMs)
(http://www.expasy.org/sprot/hpi/hpi_desc.html)
~ 10 000 proteins in cell
wide range of protein concentrations (~ 10 orders)
necessity of efficient separation of high abundant components from low abundant ones,
no PCR-like amplification method
wide range of physico-chemical properties
protein complexes
necessity of protein complex analysis for deeper understanding mechanisms of cellular
processes
about 80% of proteins perform their funcions only as a part of a complex
C7250
proteoforms

## Slide 4
C7250
~ 105 peptides
Direct LC-MS/MS analysis of the whole sample
1000 peptides/peak
~ 100 peptides
~ 900 peptides
not measured
scan rate
time limitation
Fractionation/separation
to obtain maximum information

## Slide 5
C7250
Fractionation/separation
the aim: to simplify extremely complex mixture
to separate specific group of proteins/peptides (e.g. phosphopeptides)
necessity of combination of separation principles – multidimensional separation
selection of appropriate combination for given experiment
(separation dimension might be also selected method of MS analysis)
electrophoretic techniques:
isoelectric focusing (in-gel, in-liquid)
SDS PAGE
2D gel electrophoresis (DIGE)
capillary electrophoresis
chromatographic techniques:
liquid chromatography
- reverse phase
- ionex
- molecular sieve
- affinity (IMAC, MOAC, antibody)
- HILIC (hydrophilic interaction chromatography)
off-line
on-line
immunoprecipitation

## Slide 7
Standard 1-D approaches
1-D GE
protein
digestion
separation
protein level
MS/MS
separation
peptide level
protein
digestion
MALDI-MS/MS
LC-MS/MS
„SIMPLE“ MIXTURES
1-D LC-MS/MS
shotgun proteomics
C7250
separation
protein level
MS
MS/MS
top-down
high resolution !!

## Slide 8
Protein isolate of bacteriophage – 1-D separation
Iden. – 5 major
proteins
LC-MS/MS
kDa
66.2
45.0
31.0
21.5
14.4
97.4
GE
cca 50 bands
concentration range
reduced possibility of minor component detection
it infuenced by
instrumentation
LC separation conditions
C7250

## Slide 10
2-D GE
2-D LC-MS/MS
protein
digestion
separation
protein level
MS/MS
separation
peptide level
protein
digestion
Classical 2-D approaches
2-D
LC-MS/MS
MALDI-MS
MALDI-MS/MS
on-line/off-line
LC-MALDI
C7250

## Slide 11
2-D GE/MALDI-MS
Protein isolate of bacteriophage – 2-D separation
≈ 700 spots
≈ 20 proteins
C7250

## Slide 12
Protein mix
digestion
2D - RP
MS/MS
1D - SCX
On-line (“MudPIT”)
fractionation
step by step
2D - RP
MS/MS
Peptide
fraction
1D - SCX
Off-line
UV
Peptide
fraction
Peptide
fraction
Peptide
fraction
Peptide
fraction
Peptide
fraction
Peptide
fraction
Peptide
fraction
LC
2-D LC
peptides
MudPIT (multidimensional protein identification technology)
C7250

## Slide 13
2-D LC
peptides
On-line
C7250

## Slide 14
2-D LC (peptides)
1D-RP
2D-RP, fraction 5 mM
2D-RP, fraction 50 mM
2D-RP, fraction 100 mM
On-line
Dionex application note
C7250

## Slide 15
2-D LC (peptides)
RP-RP
the same stationary phase – jiné pH
www.ace-hplc.com
Orthogonality of Separation
C7250

## Slide 16
Characterization of proteome and phosphoproteome of HEK293 cells
lysis
SDT buffer [SDS+DTT+Tris]
HEK293
SPL – „scheduled precursor list“ analysis enables repeated analysis of sample with exclusion of already identified peptides in previous analysis
TiO2
enrichment
analysis of phosphofractions
LC-MS/MS (pH 3)
(Orbitrap Elite)
Data processing
Data processing
direct analysis
w/o and with SPL
LC-MS/MS (pH 3)
(Orbitrap Elite)
reversed phase
pH 10
1D LC separation
Data processing
analysis of fractions
LC-MS/MS (pH 3)
(Orbitrap Elite)
FASP
TMT labeling
cooperation with Assoc. Prof. Bryja group, FS MU
C7250

## Slide 17
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30
LC-separation of the digested sample in 1D (high pH)
reversed phase
pH 10
1D LC separation
C7250

## Slide 18
17931
20395
86212
95781
Number of identified peptides
Data processing
direct analysis
w/o and with SPL
LC-MS/MS (pH 3)
(Orbitrap Elite)
C7250
Data processing
analysis of fractions
LC-MS/MS (pH 3)
(Orbitrap Elite)

## Slide 19
Number of identified proteins
9013
3398
3098
5474
5140
1317
1126
8560
Fractionation
three fold increase in number of identified proteins
Higher sequence coverage for most proteins
C7250

## Slide 20
Diameter of HPLC column vs sensitivity
„Sensitivity increases with a decrease in column diameter because the same sample mass (amount) is eluted in a smaller volume. Therefore the concentration of the eluting peak is higher and the detection signal is stronger.“
Amer. Lab., 2001, 33 (10), 26-38.
C7250

## Slide 21
C7250
Capillary and nano columns
Increase in sensitivity
reduction of injected sample amounts
reduced consumption of solvents
www.ace-hplc.com

## Slide 22
sorbents
1-D: ionex
reverse phase
HILIC
IMAC (phospho)
affinity (e.g. lectin – glyco)
2-D LC
peptides
On-line vs Off-line
automation flexibility
optimalization
continuous collection of fractions
C7250
2-D: reverse phase

## Slide 23
LC –MALDI
(peptides)
Peptide
fraction
nano LC (RP)
ESI-MS/MS
on-line
MALDI
TOF/TOF MS
off-line
Deposition on MALDI target
Sample storage
C7250

## Slide 25
LC separation of complex protein mixtures
Protein mix
Protein
1D fraction
Fractionation I.
Ionex, SEC, ….
Fractionation II.
Protein
1D fraction
Protein
2D fraction
RP
Various types of detection (e.g. UV)
exp.
exp.
Protein
2D fraction
digestion
1D (2D) HPLC
ESI-MS/MS
C7250

## Slide 26
proteins
peptides
C7250
LC separation of complex protein mixtures

## Slide 27
Combination of GE a LC separation
slices
protein fractionation
digestion
nano 1-D LC
proteins
peptides
1-D GE
ESI-MSMS
or
IPG strip
C7250

## Slide 28
from Carter et. al. The Plant Cell, 2004, 16, 3285–3303.
2D-On-line
2D-Off-line (3D ?)
C7250

## Slide 29
from Carter et. al. The Plant Cell, 2004, 16, 3285–3303.
C7250

## Slide 30
Depleted blood plasma
(3500 – 9000 proteins ??)
IEF (liq)
20 fractions
1. dimension
LC (RP)
1600 fractions
2. dimension
GE (1D/2D)
“ ∞ “ fractions
3/4. dimension
from H. Wang, Molecular & Cellular Proteomics, 2005, 4, 618–625.
0. dimension
Example of multidimensional proteome analysis (screening)
C7250

## Slide 31
C7250
A draft map of the human proteome
Min-Sik Kim et al., Nature 509, 575-581 doi:10.1038/nature13302
293 000 non redundant peptides
corresponding to proteins encoded by 17294 genes

## Slide 32
from A.D. Zoumaro-Djayoon et al. / Methods 56 (2012) 268–274
Targeted separation - immunoaffinity fractionation (Y(phos))
C7250

## Slide 33
from K. Bluemlein et al. / Nature protocols 6 (2011) 859 –869
Targeted MS analysis of selected proteins
C7250
Parent mass
Fragment mass
CID
Q1
Q3
Q2
Q1 „fix“
Q3 „fix“
quadrupole Q1 and Q3 are fixed to selected values of m/z ( Q1-precursor and
Q3- selected fragment), only precursors displaying production of selected
fragment during fragmentation in collisional cell are recorded
enables to follow tens of reactions (transitions) during analytical run (MRM)

## Slide 35
High throughput
C7250

## Slide 36
+ Miniaturization - chip technology
C7250

## Slide 38
Protein quantification by MS
Functional Genomics and Proteomics
National Centre for Biomolecular Research
Faculty of Science Masaryk University

## Slide 39
Protein quantification by MS
Approaches:
using isotopically different tags
  Absolute quantification
  determination of protein concentration (amount) by addition of
  corresponding standard with known amount (AQUA, PSAQ)
  Relative quantification
  evaluation of relative changes of the protein content in compared
  samples
  label free
  metods of absolute and relative quantification based on statistical processing of MS, or MS/MS data
  advantage of this approach is possibility of comparison of unlimited number of samples and absence of derivatization reaction or isotopically labeled standards
C7250

## Slide 40
Relative quantification approaches
Protein sample B
Digestion of pooled samples
Identical peptides from different samples
are distinguished
100%
Protein sample A
SILAC, in-vivo
LC-MS
LC-MS/MS (iTRAQ)
ICAT, ICPL, iTRAQ
Separated digestion of samples
iTRAQ, 16O/ 18O
Identical peptides in MS mode
are not distinguished
MS/MS
C7250

## Slide 41
W. Yan, S.S. Chen, Briefings in functional genomics and proteomics 4 (1), 1–12, (2005)
Overview of relative quantification methods
C7250

## Slide 42
Stable Isotope Labelling with Amino acids in Cell culture (SILAC)
in vivo
proteins are labeled by growing cells
in media containing isotopically labeled
amino acids
(e.g. 2H-Leu, 13C-Lys, 13C-Tyr,13C-Arg,
13C/15N-Arg)
A
B
AA labeled
cell growing
combining
purification
digestion
MS quantification
AA normal
picture from Ong et al.: MCP 1(2002), 376
C7250

## Slide 43
ICAT ... Isotope-Coded Affinity Tags
technology for protein expression analysis
improved quantitation of a wider range of proteins
overcomes limitations of 2-D gel method (e.g. membrane, low abundant proteins)
tags specific for cysteine-containing peptides (reduction of sample complexity)
easy automation of a procedure
C7250

## Slide 44
ICAT analysis
peak ratios = relative abundance
C7250

## Slide 45
from Ong et al.: MCP 1 (2002), 376
Comparison of in vivo and in vitro quantification methods (SILAC vs ICAT)
Cell cultures
C7250

## Slide 46
Mass Coded Abundance Tagging (MCAT)
Cagney G., Emili A.: Nature Biotechnol 20 (2002), 163-170
tryptic digestion
modification of digest of selected sample (K)
mixing nemodif/modif in ratio 1:1
D = 42 Da
C7250

## Slide 47
1:1
Cagney G., Emili A.: Nature Biotechnol 20 (2002), 163-170
MCAT
C7250

## Slide 48
MCAT
Cagney G., Emili A.: Nature Biotechnol 20 (2002), 163-170
peak ratios = relative abundance
C7250

## Slide 49
MCAT
possibility of utilization of derivatization for de novo sequencing
b ions unchanged , y ions in doublets (42 Da)
C7250

## Slide 50
Reductive alkylation - dimethylation
- lysine and N-term of peptide
- isotopically labeled formaldehyde (D, 13C)
Hsu et al., Anal.Chem. 2003
C7250

## Slide 51
Wu et al., Chem. Commun. 2014
C7250
Reductive alkylation - dimethylation

## Slide 52
Wu et al., Chem. Commun. 2014
C7250
Reductive alkylation - dimethylation

## Slide 54
iTRAQ
isobaric tags (4, 8), preferentially on Lys
labeled samples have the same behavior during LC separation and MS analysis
quantification based on intensity ratios of reporter ions after MS/MS
1:1:1:1
Applied Biosystems
C7250
similarly TMT tags (Thermo Fisher Scientific) – 6/10 tags (see later)

## Slide 55
iTRAQ
Applied Biosystems
C7250

## Slide 56
Applied Biosystems
iTRAQ
C7250

## Slide 57
Applied Biosystems
iTRAQ
C7250

## Slide 58
TMT značky
TMT labels
Tandem Mass Tags
from http://planetorbitrap.com
C7250

## Slide 59
TMT
C7250
Thermo Fischer Scientific
isobaric labels (up to 16-plex)
MS/MS
Cysteine-reactive mass tags (6-plex)
quantitation of the relative abundance of cysteine modifications, such as S- nitrosylation, oxidation and disulfide bonds
Carbonyl-reactive mass tags (6-plex)
glycan, steroids, or oxidized proteins quantification
lysine labeling

## Slide 60
TMT
C7250
Thermo Fischer Scientific

## Slide 61
Reagents contain different numbers and combinations of 13C and 15N isotopes in the mass reporter. The different isotopes result in a 10-plex set of tags that have mass differences in the reporter that can be detected using high resolution Orbitrap MS instruments.
TMT
C7250
Thermo Fischer Scientific

## Slide 62
EASI-tag
Easily Abstractable Sulfoxide-based Isobaric tag
bioRxiv preprint first posted online Nov. 27, 2017; doi: http://dx.doi.org/10.1101/225649
(a) Molecular structures of the triplex version of EASI-tag. The isobaric labeling reagents are composed in a
modular way of four functional groups and feature a central sulfoxide moiety, which introduces an asymmetric,
low-energy cleavage site (zig-zag lines indicate fragmentation site). The stable-isotope labeled positions of the
neutral loss and equalizer group for multiplexing are indicated by asterisks. Standard labeling protocols can be
applied to couple peptides via the amine-reactive moiety.
(b) Mass spectra of an EASI-tag-labeled yeast peptide mixed in a ratio of 1:3:10. HCD fragmentation of the doubly charged precursor ion abstracts the neutral loss group and yields the peptide-coupled reporter ion cluster.
C7250

## Slide 63
EASI-tag
Easily Abstractable Sulfoxide-based Isobaric tag
C7250
(c) Co-isolation of the natural isotope cluster in a standard isolation window centered on the precursor ion (upper panel) convolutes the relative abundance of peptide coupled reporter ions. An asymmetric isolation window (lower panel) that suppresses the signal from adjacent isotope peaks and enables direct quantification of reporter ions.
(d) The precursor mass information is retained in the peptide-coupled reporter ions for EASI-tag labeled peptides. Colored peaks indicate the peptide-coupled reporter ions from an identified yeast peptide in a two proteome experiment (mixing ratios: 1:3:10 for yeast & 1:1:1 for human). Grey peaks are peptide-coupled reporter ions from a co-isolated peptide.
(e) EASI-tag- and TMT-labeled HeLa peptides were fragmented with normalized collision energies between 10 and 34. (N = 17,565 precursors for EASI-tag & 20,610 for TMT)
bioRxiv preprint first posted online Nov. 27, 2017; doi: http://dx.doi.org/10.1101/225649

## Slide 65
Label – free approach
No labels
Samples measured individually
Comparison of „unlimited“ number of samples
Critical steps:
  data normalization
  imputation of missing values (DIA – reduction of number of missing values)
LC-MS/MS
noise removal
peak detection
intensity/area calculation for individual peaks
normalization
imputation of missing values
calculation of fold changes for individual proteins among samples
Statistics evaluation
significant changes in proteome
induced by stimuli under study
C7250
Identification based on MS/MS data, connection of identity to individual signals (intensity, area)

## Slide 66
Label – free approach
MA plots - dependence of (x-y) on (x+y)/2
C7250

## Slide 67
Label – free approach
C7250

## Slide 69
AQUA Peptide Selection
Order selected peptide isotopically labeled (15N, 13C)
Adding labeled peptide to protein mix
Digest
Analyze by LC-MS/MS to quantitate protein of interest
Select an optimal tryptic peptide and stable isotope amino acid from the sequence of your protein of interest
Optimize LC-MS/MS separation protocol for quantitation
Price !!!
Absolute quantification using AQUA peptides
Only for selected protein
C7250

## Slide 70
Absolute quantification
C7250
AQUA peptides
QconCAT
PSAQ
synthesis of
isotopically labeled proteotypic peptides
construction of artificial gene for expression of proteotypic peptides originated from up to 20 proteins
expression in E.coli using labeled medium
purification of artificial protein
MS analysis
addition of known amount into sample
digestion
expression of the whole
izotopically labeled protein (plus tag for purification)
Rivers at al., MCP 6, 1416 (2007)
protein purification
Brun et al., MCP 6, 2139 (2007)
MS analysis
addition of known amount into sample
digestion
MS analysis
addition of known amount into sample
digestion

## Slide 71
Absolute quantification
Stable Isotope Standards and Capture by Anti-Peptide Antibodies
(SISCAPA)
N.L. Anderson, J. Proteome Res., 3, 235 (2004)
MRM
PRM
S. Pan, J. Proteome Res., 8, 787 (2009)
C7250

## Slide 72
Targeted MS/MS analysis of selected proteins
relative /absolute quantification
multiple reaction monitoring (MRM)
screening – selection of candidate protein
method establishment (selection of MRM transitions – peptide + selected fragment)
Protein mixture
In-solution
digestion
Peptides
LC-MS/MS – MRM mode
final analysis and data processing
http://www.srmatlas.org
C7250
Similarly PRM

## Slide 73
Multiplex Immuno-Liquid Chromatography−Mass Spectrometry−
Parallel Reaction Monitoring (LC−MS−PRM)
Quantitation of immune markers CD8A, CD4, LAG3, PD1, PD-L1, and PD-L2
in Frozen Human Tissues
C7250
Zhang et al., J. Proteome Res. 2018, 17, 3932−3940

## Slide 74
Accurate MS-based Rab10 Phosphorylation Stoichiometry
C7250
assay to measure increased phospho Rab levels using synthetic stable isotope-labeled analogues for both phosphorylated and non-phosphorylated tryptic peptides surrounding Rab10-Thr73
Limit of detection (LOD) of SIL Rab10-pThr73 tryptic peptide (FHpTITTSYYR) with various acquisition methods; full MS, SIM, mxSIM and PRM.
Karayel et al., Mol Cell Proteomics (2020) 19(9) 1546–1560

## Slide 75
Lawless C., MCP,15, 1309–1322, 2016.
Absolute Quantification of over 1800
Yeast Proteins
C7250

## Slide 76
The end