## Slide 1: NMR Spectroscopy Basics
This project received funding by the European Commission under the GA n° 2019-1-IT02-KA203-063391
innocore-project@unitn.it
www.innocore-project.eu
Core Technologies for Education and Innovation in Life Sciences
by
Radovan Fiala, Karel Kubicek, and Pavel Kaderavek
CEITEC, Masaryk University

## Slide 2: Nuclear spin
Atomic nuclei consist of protons and neutrons (nucleons)
Protons and neutrons have spin ½
Spins tend to compensate each other but often not completely
Resulting spin quantum number of the nucleus is
I = k * ½ k is integer 0, 1, 2 ….
Proton
Neutron
Magnetic spin quantum number – number of possible spin states
m = -I, -I+1, -I+2 ……I-2, I-1, I
Examples
I = ½, m = -½, +½ 2 spin states example: 1H
I = 1, m = - 1, 0, 1 3 spin states example: 2H

## Slide 3: Magnetic moment
No magnetic field
In magnetic field B0
Only nuclei with non-zero spins have magnetic moments and are active in NMR
Magnetic moment
ħ=h/2 h Planck’s constant  magnetogyric ratio, specific to isotopes
Isotopes differ by the number of neutrons and have generally different spins.
In NMR, we refer to isotopes rather than elements, e.g. 1H (proton) or 13C instead of hydrogen and carbon

## Slide 4: Spins in magnetic field
E = hB0/2 B0 external magnetic field
= B0/2
h = 6,626.10-34 J.s h is Planck’s constant
Magnetogyric ratio, specific for each isotope
For 1H  = 42 494 369 s-1.T-1
For 100 MHz resonance frequency you need magnet
B0 = 100 s-1 /42.494 s-1.T-1  2.35 T
E
B0
E = h
S = 1/2
Research grade NMR spectrometers are produced usually with 1H resonance frequencies in multiples of 100 MHz, currently from 400 MHz up to 1,200 MHz (1.2 GHz), corresponding to magnets from 9.4 T to 28.2 T.
For protein studies, high-field spectrometers with resonance frequencies 600 MHz or higher are commonly used.
On Earth, spins are always subject to a magnetic field, but the magnetic field of Earth is only about 50 µT.

## Slide 5
NMR and electromagnetic spectrum
NMR
107
Noninvasive
Low sensitivity

## Slide 6: Chemical shift

0
5
10
Nuclei do not experience the external magnetic field B0 only,
But also the fields of other particles, especially electrons.
Net magnetic field at a nucleus
B = B0 (1 - )  nuclear shielding
Resonance frequencies differ slightly depending on the location of the nucleus in the molecule.
Resonance frequencies are field dependent, which is impractical – values are not comparable between different spectrometers.
Chemical shift – frequency difference relative to a suitable standard, expressed in ppm.
 = 106 ( - ref) / ref
For 1H, TMS (tetramethylsilane) is a common reference compound

## Slide 7: Spin-spin interactions
Dipolar coupling
Direct interaction between nuclear spins
Depends on the orientation of the internuclear vector with respect
to external magnetic field
Important in solid-state spektra
In liquids manifests itself only through relaxation phenomena
Scalar / J-coupling
Interaction of nuclei through the cloud of electrons
Does not depend on the external magnetic field
Causes splitting of signals (doublets for spins ½)
Scalar interaction constant J (in Hz, no dependence on B0)
I
S
B0
ris


## Slide 8: Reaching the resonance - CW
Continuous wave (CW)
Irradiation frequency is changed (swept) over the range. When resonance occurs, the irradiation energy is absorbed which is recorded as a signal. The resulting record of intensities vs. frequency is the spectrum.
To get undistorted spectrum the process must be SLOW (minutes)
spectrum
f1 Hz f2
frequency sweep
ppm

## Slide 9: Reaching the resonance - PFT
Pulsed with Fourier Transform
The spin system is irradiated by a single short high intensity pulse. This is equivalent to irradiating a range of frequencies. The shorter and more intense the pulse is, the broader range of frequencies is affected. After the pulse, the response of the spin system is recorded as a function of time. The record is FID (Free Induction Decay). The spectrum is produced by Fourier Transform of an FID.
FT
FID – time domain
Spectrum - frequency domain
RF pulse 90
ppm
t

## Slide 10: Relaxation
Spin-lattice relaxation - T1
Transferring the energy into surroundings (solvent/’lattice’). The spin system returns into equilibrium.
Spin-spin relaxation - T2
The intensity of the signal in FID is dropping with time (Free Induction Decay) due to loss of coherence. The energy is still in the spin system but randomly oriented nuclear magnetic moment average to zero.
Exponential decay
exp(-t/T2)

## Slide 11: Resolution
300 MHz
600 MHz
Position of signals is given by the chemical shift (relative number)
The with of 1 ppm in Hz (absolute scale) depends on magnetic field:
at 500 MHz, 1 ppm = 500 Hz,
at 1000 MHz, 1 ppm = 1,000 Hz
If the linewidth is the same, signal appear farther from each other at higher field.
Resolution and sensitivity increase linearly with magnetic field
Aromatic part of ethylbenzene spectrum

## Slide 12: Sensitivity
Energy difference between spin levels are very small.
Boltzmann distribution Na = Nb .exp(-DE/kBT)
E = h, h Planck’s constant, kB Boltzmann constant
Na, Nb – polulations of the spin states
For protons at 500 MHz and 303 K, the population difference between the ernergy levels is less than 0.01%!
We work with a small fraction od nuclei – sensitivity of NMR is inherently low
For proteins, you need about 0.5 ml of sample with 0.5 mM concentration.
Improving sensitivity by signal accumulation – more scans
Signal-to-noise ratio increases with square root of number of scans: S/N ~ √ns

## Slide 13: Increasing Resolution
Biopolymers: repetition of identical units (nucleotides, amino acids)
High resolution is needed
High magnetic field
Increasing number of dimensions

## Slide 14: NMR Spectrometer
Major parts
Magnet
Probe
Electronics
Operator’s desk with PC
Preamplifier
VT unit

## Slide 15
NMR Spectrometer - Scheme
Signal - sl(t)= sl(t)
l

## Slide 16: The Magnet
Adjusting the magnetic field homogeneity
B0

## Slide 17: The Probe
Houses the sample
Changes electric current into magnetic field and back.
Must be tuned for best sensitivity
Inverse probes, X-nuclei detection probes
Room temperature probes, cryoprobes

## Slide 18: Electronics
Frequency synthesis & signal processing
Computer (real-time control)
Power amplifiers
Magnet control
sample insert & eject
shimming
temperature control

## Slide 19
How the NMR Spectrometer Works
!!!!!!!!B1 ~ I ~ P1/2 (P=RI2)!!!!!!!!
Lp =
[dB]
Transmitter – power vs. rf field induction
Relative power ratio expressed in decibel
1 dB: P1/P2 = 1.2589254
Relative rf field ratio ex-pressed in decibel
1 dB: w1/w2 = 1.120185

## Slide 20
How the NMR Spectrometer Works
Transmitter – phase shifted pulses

## Slide 21
How the NMR Spectrometer Works
A/D converter
n=6 bits
64 levels
n=8 bits
256 levels
3bit A/D converter (8 levels)
2n = 8
A/D converter typically 16 bits
i.e. 65 536 levels
32 bits
i.e. 4 294 967 296 levels

## Slide 22
How the NMR Spectrometer Works
A/D converter – sampling frequency
Nyquist frequency
fmax = 1 kHz => D = 500 ms

## Slide 23
How the NMR Spectrometer Works
A/D-converter – signal folding

## Slide 24
How the NMR Spectrometer Works
Receiver
NMR signal
Local oscilator
Intermediate frequency
A/D converters

## Slide 25
How the NMR Spectrometer Works
Quadrature detection
mixer
cosA.cosB=1/2(cos(A+B) + cos(A-B))
cosA.sinB=1/2(sin(A+B) - sin(A-B))
(
)

## Slide 26
How the NMR Spectrometer Works
Quadrature detection
Intermediate frequence
Frequency wo+wrx removed by filter

## Slide 27
How the NMR Spectrometer Works
Quadrature detection – time vs. frequency
Spectral width fsw
Acqusition time tacq
N – number of acquisition points
D – sampling interval

## Slide 28
How the NMR Spectrometer Works
Pulse programmer
INEPT with refocusing

## Slide 29
How the NMR Spectrometer Works
Pulse programmer
;ineptrd
;avance-version (02/05/31)
;INEPT for non-selective polarization transfer
;with decoupling during acquisition
#include <Avance.incl>
"p2=p1*2"
"p4=p3*2"
"d3=1s/(cnst2*cnst11)"
"d4=1s/(cnst2*4)"
"d12=20u"
1 ze
2 30m do:f2
d1
d12 pl2:f2
(p3 ph1):f2
d4
(center (p4 ph2):f2 (p2 ph4) )
d4
(p3 ph3):f2 (p1 ph5)
d3
(center (p4 ph2):f2 (p2 ph6) )
d3 pl12:f2
go=2 ph31 cpd2:f2
30m do:f2 mc #0 to 2 F0(zd)
exit
ph1=0 0 0 0 0 0 0 0 2 2 2 2 2 2 2 2
ph2=0 2
ph3=1 1 3 3
ph4=0 2
ph5=0 0 0 0 1 1 1 1 2 2 2 2 3 3 3 3
ph6=0 2 0 2 1 3 1 3
ph31=0 0 2 2 1 1 3 3
;pl1 : f1 channel - power level for pulse (default)
;pl2 : f2 channel - power level for pulse (default)
;pl12: f2 channel - power level for CPD/BB decoupling
;p1 : f1 channel - 90 degree high power pulse
;p2 : f1 channel - 180 degree high power pulse
;p3 : f2 channel - 90 degree high power pulse
;p4 : f2 channel - 180 degree high power pulse
;d1 : relaxation delay; 1-5 * T1
;d3 : 1/(6J(XH)) XH, XH2, XH3 positive
; 1/(4J(XH)) XH only
; 1/(3J(XH)) XH, XH3 positive, XH2 negative
;d4 : 1/(4J(XH))
;d12: delay for power switching [20 usec]
;cnst2: = J(XH)
;cnst11: 6 XH, XH2, XH3 positive
; 4 XH only
; 3 XH, XH3 positive, XH2 negative
;NS: 4 * n, total number of scans: NS * TD0
;DS: 16
;cpd2: decoupling according to sequence defined by cpdprg2
;pcpd2: f2 channel - 90 degree pulse for decoupling sequence
;$Id: ineptrd,v 1.8 2002/06/12 09:05:00 ber Exp $
23.10.2012

## Slide 30
1D proton spectrum of a protein
1H 1D, Cavanagh et al., Protein NMR Spectroscopy, 2007
water
Examples
1H-15N HSQC of a well folded protein at 293 K
with approximately 155 amino acids, 600MHz

## Slide 31: Additional reading Keeler-2002-Understanding_NMR_Spectroscopy.pdf (cam.ac.uk)
YouTube videos
NMR Spectroscopy Visualized
Introduction to NMR spectroscopy Part 1, Part 2

## Slide 32
This project received funding by the European Commission under the GA n° 2019-1-IT02-KA203-063391
innocore-project@unitn.it
www.innocore-project.eu
Core Technologies for Education and Innovation in Life Sciences
The End
Questions, comments?
radovan.fiala@ceitec.muni.cz
Thank you for your attention