## Slide 1
Basics of SAXS in structural analysis (of biomolecules)
Karel Kubíček

## Slide 2
Motivation

## Slide 3
Terminology
X-ray – diffraction / scattering
XS - X-ray scattering
SAXS/WAXS - Small/Wide Angle X-ray Scattering
SANS - --------”---------- Neutron ---”---
Otto Kratky (1902, Vienna-1995, Graz)
Günter Porod (1919 near Villach, 1984 Graz)
Dmitri I. Svergun
Scattering
Scattering curve
Guinier plot
PDF (Pair-distribution function)
Bead model
Bead model - / SAXS - envelope

## Slide 4
Experimental setup
SAXS
X-ray

## Slide 5
SAXS
X-ray
Crystalized Sample Sample in Solution

## Slide 6
(very tiny) bit of theory
q=2k.sinq => q/2/k=sinq,
k=2p/l => q=4p/l.sinq
Often q is denoted as s
k
q

## Slide 7
=>
1st step: scattering to scattering curve

## Slide 8
What can we learn from the scattering curve:
Shape of the studied molecule
Fold
Secondary structure

## Slide 9
Is it really that easy?

## Slide 10
2nd step: Guinier plot & Kratky plot (from the initial region of the scattering curve)

## Slide 11
2nd step: Guinier plot & Kratky plot (from the initial region of the scattering curve)

## Slide 13
3rd step: PDF Pair-distribution function

## Slide 15
All information from the scattering curve together

## Slide 16
Bead model
Spherical harmonics problem to be solved

## Slide 17
Solutions with similar “goodness” of fit may be obtained

## Slide 19
Summary

## Slide 20
Summary (graphically)

## Slide 21
SAXS Hamburg

## Slide 29
Evaluation of the experimental data

## Slide 30
References:
Koch, M.H.J., Vachette, P., Svergun, D.I. Quart Rev Biophys 2003
Jacques, D.A., Trewhella, J. Prot Sci 2010
Svergun, D.I., Petoukhov, M.V., Koch, M.H.J. Biophys J 2001
Wriggers, W. Biophys Rev 2010
Putnam, C.D., Hammel, M., Hura, G.L., Tainer, J.A. Quart Rev Biophys 2007
Madl, T. Gabel, F., Sattler, M. J Struct Biol 2010

## Slide 31
https://deepmind.com/blog/article/alphafold-a-solution-to-a-50-year-old-grand-challenge-in-biology
AlphaFold: a solution to a 50-year-old grand challenge in biology

## Slide 32
NMR

## Slide 33
Confidence in structural features of proteins determined by
X-ray crystallography
(estimates are very rough and strongly depend on the quality of the data)
Structural feature |  |  | Resolution |  | 
 | 5 Å | 3 Å | 2.5 Å | 2 Å | 1.5 Å
Chain tracing | - | Fair | Good | Good | Good
Secondary structure | Helices fair | Fair | Good | Good | Good
Sidechain conformations | - | - | Fair | Good | Good
Orientation of peptide planes | - | - | Fair | Good | Good
Protein hydrogen atoms visible | - | - | - | - | Good

## Slide 34
XAS = X-ray Absorption Spectroscopy
XANES = X-ray Absorption Near Edge Structure
EXAFS = Extended X-Ray Absorption Fine Structure

## Slide 35
SAXS/EXAFS
EXAFS (Extended X-ray Absorption Fine Spectroscopy) poskytuje informace o nejbližších slupkách atomů sousedících s absorbujícím atomem
Fe
N
N
N
N

## Slide 36
His 108
Met 75
Met 86
Met 110
Cu(I)
b4
b5’
X-Ray Absorption Spectroscopy
Cu(I)DR1885 DE=-10.3 eV
Ligand r(Å) 2s2.103(Å2) R-exafs e(fit index)
Fit1 (1shell) 2S 2.299 4(1) 0.446 0.49
Fit2 (1shell) 3S 2.301 9(1) 0.403 0.41
Fit3 (2shells) 3S 2.300 8(1) 0.334 0.29
1N§ 1.982 4(1)
Fit4 (2shells) 3S 2.303 8(1) 0.305 0.27
1N* 1.999 7(2)
§ no MS *His, MS

## Slide 37
A BLAST search over all non-redundant GenBank genomes
M
H
M
H
M
75
86
108
110

## Slide 38
Conserved Met&His
Other Met&His residues
His 108
Met 73
Met 75
Met 88
Met 86
His 79
Met 83
Met 112
N
C
N
C
b1
b2
b3
b4
b5
b6
b7
b8
b9
Met 110
cyan – b-sheets
grey – random coil
Holo
Apo

## Slide 39: Rentgenstrukturní analýza
Krystalová mřížka působí na rentgenové záření jako optická mřížka na viditelné světlo. Nastávají ohybové jevy a na stínítku se objevuje difrakční obrazec. Tyto obrazce mohou být matematicky analyzovány, aby se získala informace o rozložení elektronů v molekulách tvořících krystal.

## Slide 40
Bragg‘s law
2d sinQ = nl

## Slide 41
Bragg‘s law
2d sinQ = nl

## Slide 42
Trojklonná
Jednoklonná
Kosočtverečná (ortorombická)
Šesterečná
Klencová
Čtverečná
Krychlová
Krystalografická soustava

## Slide 44
https://www.intechopen.com/books/x-ray-scattering/x-ray-diffraction-in-biology-how-can-we-see-dna-and-proteins-in-three-dimensions-

## Slide 47
https://doi.org/10.3390/cryst8110434
http://skuld.bmsc.washington.edu/~merritt/bc530/local_copies/phase_methods_files/vd_xtals.jpg
Phase diagram of solubility of a protein in solutions as a function of the concentration of the precipitant.

## Slide 49
X-Ray Goniometer
a device that permits the simultaneous recording of the direction of X rays diffracted by a specimen under study and of the position of the specimen at the time of diffraction.
An X-ray goniometer can be an independent device recording the diffraction pattern on photographic film; in this case it is an X-ray camera. The term “X-ray goniometer” is also applied to goniometric devices that are components of X-ray diffractometers and are used for mounting the specimen and detector in positions corresponding to the conditions necessary for the occurrence of X-ray diffraction.
https://encyclopedia2.thefreedictionary.com/X-Ray+Goniometer

## Slide 51
https://www.intechopen.com/books/x-ray-scattering/x-ray-diffraction-in-biology-how-can-we-see-dna-and-proteins-in-three-dimensions-

## Slide 52: Krystalogram B-DNA získaný v r. 1952 Rosalindou E. Franklinovou, na jehož základě Watson a Crick navrhli dvoušroubovicový model struktury DNA. C. & W. dostali v r.1962 společně s Mauricem Hugh Frederick Wilkinsem NC za fyziologii a medicínu „za jejich objevy týkající se molekulární struktury nukleových kyselin a jejich významu při přenosu informací v živých organizmech“
F
W
C

## Slide 53
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 54
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 55
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 56
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 57
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 58
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 59
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 60
http://www.udel.edu/chem/fox/MassSpecLecture09.pdf

## Slide 67
Amino Acid
Residue Composition
Residue Monoisotopic Mass
Delta Mass
Methionine
C5H9NOS
131.0405
0
Methionine Sulfoxide
C5H9NO2S
147.0354
15.9949
Methionine Sulfone
C5H9NO3S
163.0303
31.9898
Sulfur
S
31.9721
-

## Slide 69
Mass Spectrometry
ESI - electron spray ionization – high voltage applied to a liquid jet producing highly charged droplets
MALDI - matrix-assisted laser desorption/ionization
- three step process:
        1) sample mix with matrix and deposition on a metal plate,
        2) laser pulse desorbs the sample with matrix,
        3) analyte molecules are ionized and analyzed (TOF – time of flight MS technique)

## Slide 70
Quadrupole mass analyzer

## Slide 72
HDX MS - Hydrogen Deuterium Exchange with Mass Spec

## Slide 73
ARDD - average relative D-uptake difference
Scientific Reports 3, Article number: 1247, 2013

## Slide 74
http://www.biopharminternational.com/performing-hydrogendeuterium-exchange-mass-spectrometry

## Slide 75
ITC – isothermal titration calorimetry
1760s – Black measured the heat capacity and latent heat of water
1780s – Lavoisier designed an ice calorimeter and used this instrument to measure the metabolic heat produced by a guinea pig confined in the measurement chamber
=> Calorimeter was one of the earliest scientific instruments & first calorimetric experiment was a biologically relevant measurement

## Slide 76
Why ITC?
ITC is a quantitative technique
can determine:
  binding affinity (Ka),
  enthalpy changes (ΔH),
  binding stoichiometry (n) of the interaction between two or more molecules in solution.
From these initial measurements:
Gibbs energy changes (ΔG)
entropy changes (ΔS)
ΔG = -RTlnKa = ΔH-TΔS

## Slide 80
Three possibilities of calorimetric measurement:
temperature change (either adiabatic or isoperibol) [°C/time]
power compensation (often called isothermal) [mcal/time]
heat conduction (Lavoisier design)

## Slide 86
The experimental binding isotherm can be characterized
by the unitless value c